## Slide 1
IR2 – Development Status
Vasiliy Morozov
on behalf of 2nd IR Design Team
IR2@EIC: Science and Instrumentation of the 2nd IR for the EIC
March 18, 2021

## Slide 2: Luminosity Sharing
Conservative assumption: luminosity is shared between two detectors, different bunch pairs collide at different IPs
Luminosity in the medium range can pushed at the expense of acceptance
Chart: Center of Mass Energy [GeV]
 | 1
Chart: Center of Mass Energy [GeV]
 | 1
Spin and Flavor Structure of
the Nucleon and Nuclei
QCD at Extreme Parton Densities-
Saturation
100
10
1
Center of Mass Energy Ecm [GeV]
Peak Luminosity [cm-2s-1]
Annual Integrated Luminosity [fb-1]
1034
1033
1032
Internal
Landscape of the Nucleus
150
Combined of both IRs
High
Baseline
Fair-share per IR
High
Baseline
Tomography (p/A)

## Slide 3: Beam and Optics Parameters
Geometric emittance is the area occupied by bunch in phase space
is a constant typically made as small as possible
Optics and determine the beam parameters at the IP
  rms beam size
  rms angular beam divergence
  Transverse momentum spread
  Note
  Maximum beam size
Have control over through optics design
Luminosity

## Slide 4: Luminosity Optimization at Low Energies
Luminosity limited by the smaller of the physical and dynamic apertures
By optimizing the final focusing quad configuration, make full use of available physical aperture
Dynamic aperture being checked
Parameter | FDF | Units
Chrom x/y | -19.55 / -74.45 | 
βx/y* | 36 / 3 | cm
σx/y at IP | 103.9 / 9 | um
σ’x/y at IP | 0.289 / 0.301 | mrad
Parameter | Value | Units
Energy | 100 | GeV
Rms norm. εx/y | 3.2 / 0.29 | mm-mrad

## Slide 5: Luminosity and Acceptance Trade off
Larger luminosity means smaller acceptance
Minimum acceptance is determined by the angular spread at the IP
Luminosity increased by stronger focusing, i.e. increase in angular divergence
Table below is for the proton case
For same-rigidity nuclei,
 | GeV GeV | GeV GeV | GeV GeV | GeV GeV | GeV GeV
Highest | 1.54 410 / 410 | 10 330 / 330 | 7.9 290 / 290 | 6.1 270 / 270 | 0.44 90 / 160
High divergence | 1.54 410 / 410 | 10 330 / 330 | 4.5 220 / 220 | 3.7 210 / 210 | 0.44 90 / 160
High acceptance | 0.32 180 / 180 | 3.1 180 / 180 | 3.1 180 / 180 | 2.9 180 / 180 | 0.44 90 / 160
 | 1.54 410 / 410 | 10 330 / 330 | 7.9 290 / 290 | 6.1 270 / 270 | 0.44 90 / 160
High divergence | 1.54 410 / 410 | 10 330 / 330 | 4.5 220 / 220 | 3.7 210 / 210 | 0.44 90 / 160
High acceptance | 0.32 180 / 180 | 3.1 180 / 180 | 3.1 180 / 180 | 2.9 180 / 180 | 0.44 90 / 160
[ cm-2s-1]
/ [MeV/c]

## Slide 6: Luminosity and Acceptance Trade off
GeV configuration
Highest
High-divergence
High-acceptance

## Slide 7: Acceptance as Function of and
acceptance at
acceptance at
  Requires dispersion
  Secondary focus allows for
  Therefore, one can approach the fundamental limit
  Increase of and therefore may result in smaller acceptance

## Slide 8: Considerations IP8
Going from outer arc into inner arc
  IP6: from inner to outer arc
Present IR not portable to IR8
Geometric issues
IR8: Tunnel dia. 6.3m to 60m (then 5.3m dia)
IR6: 7m dia. +/- 140m
60m
H. Witte

## Slide 9: Crossing Angle Choice
Cannot be too large, mrad
  Experimental hall geometry does not allow
  IP must be shifted toward the ring center to allow RCS bypass the detector
  Requires additional crabbing cavities, not only cost but additional impedance and other dynamical issues
  Undesirable from acceptance point of view, e.g. with 50 mrad, acceptance limited to 3.5 in rapidity
  Does not allow to move the final focusing quads closer because of detector space requirements
  Unnecessarily large given that Roman pot acceptance of - mrad is sufficient; moreover, large Roman pot acceptance requires large-aperture magnets posing engineering challenge
Cannot be too small, mrad
  Hall geometry requires spectrometer dipoles to bend towards the electron beam, bending away as in IR1 is not possible because of the tunnel wall, small crossing angle would cause interference with electron beamline
  Relaxes engineering requirements
Everything seems to point to an optimal crossing angle of ~35 mrad

## Slide 10
Detection Issues with Crossing Angle
Crabbing causes apparent smear of transverse beam size at the IP
Transverse vertex position can be found by
  narrowing down its longitudinal position through precise timing of ~35 ps
  simultaneously measuring particle’s position, angle and energy in the far-forward section
Crossing angle increases the gap in the rapidity coverage in the rear direction
Asymmetry in the forward hadron acceptance
Gap in rapidity coverage:
beam pipe solid angle (~20 mrad) +
E.C. Aschenauer &
A. Kiselev

## Slide 11: 2nd IR Schematic
Forward acceptance not azimuthally symmetric because of electron dipole

## Slide 12: 2nd IR Geometry and Optics Matching and Component Integration
Beam crossing direction flipped compared to the 1st IR
Not much flexibility in electron geometry because of electron spin rotator requirements
Electron beam line is a slightly modified baseline design
Next design iteration:
  35 mrad crossing angle
  ~85 cm radial shift toward the ring center (modification happening in IR1 as well)

## Slide 13: Ion 2nd IR Optics from 135 to 275 GeV
Lengths of downstream final focusing quadrupoles optimized to provide 10 mrad polar angle acceptance with aperture-edge fields below 4.6 T
Use constraints on km and km as in the 1st IR
Upstream section is based on the 1st IR
Doublet optics with reversible polarity of the second quad depending on the energy cm (>135 GeV) cm (<135 GeV)
Secondary focus with acceptance
Roman pot
at 2nd focus
IP
Same optics and geometry as in baseline
ions

## Slide 14: Linear Optics and Chromaticity Compensation
Greatest conceptual accelerator physics question: chromaticity compensation in the collider rings with two IRs
Making use of chromatic interference of the two IRs
No symmetry requirements to IRs
Control chromatic beam smear around the ring and compensate it at both IPs
IP8
IP6
IP6
IP8
chromatic beam smear

## Slide 15: IR2 35 mrad Crossing Angle Design
Magnet parameters re-optimized for mrad Roman pot acceptance with aperture-edge fields of T
Crossing angle is 35 mrad
Forward detector space 5 m
IP shifted toward the ring center by 85 cm
Max dispersion size at 2nd focus limited by geometry but not critical if
IP8
2nd focus
Roman pot
Radial shift
RCS
Crab cavities
2nd focus
Roman pot
Dispersion
suppressed
RCS

## Slide 16: 2nd IR Modeling Under Way
Framework for IR2 simulations has been setup (Yulia and Dmitriy)

## Slide 17: Complementarity to 1st IR
Secondary focus with high- acceptance
Slightly larger Roman pot acceptance of mrad vs mrad to help cover any blind spots
Bending the ion beam by the spectrometer dipole towards the electron beam as opposed to away from the electron beam as in IR1
Different longitudinal shift of the center of the detector solenoid with respect to IP
Different crossing angle of ~35 mrad
Opposite angle of solenoid crossing by the ion beam

## Slide 18: 2nd IR Design Team
Jefferson Lab: V. Burkert, R. Ent, Y. Furletova, R. Gamage, D. Higinbotham, A. Hutton, C. Hyde, F. Lin, T. Michalski, V.S. Morozov, R. Rajput-Ghoshal, D. Romanov, A. Seryi, A. Sy, C. Weiss, M. Wiseman, W. Wittmer, Y. Zhang
BNL: E.-C. Aschenauer, J.S. Berg, A. Kiselev, C. Montag, R. Palmer, B. Parker, V. Ptitsyn, F. Willeke, H. Witte
Stony Brook University: P. Nadel-Turonski

## Slide 19: Backup

## Slide 20: Considerations IP8
If using IP6 forward dipole configuration (HSR bends away from ESR)
  Beam is bent further inside
  Can't bend back until we reach the crabs
  Requires creating a roughly 2 m transverse displacement over around 50 m length; lots of extra dipoles, issues with dispersion matching
If we put ZDC on the outside, bending HSR toward the ESR
  25 mrad crossing angle not possible: lines diverge slowly, crab cavity transverse size creates collision between HSR/ESR lines
H. Witte

## Slide 21: How to get more luminosity at lower Ecm?
For hadrons, final focus lens (vertical) is split into two magnets (tapering the aperture that way).
Doublet focusing for Ecm ~100-140 GeV.
For low hadron beam energy
(Ecm =60 GeV) can rewire into triplet focusing, reduce b*  Increase L by factor of 2
Doublet focusing
Triplet focusing
schematics
F. Willeke

## Slide 22: Operation with two Detectors
Only one detector and one IR is in the EIC budget. The project is working on accommodating a second IR and detector. Required funding of ~500M$ is unclear at this point
The bunches cannot collide in two IRs with maximum intensity.
Simultaneous collisions of all bunches in 2 Irs most likely requires to reduce the intensities by up to a factor of 2:
L  2 x L/4
Instead, we arrange for half of the bunches collide in one IR the other half in the second IR (luminosity sharing)
L  2 x L/2
So far, we don’t have (yet) a satisfactory solution for operation with 2 IRs, too much chromaticity, to much deterioration of polarization!
What works: Run collisions in one IR at a time and alter Irs
L  2 x L/2
Nota bene: Two IRs as compared to one will most likely not increase the sum of the (integrated) luminosity
F. Willeke

## Slide 23: IR 8
The first interaction region of EIC is at IR 6
Present RHIC offers IR8 as a possible second IR and detector location.
IR 8 has significantly less space than IR6.
A much larger crossing angle (35 mrad seems possible) in IR 8 compared with the present 25 mrad crossing angle in the first IR is most likely not possible without a major effort in civil construction.
The tunnel end in IR 6 is 6.9 m wide over a length of 284 m. In IR8 it is only 6.4 m wide over a length of 117 m. Further out it is only 5.27 m wide.
A detector bypass for the RCS limits the detector radius to 3.4 m
At present, we are planning the hadron and electron pathlengths in IR 8 similarly to the ones in IR6. This will constrain the differential pass length for electrons and hadrons in a later full IR8 layout, as any pathlength difference between hadron and electrons might not be able to be compensated any more by already existing accelerator arcs.
IR8 centerline needs to be moved at least 85 cm from present midline of the tunnel (outwards)
Work in progress to lay out reference design for IR with larger crossing angle and stronger emphasis on forward detection
F. Willeke

## Slide 24: IR6 vs IR 8 geometry
F. Willeke

## Slide 25: Ion 2nd IR Optics up to 135 GeV
All aperture-edge fields below 4.6 T
cm with on km and km
Assuming m 275 GeV: m, 100 GeV: m,

## Slide 26: Chromaticity Compensation
Another focus of recent effort
Strategy
  Arc 9 used for semi-local compensation of the rear side of IP8
  Arc 5 used for semi-local compensation of the forward side of IP6
  Forward side of IP8 and rear side of IP6 partially compensate each other
  Since IP8 forward and IP6 rear are different, the difference in their chromatic kicks is compensation by sextupoles in Arc 7
  Exact phase advance between the IPs and sextupoles optimized slightly