## Slide 1: Minidrift GEM detector Results Summary
EIC Tracking Workshop, Temple University
May 9, 2015
B.Azmoun, BNL

## Slide 2: Track Reco Methods Compared
Drift Gap
Transfer 1
Induction
Transfer 2
GEM 1
GEM 2
GEM 3
Mesh
X-Y Strips
Pitch: 400um
17mm
1.5mm
2mm
1.5mm
Preamp/Shaper
Primary Charge
Fluctuation
* Initially decided to determine charge arrival time (continuous variable) to determine vector z-comp., and use the pads (discrete variable) to determine the x-comp., but “rising edge method”, and others like it have modest timing resolution (~1/2 time bin). [X~1pad, Z~1/2time bin]
* Instead why not focus on improving the determination of the x-comp. In principle the charge distribution within each time slice should yield a position resolution similar to that seen for normally incident tracks (~50-60microns), which corresponds to a fraction of a pad. [X~pad fraction, Z=1 time bin]
Time Slice Method
Rising Edge Method

## Slide 3: Vector Reco Methods Compared
Ext. Trigger
40MHz Cock
Phase
uncertainty
APV Latency
Capture window
Incurs 25ns/sqrt(12) timing error for charge arrival as given by clock edge
Dx
Dt  Dz
z
x
Dx=vd*Dt*tanq
q
Can unfold phase uncertainty from time slice method, NOT rising edge method

## Slide 4: COMPASS Vs. Chevron board
Chevron Pattern --> systematic offset error can be corrected

## Slide 5: Time slice method limitations
More tail overlap at later time bins deteriorates resolution
Si Track
GEM Track
Corrected
Uncorrected

## Slide 6: Best Centroid Vs Vector Reco
The best possible resolution as determined using the centroid alone cannot compete with vector reco.
We believe the vector reco resolution is substantially better than what is shown here!

## Slide 7: Outlook: Unfolding shaper response
A. Kiselev
Raw Waveform
Unfolded
Gain access to actual charge deposit by unfolding the nominal shaper response from the raw data
Unfolded clusters are determined with full covariance matrix
Formal Chi2 analysis shows spatial resolution <70um at 30deg. using COMPASS board.
This detector configuration has huge potential beyond what was shown on previous slides!

## Slide 8: Backup

## Slide 9: Rotate Coord. Sys. Of Si to align with GEM (GEM fixed)
GEM Coord. System orientation Parameters:
Fixed: Dx, Dy, Df
Measured:<qx> , <qy >, Dz (?)
Scanned: None
Dy
x
y
z
Dx
Df
<qx>
<qy>
x
y
z
<qx>
<qy>
Mini-Drift GEM
Si Telescope
Dz
Beam
Dx
Dy
Si Tel. Coord. System orientation Parameters:
Fixed: Dx, Dy
Measured: <qx> , <qy >, Dz (?)
Scanned: f, <qx > & <qy > , Dz
Strong Scan Parameters:
  Dz & Df
  *pulse height cut threshold for defining a hit.
Weak Scan Parameters:
<qx> , <qy >  local to measured, and Dx, Dy  local to measured

## Slide 10: Mini-Drift GEM Det. + SRS Readout
Std. 10x10cm CERN 3-GEM Det.
ArCO2 (70/30)
Gain ~ 6500
~17mm Drift Gap
Drift Time ~600ns
SRS /512 channels APV 25
28 x 25ns Time Samples
RCDAQ
  Ease of use
  High flexibility
COMPASS style Readout:
256 x 256 X-Y Strips
~10cm x 400um pitch
Drift Gap
Transfer 1
Induction
Transfer 2
GEM 1
GEM 2
GEM 3
Mesh
X-Y Strips
Pitch: 400um
17mm
1.5mm
2mm
1.5mm
Preamp/Shaper
Primary Charge
Fluctuation