## Slide 1: Status of GEM R&D @ UVa
Kondo Gnanvo
University of Virginia, Charlottesville,
EIC Tracking R&D Workshop @ Temple University
05/09/2015

## Slide 2
GEM Detectors @ UVa: The group members
Faculty: Nilanga Liyanage (Associate Professor)
Research Scientists: Vladimir Neliyubin, Kondo Gnanvo
Post Docs: Huong Nguyen
Graduate Students: Xinzhan Bai, Danning Di

## Slide 3
GEM Detectors @ UVa: The Lab
Clean room: 3 × 7 m2 class 1000
X-ray source in its lead shielding box
Tests lab
Cosmic test setup for large GEMs
SRS Readout:
12k Channels

## Slide 4
Back Tracker : N. Liyanage, (Uva, Virginia, USA)
10 GEM Layers (200 × 50 cm2)
Each Layer = 4 GEM modules (50 × 60 cm2)
Front Tracker: E. Cisbani (INFN Roma, Italy)
6 GEM Layers (150 × 40 cm2)
Each layer = 3 GEM modules (50 × 40 cm2)
Proton arm layout for GEp (5) experiment
50 cm
60 cm
50 cm
40 cm
GEMs for Super Bigbite Spectrometer (SBS) in Hall A @ JLab

## Slide 5
SBS-BT-GEM: R&D
K. Gnanvo et al., Nucl. Inst. and Meth. A782, 77-86 (2015), http://dx.doi.org/10.1016/j.nima.2015.02.017

## Slide 6
SBS-BT-GEM: Production
Production of the SBS-BT-GEM Modules
40 modules to be built by July 2017
13 modules already built as of May 09, 2015
11 successfully passes the ultimate test with cosmics
  1 HV sector out of 1080 (12  3  30) was shorted and disabled
Last 2 modules just out of the clean room and will be tested in the coming days
Construction rate of 2 SBS modules / month

## Slide 7
R&D for EIC Forward Tracker: Design of EIC-FT-GEM proto I
100 cm
22 cm
44 cm
2D u/v readout strips
Entrance window
Drift region
Transfer region
Transfer region
Induction region
spacers
Gas inlet
Gas outlet
2D readout board on Honeycomb support
Key characteristics
Largest 2D GEM detector ever built: 100 cm  (44 cm – 22 cm)
Low mass and small dead area full disk chamber
  Narrow edge GEM frame support and honeycomb for the readout
  All electronics on inner and outer radius side of the chamber
Fine strips 2-d small stereo angle u/v readout on flexible board
  Good position resolution and low capacitance noise
Cross section of low mass triple GEM
Pitch: 550 m
12°
Top strips: 140 m
Bot. strips: 490 m

## Slide 8
EIC-FT-GEM @ FTBF: Spatial resolution
Good spatial resolution
Better than 130 μm for the top and bottom strips
Better than 100 μm for y and 450 μm for x
Hadron bean reconstruction from position scan
SBS-BT-GEM
EIC-FT-GEM

## Slide 9
pRad GEM: Proton Radius Experiment pRad @ JLab
Slide from D. Dutta, PasSpin, Ji’nan, China, Oct. 30, 2013
GEM chambers: X-Y veto counter

## Slide 10
pRad GEM: Assembly of the first chamber is ongoing
pRad X/Y strips readout boards
Optical inspection of pRad GEM foil
Drift cathode on the stretcher
New assembly technique used for pRad chambers (See next slide)

## Slide 11
GEM R&D: New assembly technique for large GEM
Idea:
  GEM foil stretched and glued to support frames
  Individual framed GEM stacked together in the assembled chamber
  O-ring and screws used to close the chamber and ensure the gas tighness
Pros:
  Possibility of easy replacement of GEM foils or readout board after assembly
  Work for light detector: plastic screw and narrow support frames, no rigid support needed
  Idea already being tested on the pRad GEM chamber
Cons:
  Need to evaluate gas tightness with O-ring + screw system
  Would still need spacers inside the active area
Exploded view of pRad GEM: 100 cm  55 cm
Cross section of triple GEM with new assembly

## Slide 12
GEM R&D: Copper Free GEM foil
Cu-Free GEM foil
  Standard GEM foil with the copper layer removed
  Copper clad Kapton based material comes with 100 nm Chromium (Cr) layer between Cu and Kapton
  100 nm Cr layer replace Cu as top and bottom GEM electrode
  Cu-Free GEM Samples from Rui with a grid of Cu strips
    Ensure electrical contact to be removed in the future
5 m Cu
100 nm Cr
50 m Kapton
Standard GEM foil
100 nm Cr
50 m Kapton
Cu-Free GEM foil
Grid copper strips

## Slide 13
GEM R&D: radiation length of Cu-Free GEM
Triple-GEM detector with standard GEM foil
Triple-GEM detector with Cu-Free GEM foil
About 50% reduction in the material in a EIC-like chamber with Copperless GEM
Based on the data for the SBS-BT-GEM modules
The contribution of the Cr layer has not been added but is negligible to the first order

## Slide 14
GEM R&D: Preliminary tests of Cu-Free GEM
Tests with Cosmics
HV scan with Sr90 source
Good performances of the Cu-free GEM
Need to study spark rate and ageing of the foil
High rate and long term performance study will be done with our x-ray source
Investigate Cu-less COMPASS-like readout board

## Slide 15
GEM R&D: EIC-FT-GEM prototype II
EIC GEM prototype II:
Common GEM foil design between UVa, Florida Tech (FIT) and Temple Univ. (TU) (Aiwu’s talk)
  Satisfy the requirements and constraints from 3 different assembly assembly
Low mass and light detector
  Reduce overall the material budget, Investigate copper less GEM
New detector construction technique
  Possibility to re open the detector to replace parts
New u/v strips readout design
  Finer pitch to improve spatial resolution, all connectors for FE electronics at the outer radius
u/v strips readout board
Common GEM foil UVa, FIT and TU (Aiwu’s talk)

## Slide 16
Summary
Large GEM R&D and Production Activities at UVa
  Production of the SBS Back Trackers GEM modules
  First pre-R&D prototype for EIC forward tracker GEM (successfully tested @ FTBF)
  Assembly of the largest GEM for pRad experiment is ongoing
New ideas for on large GEMs
  New assembly technique been tested  possibility to re-open large size triple-GEM chamber
  Reduce overall the material budget, Investigate copper free GEM foils
EIC-FT-GEM prototype II
  Common GEM foil design shared with FIT and TU
  Upgrade of the U/V readout design with finer pitch to improve spatial resolution and all connectors for FE electronics at the outer radius

## Slide 17
Backup

## Slide 18
EIC-FT-GEM @ FTBF: Performances
SBS-BT-GEM
EIC-FT-GEM
Cluster size vs. HV
Efficiency
ADC vs HV

## Slide 19
pRad Readout board support

## Slide 20
Proton Radius Experiment pRad @ JLab
Slide from M. Kohl
EINN2013, Paphos, Cyprus 2013

## Slide 21
Proton Radius Experiment pRad @ JLab
Slide from M. Kohl
EINN2013, Paphos, Cyprus 2013