## Slide 1: (Sub) 10 Ps TOF R&D with MRPC Technology
Mickey Chiu
Brookhaven National Laboratory
Matthias Grosse-Perdekamb, IhnJea Choi
University of Illinois at Urbana-Champaign
EIC PID Meeting 03,23,2015

## Slide 2: Outline
Status of MRPC prototype at UIUC
  Configuration of the prototype
  PCB design and electrode
  Insulation for HV and stack of glass plates
  Assembly
  Setup for cosmic ray test
Current issue and plan

## Slide 3: Signal Readout of MRPC
-6 kV HV
+6 kV HV
Glass plate
Gas gap
Smaller gas gap width -> Better timing resolution : Required many glass stacks
Differential
Preamp.

## Slide 4: Configuration of Prototype MRPC
 | MRPC ( C. Williams et al. ) | MRPC ( UIUC & BNL)
Gas Gap Width | 160um (fishing line) | 105um (fishing line, and 165, 125, 75um)
# of Gas Gaps | 4 stack x 6 layers = 24 | 4 stack x 9 layers = 36
# of thin glass layers | 4 stacks x 5 layers = 20 (250um thick glass) | 4 stack x 8 layers = 32 (210um thick glass)
Preamplifier | Differential type, NINO chip | LMH6554 2.8-GHz + Evaluation Board
TDC and DAQ | Oscilloscope (10Gs) | DRS4-V5(5Gs) + PC
Time resolution | 16ps obtained | ?
Gas gap width : 160um
(16ps timing resolution)
Gas gap width : 105um
Crispin Williams
BNL&UIUC Prototype
4 x
4 x
PCB
glass
Gas gap

## Slide 5: PCB for Electrode and Signal Pickup
PCBs (3 layers)
- One board flavor – interchangeable
- HV connection integrated on board
- Rounded readout strips
- Outer dimension : 196mm x 70mm x 1.5mm
- Readout strip : 4 strips, 170mm x 10mm
- The strips are placed in the middle layer
A MRPC needs 5 PCBs
PCB Design
HV feed pad
Post for spacers
+ fishing line
12 PCBs
ch1
ch2
ch3
ch4

## Slide 6: Electrodes on the PCB Surface
Carbon coating with carbon spray
Polished the surface with soft paper
Measured the resistivity
( 0.5 ~ 1.5 M Ohm/Square)
Preparing carbon painting
Silicon (RTV 159)
Thick glass plate (550um) for a insulation
HV connection pad
Carbon electrode
Double sided Kapton tape

## Slide 7: Electrode PCBs
Electrode coating ✔
Electricity Insulation ✔
Cable connection ✔
10 PCBs for two MRPCs(4 stacks)
Silicon (RTV 159)

## Slide 8: Wiring of Fishing Line for Gas Gap
105um diameter of fishing line
Stacking glass plates and fishing lines
4 stacks

## Slide 9: MRPCs
Two MRPCs assembled
Close view of glass plates

## Slide 10: Two MRPCs Mounted
Side view
Top view
Note:
10ps ~ 3mm of
light travel!
MRPC-A
MRPC-B

## Slide 11: Placed DRS4 Board Next to MRPCs
DRS4 Board
No preamp yet!

## Slide 12: Cosmic Ray Test Stand
Tsinghua MRPC
Trigger Modules
PMT HV
LV
Counter
LV (Backup)
MRPCs

## Slide 13: Time Resolution Measurement
MRPC-A
MRPC-B
DRS4-V5
(Wave form digitiger)
PC
(DAQ)
Silicon Tracker
(x and y strips,
500um pitch)
Hodoscope
Hodoscope
preamp
preamp
Gas Cylinder
USB
50 Ohm cable (<1m)
ch2
ch2
Muon trigger
Track positions from Si-Trackers
Gas Mixture : Freon(I134a) 90% : Iso 5% : SF6 5%
Silicon Tracker
(x and y strips)
Drift Chambers also available for the tracking

## Slide 14: Setup
Still working on the preamplifiers
-> Connected signals to the wave form analyzer
without preamps.
DRS4 Board (Wave form Analyzer)
USB extender, Connected Win8 PC
Two MRPCs ( Top cylinder)
Tsinghua Univ. MRPCs (Bottom cylinder)
+(ch2),- (ch2)
+(ch2),- (ch2)
Top MRPC
Bottom MRPC
DRS4 Channel
Connection
ch2
ch2

## Slide 15: Cosmic Ray Signal and Comparison
ns
Signal from 1st Prototype MRPC
with preamp (Beam Test @ FNAL, 2014)
Cosmic ray signal from 2nd Prototype MRPC (No Preamp)
2ns
4ns/div, 5mV/div
+
-

## Slide 16: Coincidence Signals Seen at DRS4
+,ch2 from MRPC(Top)
-,ch2 from MRPC(Top)
+,ch2 from MRPC(Bottom)
-,ch2 from MRPC(Bottom)
5mV/div, 2ns/div
2ns
Cosmic Ray Triggered
Data Taking Speed
500Event/ S
1024 samplings / Event
=(~200ns period)
Accumulated 10k events
last night
(Trigger rate : ~ 0.2Hz)
-> will analyze the signals
5mV

## Slide 17: Accumulated Cosmic Ray Events
w/o Preamp
Top MRPC
Ch2 +
Top MRPC
Ch2 -
Bottom MRPC
Ch2 +
Bottom MRPC
Ch2 +
+-9kV(18kV)
Top MRPC
Bottom MRPC
[mv] vs [ns]
Decoding code
from Mickey.

## Slide 18
Top MRPC : Ch2(+) – Ch2(-)
Bottom MRPC Ch3(+) – Ch4(-)

## Slide 19: Issue on the preamplifier
Differential Inputs
Gain : 200/50 = 4.
Negative output
(From Bottom MRPC)
-> Rising time is slow..
Without preamp
(From Top MRPC)
LMH6554 2.8-GHz
+ Evaluation Board
A preamp,LMH6881 (Gain ~ 7), has been ordered for testing.

## Slide 20: Plan
Gas simulation is required to optimize the gas gap width for the best time performance.
Time resolution measurement with gas gap width of 105um and other size (125um, others)
Use a different gas mixture
Searching for other materials for replacing the glass plate
(Plastic, Kapton/Mylar, etc.)
Cosmic ray test for efficiency and time resolution measurement
Beam test
(Rate capability, Scanning of momentum, dependence of Incident
angle of particle, etc.)

## Slide 21: backup

## Slide 22: Gluing G10 plates on the PCBs
5cm x 17cm
Thickness : 6mm,
Used G10s for stiffening the cover PCB plates
instead of Al honeycomb plate.
(Gas in the honeycomb cell uncertain..)

## Slide 23: NPL Lab at UIUC
Gas Mixing Rack
HV system
DAQ & NIM Modules
Cosmic Ray Test Stand
Mix up to four gases
HV(CAEN), CAMAC, NIM
Five drift Chambers for a muon tracking
Two Gas cylinders
MRPCs will be here

## Slide 24: Time Jitter of the DRS4-Verion 5 (PSI Co.)
Scintillator signal -> NIM Disc. -> Split into two signals -> DRS4 (ch1, ch2)
Measured time between chs on the DRS4-V5.
(With time calibration ON)
(1ns/Div, 100mV/div)
RMS of T1 – T2
-> 2.6ps
RMS of T1 – T2
-> 23ps
(With time calibration OFF)
2.6/√2 = 1.83ps !
Two copied NIM signals connected to ch1 and ch2
RMS of T1 – T2
DRS4 Oscilloscope Screen on PC
DRS4-V5