## Slide 1: Contents

## Slide 2: Stave and Barrel Design and FEA Analysis Daniel Cacace Brookhaven National Laboratory

## Slide 3: Motivation
Stave
  The stave design was based on HDI geometry.
  The HDI needs rigidity and cooling (3W).
  The stave supports two HDIs (4 sensors and 52 chips).
Barrel
  The barrels supports 56 staves (L1: 24 and L2: 32) (224 sensors and 2912 chips).
  The barrel design was based on stave design and requirements.
Both
  The stave needs sufficient clearances between adjacent staves.
  The stave needs to accommodate the MVTX (cone).

## Slide 4: Requirements
Physics
|h| ≥ 1.0 @ |Zvertex|= 10 cm
100% φ coverage
X/X˳ ≤ 1.25% per ladder
Mechanics
15°C ≤ T ≤ 22°C
δ ≤ 0.005”
ω ≥ 100Hz

## Slide 5: Ladder

## Slide 6: HDI – Design and Radiation Length
HDI Thickness: 473 um
Width: 38.0 mm
z-length total: 400 mm Sensor thickness: 320 um
FPHX chip thickness: 320 um
HDI Material | Thickness [μm] | 
Copper | 38 | 0.26%
Polyimide | 380 | 0.14%
 | Total | 0.40%
HDI Material | Thickness [μm] | 
Copper | 38 | 0.26%
Polyimide | 380 | 0.14%
 | Total | 0.40%
The HDI is composed of 7 copper layers. 4 solid ground or power layers and 3 signal line layers.

## Slide 7: Stave – Average Radiation Length
Material | Thickness [μm] | Radiation Length (mm) | 
CFC Flat | 0.3300 | 256.4122 | 0.1287
CFC Formed | 0.3411 | 256.4122 | 0.1330
CFC Tube | 0.1033 | 282.2909 | 0.0366
Foam | 1.4740 | 3771.3741 | 0.0391
Epoxy | 0.1016 | 298.7463 | 0.0340
Water | 0.0826 | 356.7854 | 0.0231
 |  | Total | 0.3946
Material | Thickness [μm] | Radiation Length (mm) | 
CFC Flat | 0.3300 | 256.4122 | 0.1287
CFC Formed | 0.3411 | 256.4122 | 0.1330
CFC Tube | 0.1033 | 282.2909 | 0.0366
Foam | 1.4740 | 3771.3741 | 0.0391
Epoxy | 0.1016 | 298.7463 | 0.0340
Water | 0.0826 | 356.7854 | 0.0231
 |  | Total | 0.3946
Material | Fraction | Radiation Length (mm)
CFC | 0.6 | 194.0909
Epoxy | 0.4 | 349.8941
 | Total | 256.4122
Water | 0.7 | 360.8000
Glycol | 0.3 | 349.2849
 | Total | 356.7854
Notes: 7
Le plan de l’expose se presente de la manière suivante :

## Slide 8: Ladder – Stave + Two HDIs and Radiation Length
Estimated Weight: 0.1lb. (0.445N)
Material | Thickness [μm] | 
Silicon | 320 | 0.30%
HDI | 473 | 0.40%
Stave | 3620 | 0.40%
 | Total | 1.10%
Material | Thickness [μm] | 
Silicon | 320 | 0.30%
HDI | 473 | 0.40%
Stave | 3620 | 0.40%
 | Total | 1.10%
All components are averaged over the area of the stave in the active region.

## Slide 9: Stave Design

## Slide 10: Stave Design – Assembly
Thickness: 0.76 mm
Height: 3.76 mm
Width: 38.00 mm
Length: 497 mm
Material: Carbon Fiber, Polymethacrylimide (PMI),
Stainless Steel and Epoxy
(radiation length = 0.40% )

## Slide 11: Stave Design – Parts
Tube Bend
(316 Stainless)
CFC Flat
(NT91500-520S + 25R
+ 20301A 34 GSM)
Endcap
(Carbon PEEK)
CFC Formed
(NT91500-520S + 25R + 20301A 34 GSM)
Rohacell 110 RIST Foam
(polymethacrylimide)
CFC Tube OD: 3mm,
ID: 2mm (T700)
Pin Receptacle
(Copper)
Tube Sleeve
(316 Stainless)
Epoxy
(Hysol 9396)
Epoxy
(EP75-1)
Between all parts

## Slide 12: Stave Tube – Assembly Drawing

## Slide 13: Stave – Assembly Drawing

## Slide 14: Stave FEA Analysis

## Slide 15: Structural – Under its Own Weight
Deflection – MAX: 0.0001 in (2.5 um)
Stress – MAX: 110 psi (0.6 MPa)
Boundary Conditions: Endcaps simply supported, HDI weight added

## Slide 16: Vibration – Natural Frequencies
First Mode – 453 Hz
Second Mode – 796 Hz
Boundary Conditions: Endcaps simply supported

## Slide 17: Thermal – Temperatures
Stave ΔT – 5.1 °C (9.2 °F)
Sensors ΔT – 1.6 °C (2.9 °F)
Boundary Conditions: Inlet temp 15C, flow rate 0.12l/m, natural convection, chips dissipate 3W total

## Slide 18: Thermal – Midplane Cross Section
Temperature
Heat Flux
Boundary Conditions: Inlet temp 15C, flow rate 0.12l/m, natural convection, chips dissipate 3W total

## Slide 19: Barrel Configuration

## Slide 20: Barrel – Two Layers
Full Detector
Half Barrel
Outer Layer
Inner Layer

## Slide 21: Barrel – Two Layer Configuration Staves
Water Cooling
1a (Inner)
1b (Outer)
2a (Inner)
2b (Outer)

## Slide 22: Barrel – Two Layer Configuration Active Area
1a (Inner)
1b (Outer)
2a (Inner)
2b (Outer)
The width of the active area is 52.6% of the total width of the ladder. In order to have overlap for full PHI coverage and have a reasonable stave thickness, the ladders were stager radially with no tilt.

## Slide 23: Barrel – Two Layer Configuration Numbers
Barrel | Center of Sensor Tangent Radius (mm) | Pseudo rapidity | QTY of Ladders | Angle (deg) | Coverage (PHI) (%) | Overlap (%) | Clearance (mm) | Chip Power Dissipation (W) | Stave Rad Length (%) | Barrel Rad Length (%)
1 | - | - | 24 | - | 100 | 2 | 2.00 | 62.30 | 0.80 | 2.20
1a (Inner) | 71.88 | 1.37 | 12 | 0 | 53 | 0 | 0.60 | 31.15 | 0.40 | 1.10
1b (Outer) | 77.32 | 1.31 | 12 | 0 | 49 | 0 | 3.80 | 31.15 | 0.40 | 1.10
2 | - | - | 32 | - | 100 | 2 | 2.22 | 83.07 | 0.80 | 2.20
2a (Inner) | 96.80 | 1.12 | 16 | 0 | 53 | 0 | 0.60 | 41.53 | 0.40 | 1.10
2b (Outer) | 102.62 | 1.07 | 16 | 0 | 49 | 0 | 3.12 | 41.53 | 0.40 | 1.10
Total | - | - | 56 | - | - | 100 | 11.22 | 145.37 | 1.60 | 4.40
BUS Extender
BUS Extender
|h| ≥ 1.0 @ |Zvertex|= 10 cm
Signal
Signal
Silicon Module
Silicon Module
Ladder Concept
HDI
HDI
|h| a | ZSi - Zvertex| / Radius
465.5 mm
Notes: 23
Le plan de l’expose se presente de la manière suivante :

## Slide 24: Barrel Design

## Slide 25: End Rings - Half Barrel, One Side
End Ring 1
End Ring 2
End Ring 3
Gap for layers 1a and 1b
Gap for layers 2a and 2b
Dry Air/Nitrogen

## Slide 26: Barrel – Cooling and Extension Connection
Ladders – No Connections
Ladders – Both Connections

## Slide 27: Barrel – Carbon Fiber Skins and Cones
Estimated Weight: 10lb. (44.5N)
Both Sides Total: 20lb. (89N)
Skin Thickness: 0.010” (0.25mm)
Cone Thickness: 0.063” (1.60mm)

## Slide 28: Barrel - Assembly

## Slide 29: Barrel - Services
With Inner Carbon Fiber
Without Inner Carbon Fiber

## Slide 30: Barrel - Integration

## Slide 31: Barrel FEA Analysis

## Slide 32: Structural – Under its Own Weight
Deflection – MAX: 0.0002 in (5 um)
Stress – MAX: 12 psi (0.08 MPa)
Boundary Conditions: Carbon fiber cones fixed-fixed, HDI weight added

## Slide 33: Structural – Under its Own Weight
Deflection – MAX: 0.0025 in (63.5 um)
Stress – MAX: 170 psi (1.17 MPa)
Boundary Conditions: Carbon fiber cones fixed-fixed, HDI weight added

## Slide 34: Vibration – Natural Frequencies
First Mode – 83 Hz
Second Mode – 85 Hz
Boundary Conditions: Carbon fiber cones fixed-fixed

## Slide 35: Summary

## Slide 36: Pre-Production

## Slide 37: Summary
The Design of the stave meets all requirements for:
  HDI ✓
  Coverage ✓
  Radiation Length ✓
  Rigidity ✓
  Stress ✓
  Modes ✓
  Cooling ✓
  Geometry ✓
  Clearances ✓
  Tolerances ✓
Ready for ladder production!

## Slide 38: Technical Data Sheets

## Slide 39: Carbon Fiber - K13C2U

## Slide 40: Carbon Fiber - XN-90-60S

## Slide 41: Carbon Fiber - T700

## Slide 42: PEEK - CA30

## Slide 43: Foam - Rohacell 110 RIST

## Slide 44: Epoxy - 25R

## Slide 45: Epoxy - EP75-1

## Slide 46: Epoxy - Hysol EA 9396

## Slide 47: Epoxy - TC2810

## Slide 48: Epoxy - ABLESTIK 2902