## Slide 1: EIC IP6 IR Design Overview
Holger Witte
March 12-13, 2021

## Slide 2: Outline
Overview
  Requirements
  General constraints
  Present IR
Luminosity
  Focusing
  Crab crossing
IR Magnets
  Apertures and Challenges
  Engineering

## Slide 3: EIC IR: Overview
Forward
Rear
RHIC yellow ring: EIC hadron ring
Add electron storage ring in existing tunnel (and the RCS)
IR location: IR6

## Slide 4: IR Requirements
EIC IR designed to meet physics requirements
  Machine element free region: +/- 4.5m main detector
    (Efforts underway to increase this to -4.5/+5m)
  ZDC: 60cm x 60cm x 2m @ ~30 m
  Scattered proton/neutron detection
    Protons 0.2 GeV < pt < 1.3 GeV
    Neutron cone +/- 4 mrad
Machine requirements
  Small b*y: quads close to IP, high gradients for hadron quads
  Crossing angle: as small as possible to minimize crab voltage and beam dynamics issues
    Choice: 25 mrad
  Synchrotron radiation background
    No bending upstream for leptons (up to ~35m from IP)
    Rear lepton magnets: aperture dominated by sync fan

## Slide 5: Considerations
Geometry
  RHIC tunnel (injection, RHIC magnets, RCS, eSR)
  Experimental hall (IR6)
  Space for detector
Physics considerations
  See requirements, other talks
Accelerator/optics
  Match into existing machine
  Dispersion, chromaticity

## Slide 6: Considerations (cont.)
Crab cavities
  Location
  Geometry
  Phase advance
Engineering
  Magnets: feasibility
  Cryostating
  Utilities
Project
  Cost, risk
  R&D required
  Vendors

## Slide 7: EIC IR: Forward Direction
Interleaved magnet scheme
  Adding magnets is challenging
Why are these magnets difficult?
  Required field
  Aperture
  Geometric constraints
Field
  Accelerator physics
  Hall/ring geometry
  Magnet technology constraints
Large apertures of magnets
  Proton forward: physics
  Rear electron: Synrad
Name | R1 | length | B | grad | B pole
 | [m] | [m] | [T] | [T/m] | [T]
B0ApF | 0.043 | 0.6 | -3.3 | 0 | -3.3
Q1ApF | 0.056 | 1.46 | 0 | -72.608 | -4.066
Q1BpF | 0.078 | 1.61 | 0 | -66.18 | -5.162
Q2pF | 0.131 | 3.8 | 0 | 40.737 | 5.357
B1pF | 0.135 | 3 | -3.4 | 0 | -3.4
IP
Hadrons
Electrons
Superconducting

## Slide 8: Hadron Forward - Apertures
275 GeV
41 GeV
100 GeV
Magnet aperture optimization:
Magnets tilted and displaced
Magnets split in two (e.g. Q1A and Q1B)
275 GeV
41 GeV
100 GeV
275 GeV +1.3 GeV px
275 GeV -1.3 GeV px

## Slide 9: EIC IR: Rear Direction
2-in-1 magnets
  Common yokes
Main issue: space between magnets
  Crossing angle
Large aperture due to synrad fan
  Comes from low-beta quads
Name | R1 | R2 | length | grad | B pole
 | [mm] | [mm] | [m] | [T/m] | [T]
Q1ApR | 20 | 26 | 1.8 | 78.4 | 2.0
Q1BpR | 28 | 28 | 1.4 | 78.4 | 2.2
Q2pR | 54 | 54 | 4.5 | 33.8 | 1.8
Name | R1 | R2 | length | B | grad | B pole
 | [mm] | [mm] | [m] | [T] | [T/m] | [T]
Q1eR | 66 | 79 | 1.8 | 0 | 14 | -1.1
Q2eR | 83 | 94 | 1.4 | 0 | 14.1 | 1.3
B2eR | 97 | 139 | 5.5 | 0.2 | 0 | -0.2
Bethe Heitler
Hadrons
Electrons
Superconducting

## Slide 10: Luminosity and Focusing
Strong focusing by =5 cm
Luminosity ~ 1/cross section
A smaller spot size at the IP means more luminosity
At the IP, (beam size)X(beam divergence)= const. in each plane (emittance)
For a given beam (= fixed emittance), a smaller IP beam size means larger divergence
A larger beam divergence leads to a larger beam size at the nearest focusing magnets – (size at magnet)=(divergence)X(distance)
Magnets need to have larger aperture while gradient (= focusing strength) remains the same – peak field at magnet poles is technically limited (also: crosstalk)
Focusing elements for both beams need to be as close as possible to the IP
  Divergence: ‘spread’ of the beam away from the central trajectory.

## Slide 11: Crossing Angle
Crossing angle: 25 mrad
  Hadrons: 17 mrad
  Electrons: 8 mrad
Smaller crossing angle: beams less separated, magnet issues
Larger crossing angle: magnet issues, crab cavities, beam dynamic issues
25 mrad

## Slide 12: Crossing Angle and Luminosity
Long (~+/-6 cm), skinny (100 um) bunches colliding at an angle have very little overlap
With 25 mrad crossing angle, each particle can only interact with a +/-4 mm thick slice of the +/-6 cm long oncoming bunch
In head-on collisions, every beam particle in one beam can potentially interact with every particle in the other beam

## Slide 13: Crab crossing to the rescue
Head-on collision geometry is restored by rotating the bunches before colliding (“crab crossing”)
Bunch rotation (“crabbing”) is accomplished by transversely deflecting RF resonators (“crab cavities”)
Actual collision point moves laterally during bunch interaction
Challenges
  Bunch rotation (crabbing) is not linear due to finite wavelength of RF resonators (crab cavities)
  Severe beam dynamics effects
  Physical size of crab cavities

## Slide 14: EIC IR
Larger crossing angle:
Cannot do more in hadron line (field/space issues)
Electrons: Synrad issues (kW of power already)
Forward
Rear
Hadrons
Electrons
Note: forward magnet cryostat is 94” dia

## Slide 15: Detector Solenoid Effects
Coherent orbit distortion
Transverse coupling
Rotation of the crabbing plane
Polarization tilt

## Slide 16: Coherent Distortion of Ion Orbit
Ions
Top view
Ions
End view
Ions
Vertical kicks by the solenoid fringe fields
mrad (41 GeV)
Rotation of the interaction plane inversely proportional to the beam energy
Side view
Particles traveling at angle through solenoid: orbit distortion due to end fields
Horizontal orbit distortion due to coupling

## Slide 17: Correction of Ion Orbit
Ions
Side view
The closer the kicks to the IP, the smaller the orbit excursion
Orbit excursion inversely proportional to the beam momentum
Concern for field non-linearity at large offsets
Vertical kick #1 (radial magnetic field)
Vertical kick #2
mm
(41 GeV)

## Slide 18: Q2pF – Collared Magnet
Hadron quadrupole
  Gradient: 41 T/m
  3.8m long
  Aperture 262 mm
    Coil R=140mm
    Pole tip field: 5.74T
  e-beam: 36-42cm distance
Field-free region for electrons
Magnet limitations
  Gradient/field
  Aperture
  Stray field
Particle Orbits
Neutron cone

## Slide 19: Q2pF Simulation Results
Field-free region: <1mT
Can be shielded with mu-metal
Peak field on wire: 7.6T

## Slide 20: Crosstalk
Iron
B
Refers to flux from one magnet leaking into the other
Leads to field quality issues
Depends on geometry and field/flux
Electrons: field free
Hadrons: quadrupole magnet
Q2pF
≈40 cm
Common issue for all IR magnets

## Slide 21: Magnet Engineering
Q1ApF
Q1BpF
Q1eF
Q2pF
B1pF
B1ApF
Standalone 48” cryostat
B0pF
B0ApF
Common split cryostat
Cold mass adjustments within cryostat
Each cold mass independently anchored
Common helium vessel, with bellows between all magnets

## Slide 22: Rear Side Integration / Beampipe
e-
p+
Ø66”
Q2pR – B2eR
Ø54”
Q1BpR – Q2eR
Ø42”
Q1ApR – Q1eR
IP
Separate cold masses - helium vessels
Separate circular cryostats with decreasing OD’s toward IP

## Slide 23: IR Layout
IR quadrants not independent of each other
Changing one sector implies changing another one
Also: need to get back to RHIC ring (HSR)
Forward
Rear
Hadrons
Electrons

## Slide 24: Synchrotron Radiation
Origin: quads and bending magnet upstream
Tails: can produce hard radiation
  Non-Gaussian
Central chamber
Beam pipe envelope and synrad heating
Even with masking: significant heating to deal with
Courtesy C. Hetzel
B2eR exit
Pumps

## Slide 25: EIC IR Effort
Ongoing effort for >4 years
  This is when I got involved…
Involves >40 people
  Part/full-time
Work split into several sub-groups/task forces
  Synrad, magnets, spin rotators, correctors
  Connections with multiple other areas/groups
Devil is in the details
Total effort?

## Slide 26: IR Design Choices
High Lumi
Strong Focusing
Large Pt acceptance
Small beam divergence at IP
Small Emittance
Magnets close to IP
Complicated magnetic shields
Crossing Angle reduced lumi instab.
Crab cavity
Expensive, beam blow-up
Large chromaticity, unstable beam
Quick separation
Synchrotron radiation generation
Detector damage/backgrounds
Reduced Acceptance
Courtesy of F. Willeke

## Slide 27: What are we working on?
Implementing 0.5m shift forward side
  Affects layout, re-optimizing magnet apertures/positions
  Needs to be approved by Change Control Board
Implement correctors
  Skew-quadrupoles, solenoid compensation
  Orbit correction
Magnet design work
Lots of challenging detailed work to be done
  Beampipe
  BPMs

## Slide 28: Summary
IR developed to meet physics requirements
  Meets requirements of ‘white paper’
  See Alex Jentsch’s talk
  Is there anything we have been missing?
Many considerations went into this IR
  Geometric constraints
  Engineering feasibility
  Magnets, cryostating

## Slide 29: Acknowledgements
J. Adam, M. D. Anerella, J.S. Berg, W. Christie, J. Cozzolino, C. Montag, E. C. Aschenauer, A. Blednykh, A. Drees, D. Gassner, K. Hamdi, C. Hetzel, H. M. Hocker, D. Holmes, A. Jentsch, H. Lovelace III, A. Kiselev, G. McIntyre, R. B. Palmer, G. Mahler, B. Parker, S. Peggs, S. Plate, V. Ptitsyn, G. Robert-Demolaize, K. S. Smith, S. Tepikian, P. Thieberger, J. Tuozzolo, F. J. Willeke, M. Blaskiewicz , J. Tuozzolo, Y. Luo, H. Witte, Q. Wu, Z. Zhang, M. Stutzman, R. Gamage, P. Ghoshal, T. Michalski, V. Morozov, W. Wittmer, M. K. Sullivan, Y. Nosochkov, A. Novokhatski
… and many more!

## Slide 30: Additional Slides

## Slide 31: Considerations IP8
Going from outer arc into inner arc
  IP6: from inner to outer arc
Present IR not portable to IR8
Geometric issues
IR8: Tunnel dia. 6.3m to 60m (then 5.3m dia)
IR6: 7m dia. +/- 140m
60m

## Slide 32: Considerations IP8
If using IP6 forward dipole configuration (HSR bends away from ESR)
  Beam is bent further inside
  Can't bend back until we reach the crabs
  Requires creating a roughly 2 m transverse displacement over around 50 m length; lots of extra dipoles, issues with dispersion matching
If we put ZDC on the outside, bending HSR toward the ESR
  25 mrad crossing angle not possible: lines diverge slowly, crab cavity transverse size creates collision between HSR/ESR lines

## Slide 33
450W
704W
Taper
22.5W
Q0eF
87W
Q1eF
Heat Load in Cold Magnets

## Slide 34: Crossing angle collisions
Beam energies of electrons and hadrons are vastly different in EIC
Focusing elements for electrons would have only little effect on hadrons, while hadron magnets would overfocus electrons
Beams need to be separated into their respective focusing systems as close as possible to the IP
A separator dipole would have to deflect the (“weaker”) electrons and would therefore generate a wide synchrotron radiation fan that would need to pass through the detector – requires large beam pipe diameter (HERA-II)
Best solution: Crossing angle collisions!

## Slide 35: Nobody’s perfect
Bunch rotation (crabbing) is not linear due to finite wavelength of RF resonators (crab cavities)
Long hadron bunches are “S”-shaped during collision
Distorted shape results in transverse offset between electron bunch and head and tail of proton bunch – reduced luminosity and severe beam dynamics effects
Longer bunches, skinnier bunches, or increased crossing angle all make this worse
Higher harmonic crab cavities can “straighten out” the kick and therefore the bunch, but at a cost – space and money
EIC already plans on 197 MHz crab cavities, plus 394 MHz harmonics
197 MHz as low as technically feasible (niobium sheets for cavity production, cavity size in tunnel)

## Slide 36: IR Magnets - Overview
9 Direct Wind Magnets (S-MD)
6 Collared Magnets
1 Special Magnet
Three groups of superconducting magnets
  All NbTi
(Also: normal conducting magnets, not addressed here)

## Slide 37: B0pF Spectrometer Magnet
Superconducting combined function magnet
  1.3T for hadrons
  Created by quadrupole magnet
Inner clear aperture of 180 mm radius
Electrons: 15T/m gradient
  In B0pF aperture
  Use dipole to create zero dipole field for electrons
  Use electron quad to tune gradient
Quadrupole
Main dipole & quad coils
Electron quad coil
Warm beam tube
20 mrad Cone