## Slide 1: An eco-friendly gaseous RICH @ EIC
Why C-F gases are the most used ?
You need as high as possible photon rate:
  Nphotons sin2q 2 (n-1) at saturation, in gas
You need as small as possible chromatic dispersion
  This is the intrinsic error affecting the measurement of the Cherenkov angle that cannot be recovered
proportional
to Nphotons
Proportional to
chromatic dispersion

## Slide 2: An eco-friendly gaseous RICH @ EIC
From YR and related comments
by external readers
Comment by H. Montgomery:
ISSUES with C-F gases
These gasses are not eco-friendly
  They attack O3
  They have high Global Warming Power
    C4F10: 9200 (100y horizon)
    CF4: 6600
    CO2: 1 (by definition)
    CH4: 28 (for comparison)
  A system ensuring no emissions and losses (if feasible) adds complexity to the gas handing system
The cost is growing and availability is difficult
  Most recent C4F10 procurement for COMPASS RICH (2019-2020)
    One single producer for large quantities identified
    Delivery after 1y from issuing the order
    Cost: 208 GBP per kg for large quantity (630 kg)

## Slide 3: An eco-friendly gaseous RICH @ EIC
Use an innocent gas with good chromaticity and
tune its refractive index using pressure
visible range
Of course,
a vessel standing pressure is needed
  Engineering approach required:
  The vessel can be light using high-tech up-to-date approaches
  Some preliminary design studies initiated in Italy; the help of the hosting labs is a necessity