## Slide 1
TK Hemmick for the EIC Tracking Consortium
Plans for a Ring-Imaging Cherenkov Detector at the Electron-Ion Collider

## Slide 2: NSAC Rumors lead us to believe:
  What is the spatial mapping of quark and gluon fields in the nucleon AND nucleus.
  Is the missing spin to be found via quark orbital momentum?
  Are new phases of matter (Color-Glass Condensate) accessible at low x in nuclei?
You
Will answer questions
Using these Devices
On this timeline (??)
Not You
  eRHIC or MEIC
  EM Calorimeters
  Hadronic Calorimeters
  Tracking (subject of workshop)
  PID (subject of this talk)
機會 (opportunity)

## Slide 3: Special Thanks for Images in this Talk:
Images enhanced by the Philadelphia community.
DFTI: Chestnut Street, Downtown Philadelphia…
Celebrating the opening of DFTI (Dress for the Image) Boutique

## Slide 4: The challenge in proton-electron scattering:
Scattering from a high-x quark yields energetic hadronic debris in the “proton” direction.
PID Challenging!
up
up
down
Proton
electron
electron
Jet of Hadronic Debris

## Slide 5: Ejectile Spectra:
ep (eA) HIGHLY asymmetric.
Moderate momenta for ALL species mid- and negative-h.
BAM! Very large lab momenta at positive-h.
Fwd Hadron ID challenging.
50-60 GeV/c Lab Momentum!

## Slide 6: Imaging Cherenkov Light
Cherenkov Light – “Optical Boom”
Cherenkov angle depends upon velocity & index
  Low n distinguishes particles to high momentum.
  Low n yields less light!
Go where the light is:
  Deep UV Cherenkov yield is highest…how to get there?
  PHENIX HBD: No Optics allows for VERY low lmin
  But a RICH requires optics! What to do?
Cherenkov Angle determines b

## Slide 7: Commercial (small) mirror Reflectivities
Bare aluminum mirrors no good (AlO…high cutoff).
Better has MgF2 overcoat (right hand).
  Exists and has been made to large scale.
  Not good enough.
Thin Film Interference!
  Tuned for peak at 120 nm.
  Retrieves (most of) the lost light.
Thin Film Interference

## Slide 8: Gas Electron Multiplier for PHOTONs!
Two copper layers separated by insulating film with regular pitch of holes.
HV creates very strong field such that the avalanche develops inside the holes
Just add the photocathode
By the way: no photon feedback onto photocathode
The original idea by F.Sauli (mid 90s) US Patent 6,011,265
Traditionally CHARGED PARTICLE detectors (not photons)
150μ
80μ
CAVEAT: PHENIX HBD too low gain (4000) to see single photons!

## Slide 9: Where do you get more gain?
5 GEMs in a stack.
Highly segmented GEMs
  10x10 cm2
  Low R-divider chain.
  Capacitive spark sensor.
  Never Sparked once.
Harder than you think…
10000 gain (staged)
  N=1  Poisson(10000)
  N=10 >Poisson(100)
Gain in a gas (Ninf.)
  Pulse height spectrum of single electron avalanche is EXPONENTIAL!

## Slide 10: Beam Studies (FLYSUB Consortium)
TK Hemmick
Shift Crew 2
Shift Crew 1

## Slide 11: Ring Imaging Cherenkov Detector Prototype
32 GeV Beam Momentum

## Slide 12: Number of Pads Included in the Fit:
Pion
Kaon
Proton
# pads
# pads
# pads
# pads
32 GeV
32 GeV
32 GeV
32 GeV
R2

## Slide 13: Complete Set of Radii Results:
Reasonable results at all measured energies.
NOTE: 32 GeV is the highest available energy for Kaons at FTBF.
Pion
Kaon
Proton
Kaon
Pion
32 GeV
20 GeV
Pion
Kaon
25 GeV

## Slide 14: Scaling of the Radius With Expectation
All data is used with equal weights.
Index of Refraction is free parameter.
Fitted result: n = 1.000558 (as expected!).

## Slide 15: Understanding the widths.
Dispersion:
Segmentation:
“Prediction”
  Constant = 244 microns.

## Slide 16: Removing FNAL Beam Spread…
Hexagon pads should NOT be used at EIC (too coarse).
Dispersion becomes limiting factor.
500 micron (sigma) photon position resolution is easy goal.
2.5 sigma separation at 60 GeV.
Practical Limit: Momentum Resolution more than RICH
NOTE: Assumptions yield “worst case”

## Slide 17: Charge Division Challenges.
Charge spot on pad plane due to a single photon is SMALL.
  Low diffusion of gas during avalanche.
  Fortunately “hole mismatch” among 5 GEMS widens charge cloud
  Extreme challenge for geometrical charge division (pad size too small).
Resistive charge division:
  DC-coupled (classical): preamp inputs connected via resistive layer. Dangerous.
  AC coupled (ATLAS/ILC):
Charge injection
Resistive Layer
pads

## Slide 18: Modeling Dynamic Signal Propagation
Dynamic Charge Dispersion Simulation (ala ILC):
  All components have to be convoluted,
  [[R*L]*A](t)=RLA can be “obtained” analytically
  [RLA*Q](t) has to be solved numerically (working on).
Recent News:
  THREE(!!) students work under the direction of Klaus Dehmelt solving Telegraph Equation.
  Initial results show “challenging” narrow sweet spot for signal propagation.

## Slide 19: So…it works…you gonna build this for EIC?
Maybe.
Initial project has proved to be a 100% successful implementation of the conceptual design.
It *WILL* be a viable choice for EIC, but will not be a unique solution to forward PID issues:
  ID’s the highest momentum hadrons (good!).
  ID’s *ONLY* the highest momentum hadrons (not so good).
TKH Personal opinion:
  Today we’ve seen a cavalcade of successful R&D efforts/results.
  Choices are coming since we would not use all these techniques.
  The Electron-Ion Collider is “getting real.”
We must build COMMUNITY

## Slide 20: R&D Committee Questions:
We must all hang together or most assuredly we will all hang separately.
Benjamin Franklin, Philadelphia Pennsylvania
Today = Party Planning