## Slide 1
Requirements on EIC detector tracking system
Alexander Kiselev
EIC Tracking R&D Workshop at Temple University
May,9 2015

## Slide 2: Topics to be covered (or just touched)
Acceptance
Resolutions
Material budget
Present configuration
Future R&D wish list

## Slide 3: Acceptance: electrons
Q2 > 1.0 GeV2: rapidity coverage -4 < h < 1 is sufficient
Increasing lepton beam energy: scattered lepton is boosted to negative h
{PYTHIA events at different electron energy}

## Slide 4: Acceptance: hadrons
Increasing lepton beam energy boosts hadrons more to negative pseudorapidity
Increasing hadron beam energy influences max. hadron energy at fixed pseudorapidity
(and p±, K±, p± look
the same)
range -3<h<3 covers entire pt & z region important for physics
{same set of PYTHIA events; Q2>1 GeV2, 0.01<y<0.95, z>0.1 cuts applied}

## Slide 5: Configuration: whole detector
hadronic calorimeters
TPC
e/m calorimeters
RICH detectors
silicon trackers
GEM trackers
3T solenoid coils
-4<h<4: Tracking & e/m Calorimetry (hermetic coverage; symmetric layout)
electrons
hadrons
9.0m

## Slide 6: Configuration: tracker
TPC
silicon trackers
GEM trackers
3T solenoid coils
1.6m
2.0m
ALICE
SBS

## Slide 7: “Raw” momentum resolution
Resolution of a few percent up to (at least) |h|~3
p+
{Box generator at fixed momentum and pseudorapidity}

## Slide 8: Smearing in kinematic variables
{PYTHIA 20x250 GeV, NO bremsstrahlung} -> {GEANT} -> {Kalman filter track fit}
same procedure; simulation WITH bremsstrahlung
-> looks good despite poor resolution at low Y and long bremsstrahlung tails

## Slide 9: “Purity” in (x,Q2) kinematic bins
Describes migration between kinematic bins
Important to keep it close to 1.0 for successful unfolding
bremsstrahlung OFF
bremsstrahlung ON
Bremsstrahlung matters even for “almost transparent” detector
“Straightforward” tracking can hardly help at Y<0.1

## Slide 10: Material budget
On the ~5% X/X0 level pretty much in the whole acceptance
“Core” part only (no TPC outer field cage & endcaps; no GEMs)
Compare:
sPHENIX: ~10%
CMS : ~50%

## Slide 11: MAPS: present configuration
~0.3% X0 in acceptance per layer
digitization: discrete 20x20 mm2 pixels
4 layers at [24..160] mm radius
[-1 .. 1] nominal pseudorapidity coverage
vertex tracker:
forward/backward trackers:
Modeled according to ALICE ITS stave design
6 disks at [250 .. 1240] mm from the IP; Rmax ~195mm
Inner barrel radiation length scan

## Slide 12: MAPS: possible R&D topics
p+; h=3
Reduce further material budget
Minimize dead area material
Optimize cooling system
Develop forward disk setup
Minimize integration time
Basically need to adapt ALICE design to the EIC environment
pixel size effect

## Slide 13: TPC: present configuration
~2m long; gas volume radius [200..800] mm
1.2% X0 IFC, 4.0% X0 OFC; 15.0% X0 end-caps
digitization: idealized, assume 5 mm long GEM pads (so up to 120 space points per track)
assume (very) modest single point resolution (>400 mm at the IP)

## Slide 14: TPC: possible R&D topics
Attain ILD design single point resolution level
Establish operation in rather inhomogeneous magnetic field
Reduce inner field cage and endplate material budget
Minimize ion back flow
Establish acceptable dE/dx performance with GEM readout
Attain higher drift velocities (?)
RICH-mode operation (?)
Need a high resolution medium size TPC

## Slide 15: GEMs: present configuration
3 segmented disks behind the TPC end-caps
SBS design
digitization: 50 mm resolution in X&Y; gaussian smearing

## Slide 16: GEMs: possible R&D topics
Establish high resolution at large track slopes
Deliver reliable “vector” measurement
Improve shaper timing
Minimize material budget (?)
Need high resolution medium size GEMs
With-GEM vs no-GEM momentum resolution
NB: 50 micron spatial resolution assumed!
Develop large-scale GEMs
Be able to cover close-to-beam-line area

## Slide 17: MicroMegas option
EIC R&D
(Temple, Saclay)
Establish <100 micron spatial resolution in a 3T field
Deliver reliable “vector” measurement
Develop large scale samples
Minimize material budget
May want to have a fast device providing “vector” track seeds between MAPS and the TPC

## Slide 18: Auxiliary acceptance detectors
electrons
Legend:
beam pipe
hadron magnet apertures
electron magnet apertures
0 m
-4.5 m
+4.5 m
-15 m
-31 m
-33m
-45 m
+18 m
Roman Pots
low Q2 tagger
photon transport line with Al exit window
dipole magnet for pair spectrometer
emcals for lumi monitor

## Slide 19: Other considerations
Vertex resolution: with MAPS we get it better than 10 microns
Radiation hardness: not a problem?
Readout speed and FE -> main DAQ throughput: acceptable?

## Slide 20
Backup

## Slide 21: PID requirements
Lepton-PID:
h+/-, g suppression: 1:1 h <4 to 104:1 h >-1
Hadron-PID:
p/K ratio 3-4 K/p ~ 1 independent of h and (√s)
h <-3: 1 GeV< p < 10 GeV
-3<h <-1: 0.1 GeV < p < 4 GeV
-1<h < 1: 0.1 GeV< p < 4 GeV
1<h < 3: 0.1 GeV< p < 30 GeV
3<h : 1 GeV< p < 100 GeV
impact on PID technology

## Slide 22: Resolution in Kinematics variables & PID
high important to
unfold measured quantities to Born level
electron method
hadron method:
DA method:
Electron PID: E/p
Hadron PID: RICH
momentum resolution is critical for
RICH performance
(no photon
detector resolution
accounted here)

## Slide 23: SIDIS: Pion Kinematics
Cuts: Q2>1 GeV2, 0.01<y<0.95, z>0.1
Increasing hadron beam energy influences max. hadron energy at fixed h (and p±, K±, p± look the same)
Increasing lepton beam energy boosts hadrons
more to negative rapidity
-3<h<3 covers entire pt & z region important for physics

## Slide 24: EIC solenoid modeling
Yield large enough bending for charged tracks at large h
Keep field inside TPC volume as homogeneous as possible
Keep magnetic field inside RICH volume(s) small
main requirements:
Presently used design: MRS-B1
-> use OPERA-3D/2D
software