## Slide 1
Augmented Signal Processing in Liquid Argon Time Projection Chambers
with a Deep Neural Network
Software Effort to Improve LArTPC Reconstruction
JINST 16 (2021) 01, P01036
Haiwang Yu (BNL)
CPAD Instrumentation Frontier Workshop 2021
18-22 March 2021
Notes: Good afternoon, I am Haiwang from BNL.
The title of this talk is ...
It is software effort trying to

## Slide 2: Signal Processing (SP) of Liquid Argon TPC (LArTPC)
Signal formation in a 3 plane LArTPC “Single-Phase” wire-readout, from Bo Yu (BNL), https://lar.bnl.gov/wire-cell/
LArTPC is the central detector in many next-gen neutrino experiments, e.g. DUNE, SBN etc.
Calorimetry and rich topology information
LArTPC wire-readout measures induced charge ⊗ response
Signal Processing (SP) of LArTPC resolves charge from the original measurement:
Current state of the art SP algorithm based on 2D deconvolution:
JINST 13 P07006 (2018)
JINST 13 P07006 (2018)
Notes: LArTPC is the next ...
Due to heat and cost concerns it is most common to use wire-readout in large scale
This animation illustrated how signal is formed for a 3 plane wire-readout of a LArTPC.
electrons drift towards to the anode wire planes and induce current on the wires according to some detector/field response following this equation.
So a very upstream step of LArTPC reconstruction is to resolve the original charge distribution from the measurement.
The current Current state of the art SP algorithm based on 2D deconvolution is introduced in this paper.
2D here includes both time and space or long-range induction effect.

## Slide 3: Remaining Challenges in Current Signal Processing (SP)
“Prolonged Track” – weak signal
“Tear Drop” - distorted waveform
Noisy dots - noise
JINST 13 P07006 (2018)
unipolar
weak
SP
channel
channel
tick
tick
Raw
After SP
Notes: However, there still some remaining challenges in the LArTPC SP. I listed 3 here:
1,
2,
3,
The first one is most concerning as with gaps like this, the topology information would be degradated.

## Slide 4: Need to improve “ROI” (Region of Interest) finding
Decon. w/ Tight LF
Decon. w/ Loose LF
ROI Finding
ROI
Noise Filtering
+ 2D decon.
Waveform data
Decon. Waveform
SP Result
Information from Other Planes:
Utilizing plane redundency linked by geometry information
Machine Learning:
Quickly cover more phase space; Utilizing more complicated correlations
Decon for charge
Waveform ⟶ charge, dense
ROI:
Hit finding, sparsify
SP result:
Sparse, charge
Notes: In this talk we try to further improve the SP with software effort based on the current hardware setup.
The SP essentially does two things: ...
which corresponds to the two major steps, Deconvolution and ROI finding
In this study, we focus on improving the ROI finding by
1, utilizing more information, specifically ...
2, substitute the current

## Slide 5: ROI finding as semantic segmentation
Raw waveform vs channels
Tagged ROI
channel
tick
2D semantic segmentation – UNet
arXiv:1505.04597
UNet: auto encoder-decoder + skip connections
Output is sparsely connected components
Input and output are similar at leading order
Forked a Pytorch implementation: https://github.com/HaiwangYu/Pytorch-UNet
intermediate images
w/ domain knowledge
channel
tick
...
Notes: For the ROI finding alg:
We treat this as 2D semantic segmentation.
And used the UNet which showed good performance in segmentation in other domains.
The U-Net contains a auto-encoder-decoder + skip connections.
However, we do not want to feed the raw ...
But engineer the input first with our domain knowledge on the LArTPC

## Slide 6: Muti-Plane Information – Geometry
1, make time slices
2, Matching active wires (with initial ROI) from multiple planes
3, On target plane, tag 3-Plane matched ROIs (MP3) or 2-Plane matched ROIs (MP2)
MP3
Using other plane information projected to the target plane: utilizing plane redundancy
Inspired by Wire-Cell ‘3D Imaging’.
  arxiv:1803.04850
Key algorithm “Fast projection” realized using “RayGrid” tools: https://github.com/WireCell/wire-cell-docs/blob/master/presentations/updates/20190321/latexmk-out/img.pdf
active wire in the time-slice :
ref. plane, target plane
in-active wire in the time-slice
MP2
U
V
W
channel
channel
channel
time
U
W
V
Notes: The idea is quite simple: when the info on one plane is not enough, we use other plane info to help.
This is possible when we have redundant planes, meaning 3 or more.
And we can use geometry information to link them together.
Specifically are 3 steps:
1,
2,
3,
This idea is inspired by the Wire-Cell ‘3D Imaging’.

## Slide 7: Input and label for DNN - ProtoDUNE Single-Phase simulation
Label
loose
tight
MP3
MP2
Input candidates
tight/loose: deconvolution with tight/loose low frequency filter
label was made by rasterization of charge depos – 2D gaussian response
Notes: Here are one example showing ...

## Slide 8: ProtoDUNE Single-Phase
Sketch of a ProtoDUNE-SP APA
from arxiv:1706.07081
major components of the ProtoDUNE-SP TPC
from arxiv:1706.07081
ProtoDUNE Single-Phase (the NP04 experiment at CERN) is designed as a test bed and full-scale prototype for the elements of the first far detector module of DUNE (next-generation, long-baseline neutrino oscillation experiment).
Notes: Speaking of ProtoDUNE, it is a full scale ...
This plot shows the major ...
And this plot shows the wire geometry

## Slide 9: Signal Simulation Validation
U plane
MC scaling: 1.6
Tick: [570, 970]
Ch: [8050, 8200]
V plane
MC scaling: 1.6
Tick: [570, 970]
Ch: [8950, 9200]
MC (black)
MC (black)
MC (black)
W plane
MC scaling: 1.6
Tick: [570, 970]
Ch: [9500, 9750]
Average waveform: data vs. MC
2D convolution based simulation for LArTPC
JINST 13 P07006 (2018)
Software stack:
  LArSoft for the generator and Geant4 simulation
  Wire-Cell Toolkit for the detector response
Notes: A critical factor for a ML algorithms to really work in physics analysis is to have a good simulation that represent data features correctly.
We used 2D convolution based simulation for LArTPC which is available in the LArSoft + Wire-Cell software stack.
These plots show good consistency between simulation and data.
This is really important if we want to use our algorithms on real data.

## Slide 10: Training
Efficient network – 500 samples already provide good performance – 6 min/epoch
Platform: I9-9900K, 32 GB memory, Nvidia GTX 2080 Ti 11GB, Samsung 970 500GB NVMe SSD
Sample: 500 APA Planes using cosmic generator (450 training, 50 validation)
Loss: cross entropy
Optimizer: Stochastic Gradient Descent with momentum
Notes: In my opinion, one important factor to consider for a practical ML algorithms is its efficiency.
In principle, if we have infinite amount of data and computing resource, a FC network with enough nodes and layers could do any thing.
But it is unpractical.
In this study, our network design + input engineering is pretty efficient.
With only 500 samples in the training, we already got pretty good performance, which we will show later.
And this leads to a low training time of 6 min/epoch.

## Slide 11: Evaluation with simulation
DNN ROI finding has higher efficiency and purity than the reference ROI finding especially at large angles.
More effective on tracks have asymmetric angles induction planes
DNN w/o MP information performs slightly better than Ref. but much worse than DNN w/ MP information
ROI finding on V plane
a
b
c
pixel based evaluation:
eff = (0 + 3 + 0)/(0+3+4) = 3/7
purity = (0 + 3 + 0)/(0+4+1) = 3/5
pixel labeled as ROI from truth
pixel labeled as ROI from reco.
Notes: The trained model was first evaluated with simulations of tracks at large angles:
These plots show the eff. and purity for 3 ROI finding algorithms:

## Slide 12: Example ROI finding event displays on simulated data
Truth
Ref.
DNN-ROI
no Geometry
DNN-ROI
with Geometry
straight-line prolonged tracks
cosmic track with a section featuring a large projection angle
an interaction vertex of a charged pion with many activities

## Slide 13
Reference SP
ProtoDUNE DATA
run: 5145
subRun: 1
event: 26918
V plane
Notes: We also tested the DNN ROI finding with pDUNE data
And I circled out some interesting cases

## Slide 14
DNN-SP
ProtoDUNE DATA
run: 5145
subRun: 1
event: 26918
V plane

## Slide 15
ProtoDUNE-SP Data
run: 5145
subRun: 1
event: 26945
V plane
Reference SP
ProtoDUNE: how and why
L. Manenti: X02.00001
and other ProtoDUNE Talks

## Slide 16
ProtoDUNE-SP Data
run: 5145
subRun: 1
event: 26945
V plane
DNN-SP
Notes: Also less noisier than the reference method

## Slide 17: Deep-Learning in Wire-Cell Toolkit
LarSoft Simulation
Energy Depos
WireCell Response
Add Noise
Raw waveform
WireCell
preprocessing for DNN
DNN Input
hdf5
Truth Tags
hdf5
WireCell
Truth Tagging
Model Training/Testing with Python API
TorchScrip Model in File
Raw waveform
WireCell
preprocessing for DNN
DNN Input
in memory
DNN ROI Finding
GPU/CPU
ROI
Training workflow
Production workflow
Established initial machinery for Deep-Learning in Wire-Cell Toolkit
https://github.com/WireCell/wire-cell-toolkit
Data preparing in LarSoft/Wire-Cell
Training with python
Production with C++
Notes: This DNN ROI finding is implemented in wct.
We also established the machineries for data preparing/training and production with the wct.

## Slide 18: Summary
DNN ROI finding algorithm provides a software improvement on LArTPC reconstruction
based on the the hardware feature - redundant wire plane
combines domain knowledge with machine learning
significant improvement on both simulation and ProtoDUNE-SP data
Ref. JINST 16 (2021) 01, P01036 for more.
Wire-Cell: https://lar.bnl.gov/wire-cell/

## Slide 19: Backup

## Slide 20: RayGrid fast projection
Non-orthogonal coordinate system
Projection on the “n” plane

## Slide 21
WireCell Detector Response Simulation
2D Conv.
Ramo’s theorem
=
Garfield, a drift-chamber simulation program User’s Guide, Veenhof, R. (1993)
Response matrix:
Field response from Garfield simulation
Electronic response
2D convolution – realized by FFT and IFFT
Add inherent electronics noise
M. Diwan. Basic mathematics of random noise part ½
Refer: JINST 13 P07006 (2018)
Hanyu Wei’ talk, DUNE collab. meeting May 2019
Inherent electronic noise spectrum for different lengths of wires, JINST 13 P07006 (2018)
Hanyu Wei’ talk, DUNE collab. meeting May 2019

## Slide 22: Signal vs. track angle
projection of a minimum ionizing particle (MIP) track on one induction plane

## Slide 23: Input Candidates for DNN - ProtoDUNE data
loose_lf
tight_lf
MP3
MP2
Notes: Here is one example inputs from pDUNE data

## Slide 24: Training
 | Unit Time | Total Time
Generator | 2 sec/event | 0.3 hour/500events
G4 | 23 sec/event | 3.2 hour/500events
detector response, truth tagging and waveform preprocessing | 68 sec/APA | 9.4 hour/500 APA
Network training | 6 min/epoch (1 epoch: 1 iteration of 500 APA sample) | 5 hour/50epoch
Sum |  | 17.9 hour

## Slide 25: Mean loss of image samples are also expected to vary
We validated this hypothesis using a bootstrapping method. 1000 test samples (each sample contains 50 images) were random chosen from a test data set. Mean loss value was calculated for each sample and the distribution is shown below. We can see that the sample mean loss has a Gaussian like distribution that varies from 0.0055 to 0.0075.

## Slide 26
ProtoDUNE Data
run: 5145
subRun: 1
event: 26925
V plane
Reference SP

## Slide 27
ProtoDUNE Data
run: 5145
subRun: 1
event: 26925
V plane
DNN-SP