## Slide 1
CORE: a COmpact detectoR for the EIC
CFNS CORE workshop, March 29-30, 2021
Pawel Nadel-Turonski
Stony Brook University

## Slide 2
a COmpact detectoR for the Eic (CORE)
CORE in Geant (fun4all)
A (nearly) hermetic general-purpose detector that fulfills the EIC physics requirements
A small size, in particular of the inner systems, is cost-effective and allows:
  An overall reduction in cost without performance loss
  Improved performance in critical areas without large additional cost
Risk is minimized by utilizing subsystems from the Generic EIC R&D program
B. Schmookler
Balance can be different in a Detector 1 or 2 proposal

## Slide 3
The core of CORE
inner CORE in Geant (fun4all)
B. Schmookler
Small solenoid (2.5 m long, 0.9 m inner radius)
  could be new, but compatible with ZEUS
Small central all-Si tracker (eRD25)
Radially compact, high-performance barrel DIRC Cherenkov (eRD14)
Dual-radiator RICH with outward-reflecting mirrors in the hadron endcap (eRD14)
Extended PWO4 EMcal coverage (up to 2p, h < 0) on the electron side (eRD1)
dRICH photosensors

## Slide 4
Solenoid options
The CORE solenoid is 2.5 m long with a 0.9 m inner radius
CORE is compatible with any field in the 2-4 T range
4 T is affordable due to the small volume of CORE
  Can be operated at 2 T (better acceptance, hID)
2 T is the current low-cost, low-risk baseline option
Ultimately the choice of field will be a collaboration decision
B. Schmookler
solenoid | field (T) | volume (m3) | 2020 cost (M$) | with 50% contingency
EIC-IP6 | 3 | 29 | 21 | 32
CORE | 4 | 6.4 | 11 | 16
CORE | 3 | 6.4 | 7 | 11
CORE | 2 | 6.4 | 4 | 6
cost (2020 M$) = 1.8 x 0.458 x (stored energy)0.7
M. A. Green and S. J. St. Lorant, Adv. Cryo. Eng. 39
The CORE and ZEUS solenoids have similar dimensions, and the latter could be used for CORE.
However, the low cost of a new 2 T solenoid limits the benefits of re-use.

## Slide 5
Central Si-tracker
B. Schmookler
A silicon tracker is compact, has a high resolution, and offers opportunities for future upgrades.
The tracker developed by eRD25 would utilize ALICE ITS3 technology and is designed for the angular resolution requirements of the DIRC, making it a good choice for CORE
 | ITS2/ALPIDE | ITS3
technology | 180 nm | 65 nm
pixel-size | 27 x 29 mm | 10 x 10 mm
thickness | 50 mm | 20-40 mm
Note: modern microprocessors use 7 nm technology. The (unfair) comparison shows an opportunity for future improvements.
eRD25 tracker
GEM layer (eRD6)
--> talk by E. Sichtermann

## Slide 6
CORE in the context of the Yellow Report
CORE systems are all designed to provide a cost or performance advantage, or be complementary to the YR reference detector
YR table 10.6 requirement matrix
CORE also seeks complementarity with the reference detector by improving muon identification, which would be useful for, e.g., charmonium production and GPD studies using timelike processes.
A small DIRC, for instance, provides the same performance as a large one, but is cheaper.
The small size makes CORE particularly suited for improving performance in two key areas: (e-side) electron ID and (h-side) hadronic calorimetry
  highlighted in the YR “matrix”

## Slide 7
e/𝜋 identification in the electron hemisphere
For the EIC, a clean identification of the scattered electron is essential.
The YR requirement matrix lists a pion suppression of up to 1:10-4 for the e-endcap and barrel.
Since the relative pion background rises at larger (less negative) h, the barrel region poses the greatest challenge and requires the best electron ID.
However, in the reference detector the best EMcal (PWO4) only covers the inner endcap (h < -2).
Q2 > 1 &
y < 0.95
to the right of orange line
B. Schmookler
h = -ln(tan(q/2))

## Slide 8
CORE solution for e/𝜋 identification in the electron hemisphere
CORE addresses the eID issue by extending the PWO4 EMcal coverage up to h < 0.
Additional e/p suppression (at least 1:10 up to 1.2 GeV) is also provided by the DIRC
The result is a barrel eID configuration that can provide good pion suppression with a high electron efficiency (potentially enabling measurement of APV).
A better energy resolution also improves photon detection in the electron hemisphere.
Q2 > 1 &
y < 0.95
to the right of orange line
B. Schmookler

## Slide 9
4𝜋 EMcal
The small size of CORE makes it affordable to extend the PWO4 coverage up to 2p.
  The PWO4 area will be half or less of that planned for PANDA, which is similar in size to CORE
An additional small-angle EMcal can be placed behind the main detector endcap
The PANDA PWO4 EMcal covers the endcap and barrel (outside of a DIRC)
up to 2p (h < 0) PWO4 coverage
h > 0 coverage (several options – including pre-showers for g/p0)
The h > 0 barrel EMcal should be relatively compact and projective
The endcap EMcal needs to be affordable and work well with a high-resolution Hcal
--> talk by C. Munoz Camacho
--> talk by C. Woody

## Slide 10
CORE 2p PWO4 EMcal superimposed on the YR reference detector
The much larger barrel EMcal for the reference is shown in green.
The CORE barrel EMcal is shown in red/white

## Slide 11
The inner part of CORE is independent of the Hcal configuration.
.
YR table 10.6 requirement matrix
Hadronic calorimetry
But the smaller size of CORE makes a high-resolution Hcal in the hadron endcap (h > 2) a particularly interesting option.
This would have a significant impact on measurements of jets where the energies are highest and tracking is least efficient
In the barrel and electron endcap, jet energies are lower and jets are best reconstructed from individual tracks (tracking, PID, EMcal).
Here, the Hcal is mainly used for individual low-momentum neutral hadrons (mostly KL). Resolution has a more limited impact.
--> talk by O. Tsai

## Slide 12
Muon ID
At the EIC, mid-rapidity muons have relatively low momenta, and it is important to minimize multiple scattering (placing a muon detector behind an Hcal is not feasible).
The Belle II KL-m (KLM) system
One can also try to enhance the muon ID capability of a more conventional barrel Hcal, or improve the energy resolution of a KLM-inspired system
Since jets are best reconstructed from individual tracks, one approach is to trade energy resolution for better muon and neutral hadron (KL) ID, and lower cost (cf. Belle II KLM)
--> talk by W. Jacobs
--> talk by O. Tsai

## Slide 13
Hadron Identification in the barrel (hpDIRC) and hadron endcap (dRICH)
Using aerogel and gas radiators with a single set of photosensors the dRICH provides continuous p/K separation of >3s up to 60 GeV and an excellent e/p separation (no TRD needed).
  e/p: 10s at 10 GeV
The hpDIRC has a p/K separation of >4s up to 6 GeV (and 2s at 8 GeV).
The minimum momentum for p/K ID in threshold mode is 0.2 GeV
--> talk by E. Cisbani, M. Contalbrigo
--> talk by G. Kalicy

## Slide 14
TOF in the hadron endcap
CORE with a gas-only RICH (eRD6) and LGAD-based TOF behind it
The dual-radiator RICH (dRICH) is a cost-effective solution with continuous coverage over a wide momentum range, but a simple TOF system could provide PID for the lowest momenta below the aerogel thresholds.
However, pending the implementation of the dRICH in fun4all, Geant simulations can start using a gas-only RICH in combination with high-resolution LGAD TOF, which is already implemented
CORE with a dual-radiator RICH (eRD14)

## Slide 15
Hadron Identification in the electron endcap
While high-resolution TOF is not competitive with Cherenkov detectors in the central barrel (small radius), it could be a good solution for the electron endcap.
A Si timing “start” layer (eRD29) could be added in-between disks
High-resolution TOF using LGADs or LAPPDs (which work up to 2 T)
t0 can be obtained using an electron scattered into the endcap and/or a separate ”start” layer integrated with the Si-tracker.
The TOF installation is modest and resolution could improve through future upgrades.
Alternatively, CORE could also support an aerogel RICH (e.g., the mRICH) by extending the endcap by 30 cm, for which there is plenty of space - although this would also extend the length of the PWO4 EMcal.
Complementarity?
--> talk by G. Giacomini

## Slide 16
Future upgrades – a few examples
Rapidly evolving technologies create natural upgrade paths
  Photosensors, Si-timing, S-tracking, optical meta materials, etc.
Advances in photosensor timing beyond 100 ps rms can in the shorter term increase the momentum reach of the DIRC; SiPMs could provide tolerance to very high magnetic fields.
The next generation of Si-trackers could improve position (momentum) resolution, readout speed, and further reduce mass.
At the time of an EIC mid-life upgrade, optical metamaterials might be available for use as Cherenkov radiator, greatly improving momentum reach for compact PID systems.
  Pioneering studies at SBU as part of eRD6

## Slide 17
Thank you!

## Slide 18
IR integration
Despite its compact size, CORE has a lot of room available for supports and services
In its nominal configuration, CORE fits into a -3 m to +4.5 m IR space.

## Slide 19
YR requirement matrix
YR table 10.6

## Slide 20
YR detector subsystem matrix
YR table 11.50