## Slide 1: Fast and full simulations in Geant4 for large-scale detector systems at the EIC with a plug and play modular approach
Makoto Asai (SLAC)
March 25, 2021

## Slide 2: Requirements
Requirements
  ability to reuse existing simulation works
  ease of switching detector options with comparable levels of detail
  ease of switching between detailed and coarse detector descriptions
  ease of leveraging new and rapidly evolving
    technologies, e.g., AI/ML
    computing hardware, e.g., heterogeneous architectures

## Slide 3: Initial work plan (1)
These requirements will be fulfilled by utilizing the “region” mechanism of Geant4.
  Each detector component is represented as a region, where the followings are taken care of.
    geometry description including different levels of detail,
    physics options including fast simulation and unique physics model configurations,
    and detector responses based on geometry and physics options
  Regions should not interfere to each other.
    Sanity checking tools provided.
  We will collaborate with developers of existing simulators, i.e. EicRoot, Eic-Smear, ESCalate and Fun4All.
We avoid unnecessary wrappers and external dependencies. We use native Geant4 functionalities as much as possible.
  Initially we try to cope with external dependencies inheriting from existing simulators by encapsulating them into a region.

## Slide 4: Initial work plan (2)
The simulation application will be built on top of the newly coming Geant4 version 11.
  Tasking (both PTL and TBB) mechanism is introduced.
    Enabling heterogeneous hardware configuration
  Current Geant4 v10.7 is an alpha version of Geant4 v11. Beta release of version 11 is scheduled in June.
Data exchange format / tool for geometry, event data, detector parameters, etc.
  We won’t invent a new wheel. We will join the discussion of EIC SW.
Concerning about physics models, we will start with a common EIC physics list with options for
  Deferent physics parameters per region
  Fast simulation / event biasing per region
Very first thing to do.
  Could someone please find a good project name / acronym?
  FAFSIG4LSDSWAPnPMA is just awful.