## Slide 1: Electron-Ion Collider : roman pots readout ASIC analogue front-end proposal
Maxime Morenas – March 2021
PhD student at OMEGA microelectronics group

## Slide 2: AC-Coupled LGAD modelisation
From Nicolo Cartiglia

## Slide 3: Charge injection modelisation
Case A :
Charge deposited closest to the pad
Fastest and largest signal :
Size the upper limit of the bandwidth and input voltage before saturation
Case B :
Charge deposited furthest from the pads
Slowest and smallest signal :
Size the lower limit of the bandwidth and the minimum charge detected
500 ps
700 ps
Injected (19 fC)
Received
Current spread in time
Current amplitude received divided by a factor 5

## Slide 4: Overall architecture
Choice criteria :
  Pixel area
  Power consumption
  Linearity versus input charge
  Signal drift time at the output of the preamplifier
Today : only detector+PA+discri simulated

## Slide 5: ASIC prototype specifications
ASIC requirements | 
Pixel size | 500 µm
Number of channels | 1024
Typical charge | 19 fC (120 ke- rms)
Minimum threshold | < 2 fC
Noise | < 0,4 fC
Dynamic range | 100 fC
Channel jitter at 19 fC | < 20 ps
Power per channel | < 3 mW
TDC LSB | 20 ps (TOA)
TDC range | 2,5 ns (TOA)
Hit rate | 15 hits/pixel/second
Clock frequency | 45 MHz
TID and neutron fluence | None

## Slide 6: Preamplifier : a voltage preamplifier architecture
Tunable :
  Id2 current :
  Set the DC output voltage,
  thus the dynamic range before saturation
  Set the current drawn by the preamplifier and the final jitter
  Feedback resistance (R2) :
  Set the DC input bias
  Set the open-loop gain :
  Thus set the preamplifier input impedance :

## Slide 7: Simulation results : with LGAD signal with neighbours
Preamplifier output
Return to baseline in more than 15 ns :
Preferable to integrate the charge with a shaper instead of using long range TDC
100 fC (max)
19 fC (MIP)
Rise time :
~700 ps

## Slide 8: Simulation results : with LGAD signal with neighbours
Preamplifier linearity
160 mV at 19 fC
TOA [ns]
1,6 ns at 19 fC
RMS noise = 1,5 mV
→ Minimum threshold at 2 fC (7,5 mV)
Jitter [ps]
7 ps at 19 fC
TOT [ns]
8,6 ns at 19 fC

## Slide 9: Conclusion
Power consumption and small charge detection are antagonists
Going beyond 2 fC is a challenge !
Long time constant makes shapers preferable
Further design tuning requires updated typical and pessimistic detector characteristics
Integration over 20 ns after TOA
Preamplifier ouput voltage