TPOT* proposal for sPHENIX
A Micromegas detector to reconstruct space
charge distortions in the SPHENIX TPC
 Hugo Pereira Da Costa
CEA Saclay/LANL
on behalf of the sPHENIX TPOT team
NPP PAC meeting - June 22, 2021
(*) TPOT: TPc Outer Tracker

---
Context
sPHENIX will take data for 3 years (2023-2025) and is committed to deliver its physics output well before EIC startup, before resources get redirected.
Requires robust, efficient and redundant calibration of the detectors
Especially true for the sPHENIX TPC
Main tracking device of sPHENIX, critical to sPHENIX HF and jet programs
The TPC is operated in continuous readout mode
No gating grid to stop the ions coming from the avalanche in the readout detectors
Sustains up to 50kHz Au-Au collision rate,
up to 3MHz pp collision rate
2.1 m
1.6 m
Inner field cage
Outer field cage
Central cathode
Readout detectors

---
Distortions in the TPC
In an ideal TPC, primary electrons drift longitudinally at constant velocity v
Sources of distortions to the ideal case:
static distortions due to E,B field inhomogeneities, alignment etc.
Length scale: O(1cm)
Measured during commissioning, without beam, once per year
beam-induced distortions due to charges from primary ionization and IBF in drift volume, that create an additional position and time-dependent E field
Length scale: O(1mm)
Vary with luminosity and beam conditions, on time scale ~ 1/2h
event-by-event fluctuations of the beam-induced distortions due to multiplicity/centrality fluctuations
Length scale: < 100μm
Time scale: O(10ms)
To meet its Ultimate Performance Parameters, sPHENIX must measure and correct these distortions to < 100 μm accuracy
1.6 m
2.1 m

---
Means of reconstructing the distortions in the TPC
directed lasers to reconstruct static O(cm) distortions during commissioning
tracks to reconstruct beam-induced, O(mm) space-charge distortions
diffuse laser (and digital currents) to monitor event-by-event (<100μm) fluctuations
need all methods, cooperatively, to fully address distortions in the TPC to the required 100μm accuracy level
TPOT proposal relevant to using tracks for reconstructing beam-induced distortions
Direct laser trajectories
Track extrapolation to the TPC
Central membrane metallic pads

---
Reconstructing the distortions in the TPC using tracks
Adapted from EPJ. Web Conf. 245 (2020) 01003
Not to scale !
ALICE
sPHENIX
baseline
sPHENIX
+ TPOT
ALICE:	ITS, TRD and TOF
sPHENIX baseline:	MVTX and INTT
Available detectors
TPOT is meant to provide an additional space point on the outside of the TPC, playing a similar role as TRD and TOF for ALICE
Principle
Extrapolate tracks from detectors outside of the TPC
Measure residuals between TPC clusters and tracks along ΔΦ and ΔZ in small TPC volume elements
Compute distortions along ΔΦ, Δz and Δr from measured residuals

---
TPOT detector proposal
26 Micromegas modules, consisting of two detectors
(z and ϕ layers) to provide one space point (2 x 1D measurements)
detector technology: Bulk, resistive Micromegas built at CEA Saclay
dimension: 50x25cm (active area)
front-end: SAMPA (same as sPHENIX TPC, also used in ALICE)
anticipated spatial resolutions: 200μm (ϕ), 300μm (z)
Micromegas module
Covers key sections of the TPC acceptance:
one module for each sector of the TPC on each side, due to sector-to-sector variations of IBF
one sector of the TPC equipped with 4 modules to fully measure the z dependence of the distortions
Remaining fraction of the acceptance covered by means of interpolation over short distances (see backups)
Module layout

---
Impact
1) TPOT allows to make the maximum use of tracks to reconstruct space charge distortions, by improving track extrapolation accuracy in the TPC. This
reduces the weight on the other methods
enables faster space charge reconstruction
2) TPOT provides a direct measurement of full z dependence of the distortions, in limited azimuth. This provides
redundancy
cross-check of other methods
systematic uncertainties assessment
3) TPOT ensures that sPHENIX will make the most out of collected data. In particular it was verified that TPOT allows to calibrate the TPC even with distortions 2x larger than expected
TPOT configuration
2)
1)
Single-track extrapolation accuracy to the TPC

---
Impact on track-based space charge distortion correction
Without TPOT, track-based corrections alone are not enough to recover the Upsilon inv. mass resolution
With TPOT, one can recover the nominal inv. mass resolution, without relying on the other methods
(lasers, digital currents)
Same conclusion applies to charged particle momentum resolution, critical for sPHENIX HF and Jet program
Shown performance are robust to distortions x2 larger than expected
σ = 72 MeV/c2
Nominal Upsilon invariant mass distribution in (ideal) simulations
σ = 180 MeV/c2
Upsilon invariant mass distribution, with time-averaged space charge distortions and track-based correction (INTT+MVTX)
σ = 180 MeV/c2
Upsilon invariant mass distribution, with time-averaged space charge distortions and track-based correction (INTT+MVTX+TPOT)
σ = 75 MeV/c2

---
Organizational chart (WIP) and participating institutions
Institutions:
CEA:	Micromegas detector, HV boards, FEE transition boards
LANL:	mechanical integration, LV, HV, grounding, gas
MIT:	mechanical support
SBU:	FEE, DAQ integration
BNL:	bit of everything but mostly consultative

---
More on TPOT pre-studies
Total cost estimated to $2-$2.5M (including burden and contingency)
Prototyping phase is ongoing, thanks to $40k contract between BNL and CEA Saclay.
First prototypes available this summer
Detailed construction + installation schedule is WIP
To cope with very short deadline, staged installation is anticipated with
4 to 8 detectors (out of 26) installed for Run1 (2023) data taking
remaining detectors installed for Run2 and Run3 (2024-2025)
Prototype PCB, transition board, HV board
3D printed frame
Dimension: 542x316x15.6 mm
Active area: 518x262 mm
8 MEC8 connector per layer
1HV card (5Ch) not shown

---
Summary
TPOT would represent a critical asset, in addition to existing solutions in sPHENIX, to calibrate the TPC:
It allows to make the maximum use of tracks to reconstruct space charge distortions, reducing the weight on the other methods
As an illustration it allows to fully recover the Upsilon invariant mass resolution from time-averaged space charge distortions, without resorting to other methods (laser systems, digital currents)
It provides a direct measurement of full z dependence of the distortions, critical for redundancy, cross-check of other methods, systematic assessment
It is robust to distortions x2 larger than expected
It reduces risk and speeds the deployment of precise distortion corrections, ultimately ensuring timely delivery of sPHENIX science potential
Thank you !

---
Backup

---
Distortions in the TPC
Static distortions due to E and B fields inhomogeneities and misalignment
Are present also without beam
Measured during commissioning
Length scale: O(1cm)
Time scale: 1y data taking
Beam-induced distortions due to ions
(primary << IBF)
Time-average varies slowly with beam intensity/conditions
Length scale: O(1mm)
Time scale: 1/2h
Event-by-event, due to particle multiplicity fluctuations
Length scale: < 100μm
Time scale: O(10ms)

---
Micromegas detector
Detector technology: 1D bulk, resistive Micromegas
The resistive layer quenches discharges (sparks) by reducing amplification field when large current is induced on resistive strip
Signal induced on measurement strips via capacitive coupling
One module consists of 2x1D bulk micromegas detectors, back-to-back
pillar
3mm
-1000V

---
Timeline
Jul. 2019:	First quantitative discussions with sPHENIX about an Outer Tracker detector
late 2019-early 2020:	first concrete Micromegas proposal to sPHENIX Institutional Board / creation of a taskforce dedicated to optimize detector design and sPHENIX integration
Nov. 2020:	writing of a preliminary “management plan” (project description, deliverable, schedule, cost breakdown)
Dec. 2020:	internal review of the detector proposal with sPHENIX
Feb. 2021:	setup first contract BNL-IRFU/DEDIP for building prototypes

---
Reconstructing distortions using tracks
Find tracks using all detectors and large search windows
Fit tracks using the detectors outside of the TPC
Form residuals (cluster - track) in the TPC along Φ and z
In each volume element ( > 40000), derive distortions along Φ, r and z from ΔΦ and Δz residuals
Remarks:
TPC only measures Φ and z, at a given r. For δr distortions, use correlation between ΔΦ (Δz) and track angle in the (r,Φ) (resp. (r,z)) plane
Due to large number of volume elements, prefer analytic solution to fit, for getting distortions from residuals
Same method applicable to line lasers, with the laser, instead of tracking to provide reference track

---
Reconstructing distortions using tracks (cont.)
For each volume element, form χ2 from linear relation between residuals and track angles, weighted by relevant uncertainties:
𝑟 Δ 𝜙 = 𝑟 𝛿𝜙 + 𝛿 𝑟 . tan α
Δ 𝑧 = 𝛿 𝑧 + 𝛿 𝑟 . tan 𝛽
{𝜒} ^ {2} = sum {{{left [𝑟 Δ 𝜙 − left (𝑟 𝛿𝜙 + 𝛿 𝑟 . tan α right ) right ]} ^ {2}} over {{𝜎} rsub {𝑟 𝜙} rsup {2}} + {{left [Δ 𝑧 − left (𝛿 𝑧 + 𝛿 𝑟 . tan 𝛽 right ) right ]} ^ {2}} over {{𝜎} rsub {𝑧} rsup {2}}}
With:
ΔΦ and Δz residuals in the TPC (measured)
α, β local track angles in (Φ,r) and (z,r) planes (measured)
δΦ, δr and δz the distortions (unknown)
To minimize, set the partial derivatives on the three unknown quantities δΦ, δr and δz to zero.
Since χ2 is quadratic in δΦ, δr and δz, this results in three linear equations:
left (matrix {sum {{1} over {{𝜎} rsub {𝑟 𝜙} rsup {2}}} # 0 # sum {{tan α} over {{𝜎} rsub {𝑟 𝜙} rsup {2}}} ## 0 # sum {{1} over {{𝜎} rsub {𝑧} rsup {2}}} # sum {{tan 𝛽} over {{𝜎} rsub {𝑧} rsup {2}}} ## sum {{tan α} over {{𝜎} rsub {𝑟 𝜙} rsup {2}}} # sum {{tan 𝛽} over {{𝜎} rsub {𝑧} rsup {2}}} # sum {{{tan} ^ {2} α} over {{𝜎} rsub {𝑟 𝜙} rsup {2}}} + {{tan} ^ {2} 𝛽} over {{𝜎} rsub {𝑧} rsup {2}}} right ) . left (matrix {𝑟 𝛿𝜙 ## 𝛿 𝑧 ## 𝛿 𝑟} right ) = left (matrix {sum {{𝑟 Δ 𝜙} over {{𝜎} rsub {𝑟 𝜙} rsup {2}}} ## sum {{Δ 𝑧} over {{𝜎} rsub {𝑧} rsup {2}}} ## sum {{𝑟 Δ 𝜙 . tan α} over {{𝜎} rsub {𝑟 𝜙} rsup {2}} + {Δ 𝑧 . tan 𝛽} over {{𝜎} rsub {𝑧} rsup {2}}}} right )
Minimization results in inverting a 3x3 matrix for each volume element

---
Extrapolation to full acceptance
1. small z interpolation between MM modules
2. copy z dependence in fully equipped sector to other sectors, normalized by local measurement
3. interpolate between sectors to cover
full acceptance
Input from diffuse laser on central membrane can also be used at steps 2 and 3 to improve normalization accuracy

---
Impact of staged installation
Year-1 setup (2023)
Full setup, corresponding to performances described above
4 to 8 detectors installed depending on schedule, resources and funding profile
Extrapolation procedure to other Φ sectors will need to rely on diffuse-laser + central membrane data
No anticipated loss of momentum and inv. mass resolution but:
no/little redundancy for checking the extrapolation procedure
no/little redundancy for checking the z-dependent extrapolated corrections
Negative impact of staged installation mitigated by the fact that Year-1 data is dedicated mostly to commissioning and low-luminosity. Year-2 (reference and CNM) and year-3 will deliver the core of sPHENIX physics.
year-2 and 3 setup (2024-2025)

---
Ability to reconstruct space charge distortions
Using nominal beam-induced distortions
Black: input distortions
Red: reconstructed
Remaining difference in |Δr| < 200um, being investigated (likely tracking artifacts)

---
Ability to reconstruct space charge distortions (cont.)
Using beam-induced distortions with x2 scale factor
Black: input distortions
Red: reconstructed
Remaining difference in |Δr| < 200um, being investigated (likely tracking artifacts)