## Slide 1
E.C. Aschenauer
Results from the STAR Cold QCD program and readiness of the Forward upgrades
BNL NPP 2021 PAC Meeting

## Slide 2: The Pillars of the STAR Cold QCD Program
longitudinal
polarized pp
transverse
polarized pp, pA
unpolarized
pp, pA
Helicity PDFs
TMD PDFs
& FF
(n)PDFs
& (n)FF
data taking finished ≤ 2015
upcoming 2022 & 2024
upcoming 2022 & 2024
DG
Dq
Lg,q

## Slide 3: The Uniqueness of STAR
large rapidity coverage -1 < h < 4  high to low x
  lowest x at forward rapidity at 500 GeV
  highest x at forward rapidity at 200 GeV
PID – dE/dx & ToF  quark flavor separation
large acceptance  enables observables with complicated structures, i.e. di-jets

## Slide 4: W+/- and Z0 Cross section
Run11-13, PRD 103, 012001(2021)
Unpolarized sea quark ratio :
STAR kinematics at the mid-rapidity (|| < 1) is sensitive to the region 0.1 < x < 0.3 at
extremely clean observable theoretical and experimental
All Data: 2011 - 2017
Z0 cross section can constrain unpolarized TMD PDFs

## Slide 5: Probing Non-linear Effects in QCD
Forward rapidities at STAR provide an absolutely
unique opportunity to have very high gluon densities
 proton – Au collisions
combined with an unambiguous observable
p
p
p
A
counting experiment of Di-jets in pp and pA
Saturation: Disappearance of backward jet in pA
A dependence: at low pT more suppression in pAu than pAl in comparison to the pp
x dependence: at high pT range (large x) no suppression in pA

## Slide 6: Helicity PDFs: Dqs and DG
Golden probes for Dg:
Double spin asymmetry ALL for jets, di-jets and p0
Remember: to increase x-range covered:
go to higher √s (200 GeV  500 GeV)
or
go to higher rapidity: -1<h<1  -1 <h<1.8 (-1 <h<4 with fSTAR)
or both
Di-jets: constrain the shape of the Dg(x,Q2)
 4 papers in the last years  all but < 5 papers published
Golden probe for light sea quarks : W+/- production
Remember:
Ws naturally separate quark flavors
rapidity: sea vs. valence quarks
Ws are maximally parity violating
Ws couple only to one parton helicity
 all results published
Phys. Rev. D 99, 051102(R)

## Slide 7: Helicity PDFs: DG
STAR, PRD 103 (2021) L091103
Newly published results:
Largest 200 GeV longitudinally polarized pp dataset (2015); improved both statistical and systematic uncertainties
This result will reduce the uncertainty of gluon polarization for xT > 0.05 if included in global fits
STAR, PRD 103 (2021) L091103
Two different η topology bins
Di-jets: Much narrower ranges of initial state partonic momentum fraction tested; different topologies enhance sensitivity of the data to selected x;

## Slide 8: Helicity PDFs: DG
STAR, PRD 100 (2019) 052005
Measurement of jet and di-jet ALL at 510 GeV with 2012 data:
Higher √s pushes sensitivity to lower x (down to 0.02)
Consistent results from both energies
Run 2013 ALL publication in preparation
Four different η topology bins
STAR has concluded the collection of longitudinally polarized data

## Slide 9: Transverse Momentum Dependent PDFs and FF
RHIC unique kinematics: from low to high x at high Q2  TMD evolution
high precision data to test factorization and universality of TMDs
pp   DIS@EIC
Before STAR TMDs came only from fixed target ep data  high x @ low Q2
need to establish concept at high Q2 and wide range in x
Collins effect:
Correlation between the polarization of a scattered quark and the momentum of a hadron fragment transverse to the scattered quark direction:
Sivers effect:
In a transversely polarized proton, the constituent parton has a flavor dependent intrinsic transverse momentum.
Non-universality:
SiversDIS = -- (SiversDY or SiversW,Z0)

## Slide 10: 2017: AN for W+/- and Z0
Improved uncertainties from run 2017 preliminary results
Bury, Prokudin, and Vladimirov PRL 126, 112002 (2021) – extraction includes SIDIS, DY and 2011 STAR data with N3LO and NNLO accuracy of the TMD evolution assuming sign-change
2x more statistics from run 2022 at 510 GeV with STAR iTPC (expec. ~350 pb -1)

## Slide 11: Collins asymmetry for in jets
Collins asymmetries of measured with extremely high precision
Strong constrain theoretical calculations of transversity and Collins FF
STAR, DIS2021 and PRL 115 (2015) 242501
Di-hadron correlation measurements:
“interference FF” (collinear framework)
Correlation of transverse spin of fragmenting quark and momentum cross-product of di-hadron pair
 strong constrain on IFF and transversity

## Slide 12: TMDs at forward rapidities 2.7 < h < 4
incl. EM jets AN
π0 in EM jets AUT
π0 AN
STAR, PRD 103 (2021) 92009
STAR, PRD 103 (2021) 92009
STAR, PRD 103 (2021) 92009
Weak dependence on the center-of-mass energy
Measured small AN Collins asymmetry for π0 within EM jets
  small contribution from Collins to p0 AN
AN for non-isolated π0 and higher-multiplicity EM jets lower
  additional mechanism needed to explain asymmetries  diffractive subprocesses?
STAR forward upgrade capabilities with jets and charged hadrons
Study forward Sivers, Collins and Diffractive processes:
→ charged-hadron enhanced jets (prediction from Twist-3 formalism), hadron in jet
Collins asymmetry, diffractive processes with rapidity gaps
Impact of forward EM jets AN on u and d Sivers function

## Slide 13: Nuclear Dependence of AN
STAR, PRD103 (2021) 072005
TSSA for forward in pp, pAl and pAu collisions using 2015 data
Ratios of average AN as a function of logA in xF bins
Suppression of AN in pA to AN in pp collisions is observed  nuclear dependence of TMDs?
Type1: correlated uncertainties in the ratio; Type2: without correlated uncertainties

## Slide 14: The STAR Forward Upgrade
HCal
ECal
sTGC
Silicon
Observables:
inclusive and di-jets
hadrons in jets
Lambda’s
correlations mid-forward & forward-forward rapidity
Requirements from Physics:
good e/h separation
hadrons, photon, p0 identification
Detector | pp and pA | AA
ECal | ~10%/√E | ~20%/√E
HCal | ~50%/√E+10% | ---
Tracking | charge separation photon suppression | 0.2<pT<2 GeV/c with 20-30% 1/pT
STAR forward upgrade: 2.5 < h < 4
faces blue RHIC beam
rapidity coverage the same as
EIC hadron Arm
Combines:
Electromagnetic and Hadronic Calorimetry
with SiPM readout & new ADC + trigger modules
with Tracking
Silicon detectors and
small-strip Thin Gap Chambers (sTGC)

## Slide 15: High Level Schedule – Slide from PAC-2020
September
14th , 2020
January
25st , 2021
July
12th, 2021
(9th Aug)
November (Dec.)
15th , 2021
24 (28)Weeks
BES-II
4.5 Month
Shutdown
18 weeks
Shutdown
ECal already installed
Installation of:
ECal SiPMS & FEEs
HCal
HCal SiPMS & FEES
All DAQ & Trigger electronics
 ECal and HCal ready for data taking
Full System check of Silicon
  Cooling system
  DAQ
  one Si prototype module
Si support structure test installation
sTGC gas system installation &
commissioning
Till today all work done according to plan
Work during Run-21:
Commissioning of
Calorimeter system
Full System check of sTGC
with beam
  one sTGC prototype module
  VMM electronics prototype
  Gas system
  DAQ
Installation of:
Si - tracker
sTGC-tracker & Readout (maybe
partially installed earlier during run)

## Slide 16: fSTAR: Forward Calorimeter System
Forward Calorimeter System (FCS)
ECal – 1496 channels ~ 8 tons
HCal – 520 channels ~ 30 tons.
SiPM Readout Bias ~ 67V
New digitizers + Trigger FPGA = DEP boards
Members of UC EIC Consortia
Assembling FCS in Autumn 2020 at BNL
Large group of STAR collaborators actively engaged in all aspects of the project: ACU, BNL, UCLA, UCR, Indiana University CEEM, UKU, OSU, Rutgers U., Temple U., Texas A&M U., Valparaiso U.
Could engaged students despite COVID  nobody was infected

## Slide 17: https://www.bnl.gov/newsroom/news.php?a=217681
FCS Construction and Initial Commissioning Completed.
Intensive help from CAD Tech’s
 Big Thank you

## Slide 18
FCS is ready for data taking
On-line machinery in place
Monitoring systems checked
Slow controls integrated in STAR SC system
Off-line and MC machinery in place
Trigger commissioned
Grad students well engaged and analyzing OO data
From jEVP @ STAR physics run (AuAu 7.7GeV)
FCS Readout and Commissioning, Run 21

## Slide 19: fSTAR: Silicon Tracker – Status
Detector Module Assembly
  40 fully assembled and tested (36 needed for installation)
  2 sensor currents higher than normal, 1 missing an APV in readout
  Not usable: 4 sensor current issue, 2 readout issue, 1 cooling tube issue
DAQ System
  Status of the crates and readout electronics boards verified in September 2019
  Expect to have 40+ inner signal cables made by end June
Cooling System
  Cooling unit is running with <1% per day leakage
  Significantly increased leakage rate after connecting soft cooling tubes and modules -> Solved by switching to a different kind of soft tube used at PHENIX
Integration
  Support structure assembled in the clean room
  Installation tool checked and adjusted for the measured TPC cone dimensions
  Risk in connecting soft cooling tubes -> risk reduced with the new type of soft tube
Slow Control
  EPICS IOC and GUI for the DAQ system are ready
  EPICS IOC and GUI for cooling system ready
Online and Offline Software
  Online monitoring plots - first version ready this week
  Online zero-suppression and common mode noise subtraction to be implemented
  Offline software under development
STAR Collaborators:
UIC, SDU, IU, BNL, NCKU

## Slide 20: fSTAR: Silicon Tracker – Plan
6/14-6/20: mount the first 6 modules, connect cables and cooling tubes, verify status
6/21-7/18: mount the rest 30 modules, connect cables and cooling tubes, verify status
Survey: procedure and requirements to be documented, exact time to be determined
7/30-8/27: installation and commissioning

## Slide 21: fSTAR: sTGC Module Status
Leakage current << 500nA and stable
Efficiency >97%
The last module has been produced on June 8th 2021.
All module production has been completed. Performance tests are continuing.
All modules will be at BNL mid of July
STAR Collaborators:
SDU, USTC, BNL

## Slide 22: fSTAR: sTGC Readout Electronics Status
VMM chip arrived at USTC on May 31st.
150 perfect VMM chips has been chosen for the 1st batch FEB soldering.
The schedule of electronics production will be kept based on the current VMM quality (70-75% perfect).
All FEB and ROD boards has been produced.
All RODs have been shipped to BNL.
 | Finish Time
VMM3a arrival at USTC | May 29th
VMM3a test and selection | June 14th :150 VMMs for 1st Batch June 24th : 400 VMMs for 2nd Batch
FEB board production | Completed
FEB soldering and preliminary test | June 25th : 35 FEBs for 1st Batch July 10th : FEBs for 2nd Batch
FEB functionality and performance test | Middle July: good FEBs in 1st batch can be prepared. August: All the FEBs completed.
Electronics in testing
VMM chips arrived at USTC

## Slide 23: fSTAR: sTGC Gas System
Gas distribution panel
Front of controls cabinet
Use Pentane + CO2 gas mix
Gas system completed, tested and safety refuse successfully complete
Gas system and interlock functionality operated using
60 x 60 prototype installed at west platform for Run21
 fully ready to be connected to sTGC and being operated in 2022
Gas cabinet

## Slide 24: fSTAR: DAQ – Slowcontrol Status
FCS readout completed and commissioned in the FY21 physics run
  electronics frontend cards (FEE) working and integrated into STAR Slow Controls
  digitizers (DEP/ADC) working
  trigger processors (DEP/IO) and fast trigger pathways with integration to STAR Trigger commissioned
  DAQ PCs with optical Receiver Boards all tested and integrated into STAR DAQ
STGC readout mostly complete
  frontend cards {FEB) with VMM ASICs have all been built and assembled apart from VMMs
    VMM assembly onto the FEBs in progress
  readout boards {ROD) completed and at BNL
  DAQ PCs with optical Receiver Boards commissioned and integrated into STAR DAQ
  system test with 1 FEB & 1 ROD connected to the STGC 60x60 prototype completed with real physics tracks in the FY21 OO200 RHIC run
FST readout is based on the older STAR IST readout
  system already re-tested and re-integrated into STAR DAQ
Slowcontrol complete and data monitoring close to be finalized

## Slide 25: Conclusion
High Impact Cold QCD program
longitudinal polarized data taking concluded and remaining papers close to finished
Many new impactful results from transverse polarized data taking
  first impact on TMD extraction has become available -- much more to come
Clear observation of di-hadron suppression with A
   non-linear QCD effects
results lay the foundation for the fSTAR physics program and test of factorization and universality with the EIC data
STAR forward upgrade will be fully ready for data taking for Run-22

## Slide 27: Workforce
Several people plan sabbaticals, if COVID-19 situation allows:
Don Isenhower Oct 2020 – April 2021
Carl Gagliardi: 2021 and others
Installation supported
by CAD

## Slide 28: STAR Forward Silicon Tracker - Overview
Three disks, 36(+12) modules
  Flexible hybrid (SDU/IU)
  Mechanical structure (NCKU)
  Silicon sensors (UIC/BNL)
  APV25 frontend chips (UIC)
  Assembly (UIC/FNAL-SiDet)
Integration (BNL)
  Mechanical supporting structure
  Installation tooling
Cooling system (BNL/NCKU)
  Cooling lines
  Cooling manifold
  Rack (cooler, pumps)
DAQ system (BNL/SDU/IU)
  Inner signal cables and T-boards
  Outer signal cables, patch panel boards, readout modules, readout controllers, crates
Blue: existing Red: new

## Slide 29: STAR Forward Silicon Tracker – Milestones
Detector Module Prototype
  Silicon sensor: 06/30/2019 -> 08/23/2019
  Flexible hybrid: 05/31/2019 -> 12/26/2019
  Inner signal cable: 01/31/2020 -> 02/05/2020
  Mechanical structure: 04/30/2019 -> 06/19/2020
  Detector module assembly: 09/31/2019 -> 07/27/2020
  Detector module testing: 12/31/2019 -> 08/15/2020
Detector Module Production
  Flexible hybrid: 03/31/2020 -> 09/21/2020 -> 10/21/2021
  Mechanical structure: 05/31/2020 -> 01/15/2021 -> 03/23/2021
  Silicon sensors: 07/31/2020 -> 02/15/2021 -> 02/08/2021
  Detector module assembly (complete): 02/28/2021 -> 06/30/2021 -> 06/09/2021
Supporting Structure and Cooling System
  Design and Fabrication 09/31/2020 -> 11/30/2020 -> 02/08/2021
DAQ System
  T-boards and inner signal cables: 12/01/2020 -> 06/30/2021
Installation
  Installed onto supporting structure: 04/30/2021 -> 07/31/2021 -> 07/18/2021
  Installed into STAR: 07/15/2021 -> 08/20/2021 -> 08/20/2021
Nov 2018
Aug 2020
June 2021

## Slide 30: Integration Plan
6/14-6/15:
  practice mounting dummy modules and problematic modules, develop the procedure
  verify status of the DAQ and cooling system, and slow control
  obtain all the pieces needed for module mounting and testing
6/16-6/18
  install 6 production modules
  identify good cables, patch panel boards
  run the cooling and DAQ over the weekend
6/21-6/25
  install 12 production modules
  identify good cables, patch panel boards
  run the cooling and DAQ over the weekend
6/28-7/2
  install 12 production modules
  identify good cables, patch panel boards
  run the cooling and DAQ over the weekend
7/5-7/9
  install 6 production modules
  identify good cables, patch panel boards
  run the cooling and DAQ over the weekend
7/12-7/16
  verify the status of all the modules, prepare for installation

## Slide 31: Organizational Structure STAR Forward Upgrade
Dedicated manpower with large expertise for each subsystem
sTGC
Silicon
ECal
HCal
DAQ/Readout
Software
Integration
Calibration
Slow Controls
and the STAR collaboration, which stands enthusiastically behind the upgrade

## Slide 33: Scope: ECal & HCal
Location: 7 m from the IP on the “FMS platform”
Readout: SiPMs
Used in Trigger
Split in 2 movable halves inside and outside of ring
Slightly projective
ECal:
reuse PHENIX PbSC calorimeter with new readout on front face  1496 channels
  Secured one Sector (2592 towers) PbSc towers: 5.52 x 5.52 x 33 cm3 (18 X0)
66 sampling cells with 1.5 mm Pb,
4 mm SC & Wavelength shifting fibers
HCal:
Fe/Sc (20mm/3 mm) sandwich.
520 readout channels
Lateral tower size 10 x 10 cm2, ~ 4.5 l
  in close collaboration with EIC R&D
Preshower
Use EPD  need to built splitter for the signals
Installation of entire system (HCal + ECal + Electronics) finalized by Feb 2021
~9 month to commission systems before Run-22 500 GeV pp

## Slide 34: Scope: Silicon & sTGC
4 sTGC disks: at 307, 325, 343 and 361 cm from IP
location inside Magnet pole tip opening
  inhomogeneous magnetic field
4 quadrants double sided sTGC  1 layer
  diagonal strips to break ambiguities in the sTGC
Position resolution: ~200 mm
Material budget: ~0.5% per layer,
Readout: based on VMM-chips
 following ATLAS design
3 Silicon disks: at 146, 160, and 173 cm from IP
Built on successful experience with STAR IST
Single-sided double-metal mini-strip sensors
  Granularity: fine in f and coarse in R
  Si from Hamamatsu
Frontend chips: APV25-S1  IST all in hand
Material budget: ~1.5% per disk
Reuse
  IST DAQ system for FTS
  IST cooling system
Si
sTGC
Installation of entire Si and sTGC finalized by Mid of September 2021
~2-4 month to commission systems before Run-22 500 GeV pp

## Slide 35: Importance of STAR forward upgrade for EIC
STAR forward upgrade: 2.5 < h < 4
rapidity coverage the same as
EIC hadron Arm
 high-x EIC physics
HCal +SiPM readout same as
EIC-fHCAL
same rapidity as EIC
  background
small-strip Thin Gap Chambers (sTGC)
sTGC alternative technology to
EIC GEM Trackers
HCal
ECal
sTGC
Si
Analysis:
Learn how to reconstruct Jets close
to beam rapidity
Jet solid angle ~ R2/cosh2(h).
so for fixed jet multiplicity, dN/dΩ grows like cosh2(h)
15 times larger at h=2, 100 times larger at h=3
what are the effects of underlying event ep & eA
and √s
Training of young scientific generation:
20+ undergrads working > 2019/06
hadrons
electrons
Barrel Hadronic calorimeter not shown
HCal
ECal
Si
sTGC or GEM