## Slide 1: Finale of RHIC Beam Energy Scan II Operation
June 11, 2021
Chuyu Liu on behalf of the RHIC team

## Slide 2: Outline
Overview of Run-21
Run-21 programs
Summary

## Slide 3: Trilogy of BES-II
1st year
2nd year
3rd year
The third year of BES-II operation is the most challenging, exciting and rewarding one of the three.
Courtesy by Wolfram Fischer

## Slide 4: Major changes between BES-I and BES-II
4 bunches per AGS cycle with 2.3E9 Au ions per bunch at AGS extraction with Tandem ion source.
Implementation of third harmonic cavity to flatten bunch profile for reduced space charge, therefore high intensity in RHIC.
Stable LEReC cooling operation, improved cooling performance with long electron bunches made possible by 1.4 GHz cavity. Beta squeeze in the middle of stores.
Switching to lower tune for better ion beam lifetime therefore higher intensity, and scanning of e beam current.
Implementation of bunch-by-bunch damper ensured higher intensity operation.
Orbit corrector controller upgrade and improved measurement and control of beam properties.
Reduce lattice nonlinearity due to persistent current and stabilize the magnetic field with wiggle ramp (demagnetization cycle).
Employment of three 9 MHz cavities per ring.
injection kicker reconfiguration for short rise time and longer flattop.

## Slide 5: Run-21 programs and schedule

## Slide 6: Run-21 timeline
Au+Au CoM 7.7GeV
FXT
O+O CoM 200 GeV
Au+Au
CoM 17.3 GeV
FXT + misc + dAu?

## Slide 7: Operation of Au+Au at 7.7 GeV
The lowest energy in collision mode

## Slide 8: Non-stop performance improvement of Au+Au collision at 7.7 GeV
Switch to Low tune
E-beam current scan
Tune scan
Damper engaged
IR steering
LEReC cooling
Beta squeeze
RF voltage ramp
LEReC optimization & long bunch

## Slide 9: LEReC – world’s first electron cooler based on rf-accelerated electron bunches employing high-current electron accelerator (as such, a prototype of high-energy cooler)
COOLING
in Blue RHIC ring
COOLING
in Yellow RHIC ring
High-Power Beam Dump
Extraction beam line
DC e- Gun
704 MHz SRF
Booster Cavity
2.1 GHz Cu Cavity
9 MHz Cu Cavity
704 MHz Cu Cavity
Injection beam dump
RF Diagnostic Beamline
RHIC TRIPLET
RHIC DX
180°
Bending
Magnet
e-
e-
e-
* NOT to scale
Cathode
loading system
LF solenoid
HF solenoid
Transport solenoid
ERL solenoid
Quad corrector
Trim corrector
Corrector 3.8 ID
Corrector 6.0 ID
BPM 2.4 ID
BPM 4.8 ID
Bellows
Ion pump
Merger
Beamline
Transport
Beamline
704 MHz Cu Deflector Cavity
New 1.4 GHz RF cavity allows LEReC operation with longer electron bunches which helps to reduce “heating” effect on ions from the electrons.

## Slide 10: Cooling vs no-cooling
With cooling
W/o cooling
Beta squeeze
With cooling
W/o cooling
W/o cooling
With cooling
Bunch length
Beam size
Cooling reduces/maintains the longitudinal and transverse size of the beam therefore reduces the luminosity decay rate. In addition, it enables beam size reduction by squeezing the beta (envelope) function at IP.

## Slide 11: High tune vs low tune
High tune
Low tune
Low tune optimized
At low tune (0.12), beam lifetime is better than that at high tune (0.23) so RHIC can take more beam from the Tandem source.
Even the cooling is less efficient at low tune, higher integrated lumi was achieved.

## Slide 12: Suppressing beam instability by bunch-by-bunch damper
Bunch-by-bunch feedback system was engaged operational in 2021 to enable 10-15% more intensity.
Feedback has been on from start of injection to the start of physics data taking.
Dampers on
Dampers off

## Slide 13: Alleviating space charge effect
w 3rd harmonic
The reduction of peak current by engaging 3rd harmonic cavities improves greatly the beam lifetime.

## Slide 14: Operation of FXT, O+O, Au+Au at 17.3 GeV

## Slide 15: Fixed target operation
Fixed target at beam energy 3.85, 44.5, 70 and 100 GeV.
12 bunches with moderate intensity (1.5E9 ions per bunch) equally distributed in the yellow ring.
Vertical orbit bump to bring beam close to the target and maintain the rate.
100 GeV FXT was performed with big challenges on machine side.
  An orbit bump of ~17 mm was set up with maximum available strength on IR correctors.
  All available methods were used to blow up emittance: Injection mismatch, ARTUS kicker, IBS & coupling, BBQ kicker.
FXT setup
100 GeV Au FXT

## Slide 16: O+O at CoM 200 GeV
Oxygen is a new species for RHIC. The setup took 3 calendar days with FXT running overnight.
Store length was over 20 hours and 15 hours for the min-bias and central run.
Calibration run for a day with STAR solenoid polarity reversed.
To reduce vertex longitudinal rms to 10 cm, beam was rebucketed and crossing angle of 1.65 mrad was put in.
Transition to central run

## Slide 17: Crossing angle effects
rate
Vertex rms
Vertex mean
Implementation of horizontal crossing angle
The crossing angle was less effective than predicted to reduce the vertex rms due to non-gaussian bunch profile.
The fittings on the right plots were performed with bunch length as a variable.

## Slide 18: Au+Au at 17.3 GeV
New energy for collision mode.
Experience of low energy operation gained in the past two years gave us guidance on the optimal configuration of RHIC for this energy.
Careful evaluation of the exact energy due to its proximity to AGS transition energy.
Beam setup in AGS needed more care but went smoothly.
Goal of average rate
Achieved average rate

## Slide 19: Coherent electron Cooling experiment at RHIC in Run-21
Current CeC system has seven high field solenoids, five of which serve as a 4-cell Plasma-Cascade μ-bunching amplifier with 15 THz bandwidth and amplitude gain exceeding 100.
All necessary electron beam parameters – the beam energy and peak current, the beam emittances and energy spread, the low noise in the beam (critical and most not-trivial requirement) - had been demonstrated. The full CW beam was propagated with low losses through the newly built PCA CeC
The CeC run achieved the following last year:
  1. Demonstrating KPP for the e-beam
  2. Plasma Cascade amplification
  3. Ion imprint
The team worked on solenoid alignment, ion and electron beam alignment this year.
Parasitic fixed target data acquisition during CeC studies.
The project plans are to demonstrate longitudinal CeC in 2021 and 3D (both longitudinal and transverse) CeC in 2022.
Courtesy V.N. Litvinenko
RHIC 26.5 GeV/u ion beam
1.25 MV SRF
photo-electron gun
Ballistic
bunch compression beamline
1.5 to 10 nC per bunch
13.1 MV SRF linac
Time-resolved diagnostics beamline
CeC with 4-cell Plasma Cascade μ-bunching amplifier
Modulator
Kicker
Plasma Cascade Amplifier

## Slide 20: Accelerator Physics Experiments (APEX)
Cooling studies:
  Electron-ion heating
  Bayesian optimization
  Coherent excitation
  Dispersive cooling
  Painting cooling
  Recombination study
  Electron-ion focusing
Electron-ion collider studies:
  Radial shift test
  Fine decoupling
>120 hours

## Slide 21: Summary
The final year of BES-II was most challenging. Both LEReC and RHIC performance were greatly improved.
A few good decisions were made for the Au+Au at 7.7 GeV to make use of the full potential of the source, injector and RHIC.
Switching between multiple physics programs was again demanding.
Physics programs, CeC experiment, APEX studies and other tests coexisted in harmony.

## Slide 22: Section Break
Subtitle

## Slide 23: Print-friendly Section Break
Subtitle