## Slide 1: Updated proposal: Precise measurements of very forward particle production at RHIC -- RHICf experiment --
Yoshitaka Itow
(KMI/STEL, Nagoya University)
for the RHICf Collaboration

## Slide 2: RHICf: neutral particle measurement at zero-degree of RHIC by a dedicated small calorimeter
h>5.8
p
RHICf
Beam pipe
IP
Front counter
Existing ZDC
LHCf calorimeter
Manipulator
Neutral particles
9 cm
29 cm
LHCf detector
18m

## Slide 3: The LHCf detectors
16 tungsten + pl.scinti. layers
20mmx20mm+40mmx40mm
4 SciFi tracking layers
44X0,
1.6 lint
16 tungsten + pl.scinti. layers
25mmx25mm+32mmx32mm
4 Silicon strip tracking layers
Arm2
Arm1
Here we assume to use Arm2

## Slide 4: The RHICf Collaboration
Y.Itow, H.Menjo, T.Sako
  Nagoya University (Japan)
K.Kasahara, T.Suzuki, S.Torii
  Waseda University (Japan)
O.Adriani, L.Bonechi, R.D’Alessandro
  INFN/University of Firenze (Italy)
A.Tricomi
  INFN/University of Catania (Italy)
Y.Goto
  RIKEN/RIKEN BNL Research Center (Japan)
K.Tanida
  Seoul Natioanl University (Korea)

## Slide 5: History
2011 First discussion
2013 LOI
2014 Proposal for RUN16 with PHENIX
2015 Proposal for RUN17 with STAR

## Slide 6: Outline of the proposal (original last year => update this year)
Physics motivations:
  To understand CR air shower interaction in a wide range of √s, combining also the results at LHC
  Precise measurements of spin asymmetry of forward particles
Technical issues:
  To install position sensitive electromagnetic calorimeters in front of one of the PHENIX STAR ZDCs using one of the existing LHCf detectors after the LHC 13TeV run (2015)
Beam conditions:
  510 GeV polarized p+p collisions with β*=10m
  1 day for physics and 1 day for contingency
  1-5 days for beam setup depending on the previous mode
  => 2 days in case of switching from 510GeV p+p small β*
  Data taking in RUN16 => RUN17

## Slide 7: Motivation : cosmic ray interactions
1020
1017
1014
eV
14TeV
7
0.5
0.9
Knee
GZK
Ankle
AUGER, TA
TALE
2nd Knee?
HEAT
2.2
Cosmic rays
Colliders
Air shower
0.2
TibetAS
HAWC
Need dedicated very forward measurement at hadron colliders
So far LHCf measured pp (7, 2.76, 0.9 TeV) and p-Pb(5TeV/n)
RHIC data at the low end is important for extrapolation to 1020eV
RHIC can serve p-LI or LI-LI collisions ( LI: light ion, ex, Nitrogen).

## Slide 8
① Inelastic cross section
(TOTEM and others)
② Forward energy spectrum
( LHCf g /p0 spectrum)
⑤ 2ndary interactions
(√s dependence )
③ Inelasticity k= 1-plead/pbeam
(LHCf forward neutron, n / g ratio )
④ Nuclear effect
(shadowing, Cronin effect)
Atm. depth
#of particles
SD E-scale error
Composition error

## Slide 9: The LHC forward experiment
ATLAS
LHCf Arm#1
LHCf Arm#2
140m
Two independent detectors at either side of IP1 (Arm#1, Arm#2 )
Charged particles (+)
Beam
Charged particles (-)
Neutral
particles
Beam pipe
96mm
All charged particles are swept by dipole magnet
Neutral particles (photons and neutrons) arrive at LHCf
0 degree is covered ( 8.6 < | h | < infinity )
Carried out at LHC 0.9, 2.76, 7, and 13 TeV p+p and 5TeV p+Pb

## Slide 10: LHCf results summary
Preliminary
h> 10.76
h>10.94
7 & 0.9 TeV pp
photon
7TeV pp
neutron
7TeV pp
p0
5TeV pPb
p0
PLB 703 (2011) 128-134
Submitted PLB
PLB 715 (2012) 298-303
PRD 86 (2012) 092001
PRC 89 (2014) 065209

## Slide 11: LHCf 13 TeV run (Jun 2015)
Completed data taking last Saturday.
Detectors removed this Monday.

## Slide 12: Why RHIC ?
ZDC closer to IP, same PT acceptance as LHC
  RHIC ZDC @ z=18m @500GeVpp,
  LHC ZDC @ z=140m @ 7, 13 TeVpp
Rich experience and opportunity for p-A, A-A
  Understanding nuclear effect in air shower
Polarized proton collisions
  Precise spin asymmetry for forward neutrons
  Probe for forward productions
Feynman scaling in forward region; 0.5 TeV n 7 , 13 TeV

## Slide 13: Feynman scaling : a key for extrapolation
Many models naturally include XF scaling violation
Important to extrapolate from LHC to GZK
Impact also on air shower structure； Xmax
Preliminary
7TeV scaled (h>10.94)
0.9TeV (h>8.68)
Data
LHC single gamma data
(900GeV pp / 7TeV pp)
Expected from models
(5TeV, 14TeV and 50TeV)

## Slide 14: Feynman scaling violation and air showers
T.Wibig, Phys Lett B 678 (2009) 60
a ; scaling violation parameter
Air shower max for UHECR data

## Slide 15: Feynman scaling in p0 production
LHCf π0 spectra at √s= 2.76 and 7 TeV (preliminary)
RHICf can add data at √s=510GeV, pT<1GeV/c
preliminary
preliminary

## Slide 16: LHCf average PT of p0
preliminary
RHICf

## Slide 17: Spin asymmetry of forward neutron
Combination of ZDC (good Ehad resolution) and RHICf detector (good position resolution) provide good pT resolution in neutron measurements
With horizontal polarization, covering pT<1GeV/c
Notes: 右図改訂版：12時間測定での中性子asymmetry測定。縦軸の統計精度は全て1%以内（絵にしにくいので1%くらいにしてある。楕円横幅は各Ptでの Pr精度を反映。binningは 0.1GeV/cきざみ。1GeVまで拡張可能。）

## Slide 18: Impact of “RUN16 to RUN17”
RUN16 500GeV pp with PHENIX is no more possible because of their shutdown for upgrade
  Collaboration with the central detector is important to identify diffractive events
  Important to interface to machine signals and to determine luminosity in established way
  Discussion with STAR started
Availability of LHCf Arm1 and Arm2 detectors can change (we assume Arm2 here)
  LHCf operation at LHC 13 TeV p+p collisions successfully finished and detectors were uninstalled on this Monday
  Re-scheduling impact on future LHCf is being reviewed

## Slide 19: New time line for RUN17
Visit STAR during 2015 summer shutdown to define cabling, support structure and electronics installation
Shipping a LHCf detector from CERN to BNL to be ready in 2016 shutdown

## Slide 20: Beam setup time (from “RHIC Collider Projections (FY2014-FY2018”)
Expected in RUN17
1day for β* setup, 1 day for polarization direction, 1 day for physics + contingency
=> 5 days of dedicated time needed

## Slide 21: First discussion with STAR
29-May, 2015
  Presentation of RHICf ideas at the STAR management meeting
Answer from STAR council meeting
  “supportive” to host RHICf
To be discussed
  integration plan, DAQ and common operation
  Extend physics cases integrated with STAR detector
  Authorship, collaboration policy , etc.

## Slide 22: Diffractive mass tagging with a Roman pots (joint operation with Roman pots)
Forward neutron ( PYTHIA8 13TeV pp)
zero degree
determination of ξ by RP
(ξ :fractional momentum loss)
detection by RHICf
single diffraction

## Slide 23: Summary
RHICf : neutral measurement at RHIC zero-degree by one of LHCf detectors.
  Verify cosmic ray interactions at ~1014eV
  Spin asymmetry for forward (neutral) particles
  Don’t forget nuclear-effect study in p-A
RHICf 500 GeV pp gives similar acceptance as LHC 7 TeV.
  Good verification of Feynman scaling in similar condition with the same detector.
RUN17 with STAR
  Discussion just started. Basically positive.
  Every technical and management issues should be addressed soon.

## Slide 24: Backup

## Slide 25: √s scaling : a key for extrapolation beyond the LHC
Comparison done in the very limited phase space of 900GeV collisions
(green triangle in the phase space plot)
7TeV scaled (η>10.94)
0.9TeV (η>8.68)
LHCf single photon data
(900GeV pp , 7TeV pp)
Preliminary
All π0 expected from models
(0.5TeV, 14TeV and 50TeV)
DPMJET3
QGSJET II

## Slide 26: LHCf Arm2 Detector => RHICf Detector
Arm#2 Detector
25mmx25mm+32mmx32mm
4 XY Silicon strip detectors
Imaging sampling shower calorimeters
Two calorimeter towers
Each tower has 44 r.l. of Tungsten,16 sampling scintillators and 8 (4XY pairs) silicon strip sensors
Sensitive to photons, neutrons and photons from π0

## Slide 27: Event sample (π0 g 2γ ) at LHC 7TeV p+p
Longitudinal development measured by scintillator layers
Lateral distribution measured by silicon detectors
X-view
Y-view
25mm Tower
32mm Tower
600GeV photon
420GeV photon
Hit position,
Multi-hit search.
Total Energy deposit
Energy
Shape
PID
π0 mass reconstruction from two photon.
Systematic studies

## Slide 28: RHICf coverage
Detector is moved up-down; wide pT coverage and to avoid ZDC interference
xF-pT coverage identical to LHC 7TeV collision
Wider coverage and higher resolution in pT than ZDC measurements (joint analysis between ZDC and RHICf)
Installing the LHCf Arm2 detector at RHIC
vertically movable
ZDC
IP
limited by
beam pipe
View from IP
pT (GeV/c)

## Slide 29: XF scaling of very forward neutron
A. Adare, et al., Phys. Rev. D, 88, 032006 (2013)
LHCf 7TeV neutron (Arm1 only)
0<PT<0.11xF GeV/c
RHIC PHENIX (200GeV),
ISR (30.6-62.7 GeV)
K.Kawade PhD thesis (2014)
Preliminary

## Slide 30: Detector performance
Number of event
x-pos[mm]
200 GeV electrons
sx=172 mm
Position resolution
Eg resolution
4%
For hadron, Dx~2.5 mm
100
200
E(GeV)
Ehad resolution
350GeV protons

## Slide 31
position resolution (mm)
PID (SPS energy)
EM shower (SPS)
NIM, A671 (2012) 129-136
JINST, 5, P01012, 2010
Hadronic shower (LHC MC)
JINST, 9, P03016 (2014)
energy resolution (%)
energy resolution (%)
position resolution (μm)

## Slide 32: Hadron shower reconstruction
Check by SPS 350GeV p beam

## Slide 33: LHC impact on UHECR air showers
UHECR MC (EPOS, QGSJET II) tuned by LHC data now
Shower max diff. improved ( 50 -> 20gcm2 ), c.f. 100gcm2 btw p - Fe
But yet LHCf results not fully implemented (due to its difficulty)
Another missing piece -> Nuclear modification factor
T.Pierog, S.Ostapchenko,
ISVHECRI2012
EPOS
QGSJET-II
1017
1020
0g/cm2
Xmax
Notes: ----- 会議メモ (2014/06/17 13:26) -----
LHC data
Xmaxのポンチ絵
Energyを大きく

## Slide 34: Expected Results (single photons)
Photon spectra at 4 rapidity samples
12 hours statistics (12 nb-1 effective luminosity; 360nb-1 delivered)
Statistical error is almost negligible except at the highest energy bins
6.26<η<6.49
6.87<η<7.40
7.40<η<7.83
8.27<η

## Slide 35: Expected Results (single neutrons)
Neutron spectra at 4 rapidity samples
12 hours statistics (12 nb-1 effective luminosity; 360nb-1 delivered)
RHICf resolution not considered; true spectra
Statistical error is almost negligible
6.26<η<6.49
6.87<η<7.40
7.40<η<7.83
8.27<η

## Slide 36: Expected Results (single neutrons)
Neutron spectra at 4 rapidity samples
12 hours statistics (12 nb-1 effective luminosity; 360nb-1 delivered)
RHICf resolution taken into account, but ZDC joint analysis not considered
Statistical error is almost negligible
6.26<η<6.49
6.87<η<7.40
7.40<η<7.83
8.27<η
measured energy
(resolution folded)

## Slide 37: Expected Results (π0)
π0 spectra at 4 rapidity samples
<60GeV not detectable due to large opening angle of γγ
24 min statistics (12 nb-1 effective luminosity; 12 nb-1 delivered)
Statistical error will be negligible with a reasonable run time
6.04<y<6.16
6.36<y<6.70
6.70<y<6.88
7.25<y<7.62

## Slide 38: Requested Beam Condition

## Slide 39: Scaling violation and Air shower (on going study)
QGSJET II-04 π0
Artificial scaling-violation function applied to DPMJET3 (perfect scaling model)
DPM Original
DPM modified
e+/- size
μ size
500GeV
7TeV
1TeV/500GeV
7TeV/500GeV
28TeV/500GeV
:
proton shower 1018eV