## Slide 1
TK Hemmick, R Preghenella, F Geurts for ATHENA
PID

## Slide 2: Yellow Report Detector
Strategy
  Implement Minimal Config
    mRICH Backward
    DIRC Barrel
    dRICH Forward
  Define Competing Design(s)
    Alternatives
    Additions
  Demonstrate efficacy for all technology beyond minimal
ATHENA models closely the Yellow Report Concept.
PID is challenging in Asymmetric System.
Varied Technology w/ h
ATHENA in DD4HEP

## Slide 3: PID ~ Velocity
p = mgb E = mg velocity(b) measurement yields mass.
Direct measurement:
  Record signal time at multiple locations, calculate v.
  “Fast” detector = low transit time spread (most easily achieved at small transit time)
Velocity-dependent interaction(s) with detector:
  Specific Ionization (aka )
  Cherenkov Radiation:
    qC measured wrt track direction.
    Thus dependent upon deliverables from tracking
  Bremsstrahlung:
  Transition Radiation:
eID mechanisms

## Slide 4
Hadron End: Dual RICH (dRICH)
Cherenkov radiator
○ Refractive Index
n = 1.02 (aerogel) 1.0008 (C2F6)
○ Length of the radiator
L = 4 cm (aerogel) , 160 cm (C2F6)
Mirrors
Photon Detector
3 mm pixel size; 200-500 nm MAPMT
Particle Generation
Originate from the vertex
Exquisite detail in simulation.
AI-based optimization.
Uses constant external angular resolution assumption.
Similar external constraint assumed as deduced for separate gas & aerogel RICHes
Tracking maybe tolerates ~2X sim (0.5 – 1.0 mrad)
NOTE: PMTs to the side makes optical aberration (“Emission”) dominant

## Slide 5: dRICH in ATHENA
Much work has gone into refining the optics beyond the menagerie.
“Menagerie” Implementation

## Slide 6: Current dRICH Model
Dramatic improvement of optical performance.
Present studies target the full system performance:
  Internal RICH parameters
  External Detector influence.
Cautionary Note:
Nominally RICH runs with 1 atm “heavy gas” (fluorocarbons: CF4, C2F6, C4F10, C4F8O, …)
Environmental Considerations threaten this future.
  Even if you scavenge gas, you still must buy it.
3 bar Ar foreseen as a viable substitute for C2F6
  Requires safety engineering.

## Slide 7: Magnet Optimization
Competing Optimizations:
  Homogeneity in the barrel.
  Projectivity in the End Cap
Impact dominant at:
  lowest momentum.
  Lightest mass (e-p has most impact)
Detailed simulations show non-zero but tolerable impact.

## Slide 8: hpDIRC in Barrel Region
At normal incidence, Cerenkov light is internally reflected for
Original BaBar DIRC was effectively “proximity focused”
hpDIRC section creates focused ring improving resolution.
p-K to 6 GeV/c
Strict requirements on “correlated terms”, (e.g. angular resolution of tracking)
DIRC in DD4HEP

## Slide 9
Electron Arm: Modular RICH (mRICH)
Cherenkov radiator
(Aerogel) refractive index, n = 1.03
Length of the radiator, L = 3cm
lens with focal length, 𝑓= 6”
Photon Detector
3 mm pixel size
NOTE: Similar performance to aerogel in dRICH
Hadron ID requirements relaxed…aerogel only
Additionally require eID ~ 4GeV/c
Modular RICH focused by Fresnel Lens
  Sharp image improves resolution.
  Transmission of lens combats dispersion
Provides TOF with suitable readout device (LAPPD)

## Slide 10: mRICH in Backward Region
Implemented as a pseudo-projective array:
  Detector envelope ~planar in Zed.
  Individual modules tilted toward nominal collision point.
Advanced stage of implementation in DD4HEP
Cherenkov Photons in DD4HEP
Test Beam Implementation:
LAPPD Readout
TOF for particle & Cherekov Light

## Slide 11: Beyond the Baseline Options: Low p in Barrel via GridPIX
The opportunity:
DIRC has low-p limitations:
  Curl Up (0.45 GeV/c)
  Kaon threshold (0.47 GeV/c)
Desired: PID at low radius.
First Option: dE/dx measurement
    Separations large
      1.6X pi-K
      2.25X K-p
  GridPIX is ultimate dE/dx device.
    Avalanche grid in front of 55 x 55 mm2 pixels.
    >90% efficiency for single electrons.
    Established; Robust; Excellent tracking
      Topological Decays added to physics program
  Challenge is removing the heat.
Pessimistic
Optimistic
<40oC
6% R.L.
Test Beam

## Slide 12: Beyond the Baseline Options: Low p in Barrel by TOF
Competition with Multiple factors:
Radius, Resolution, Kinematic limit
Low-p goal | TOF Radius |  | Tracking Impact?
100 MeV/c | ~22 cm | 17 psec | Yes
200 MeV/c | ~43 cm | 33 psec | No
Low-p goal | TOF Radius |  | Tracking Impact?
100 MeV/c | ~22 cm | 17 psec | Yes
200 MeV/c | ~43 cm | 33 psec | No
Maximal
Tracking
Impact
Assumes LGAD Layer(s)
~20 psec/layer

## Slide 13: EMCAL with Intrinsic TOF
The opportunity:
Imaging calorimeter dramatically improves e-p separation at low momentum.
To allay costs ATHENA proposes hybrid solution:
  Initial few layers are imaging (Astropix)
  Late shower W-power SciFi
Calorimetric considerations start with absorber.
  LGAD as the opening layer adds TOF capability at the largest radius (~20 psec)
TOF Opportunity!

## Slide 14: Aerogel-RICH layout
Single layer aerogel
L=2 cm
d ~ 20 cm
SiPM
Baseline layout:
no focusing
n=1.03 aerogel layer
Photodetector (SiPM HPK 13360 3050CS)
Hydrophobic aerogel
SiPM HPK 13360 3050CS
3x3 mm2 pixel
Dark rate ~ 50 kHz/mm2
50 ps time resolution
(p.e.) = = 7.2 mrad
1.1 mrad | 6.1 mrad | 3.7 mrad
Aergoel n=1.03, p.d. @ R=1.2 m, HPK 13360 3050CS (pixel 3x3 mm2, DCR 50 kHz/mm2, 90% fill factor)
single particle events
  uniform energy distribution
  isotropic angular distribution
  origin from (0, 0, 0)
  one particle per event: e⁻ π⁻ μ⁻ K⁻ p
  10 k events/particle
Pythia8 pp collisions
  √s = 14 TeV
  c-cbar biased processes
  100k events
Pythia8 Xe-Xe collisions
  √s = 5.76 TeV
  minimum bias
  1k events
The opportunity:
DIRC has p-K up to 6 GeV/c
Jet physics wants 10 GeV/c
Aerogel RICH can extend range

## Slide 15: Barrel RICH results in the fast parametric model
R. Preghenella

## Slide 16: SiPM for RICHes? R&D Required
The ATHENA 3T magnetic field is excellent for physics.
3T is challenging for most single photon detector technologies
SiPM can suffer radiation damage
  Limited impact to calorimeters (~pedestal shift)
  Significant impact to RICH (single photon signals!)
Is annealing helpful?
Dark Rate drops ~1 order of magnitude following annealing
  138o anneal limited by solder.
  High annealing temp in the future.
Basic Concept:
  Cooling system (e.g. fluid) doubles as heater.
First results promising.
Higher Temperature annealing to be tried in the future.

## Slide 17: More Opportunities: TRD & Endcap TOF
The opportunity:
Improved eID Backward
Vector meson  e+e- Forward
Transition Radiation Detector
The opportunity:
dRICH can miss softest particles
TOF will not miss them
LAPPD has best st~5 psec.
NOTE: Possibility in backward direction to combine TOF with mRICH

## Slide 18: Summary
ATHENA ongoing development is simulated in stages:
  Minimal configuration:
    mRICH Backward; DIRC Barrel; dRICH Forward
  Performance and Physics reach of minimal challenged by simulated options
    Low p PID in the barrel
      GridPIX; LGAD TOF
    High p PID in the barrel (beyond DIRC)
      Barrel RICH;
    Low p in the Forward Endcap
      LAPPD TOF measurement
    eID in the Endcap(s)
      TRD
Detector configuration final decision based upon realistic Monte Carlo
  Physics impact leads to down-select.
  Baseline simulations nearly ready.
  Some options in advanced stage.