## Slide 1: Low Momentum PID @ High B-field
TK Hemmick, K Dehmelt, (SBU) N Smirnov, (Yale) J Kaminski (Bonn)

## Slide 2: Low Momentum PID
dE/dx Device
GridPIX
membrane
High magnetic field curls low(er) momentum particles.
  Option #1: We don’t care about them. (bad option)
  Option #2: Lower the B-field for “special runs”. (poor option)
  Option #3: PID on these particles BEFORE they curl up.
Mostly

## Slide 3: GridPIX Overview
Ultimate dE/dx device.
  Avalanche grid in front of 55 x 55 mm2 pixels.
  >90% efficiency for single electrons (Polya NOT exponential).
  Goal:
    Enough diffusion to get every electron into a different hole.
    Count electrons one-by-one.
  Three generations of development and continuing.
Large area is VERY expensive, but this proposal is small area.
  Need:
  Careful: ~3kW of power must be removed.
Pros:
Known/Proven Technology
Active further development (Bonn)
Best possible (~count each electron)
Affordable for a small area
High resolution tracking
  Also loves outer MPGDs!
Low mass in electron arm
Continuous (aka streaming) readout
Cons:
3 kW of power.
Must find a low mass way to handle.
Services “bulky” (compared to just Si)
  Gas
  HV membrane (~10 kV)
  Cooling
  DC power lines (3kW also goes out!)
3D e-by-e tracking