## Slide 1
GASEOUS RICH VESSEL, general considerations
What has to be fixed in space in a gaseous RICH?
The Mirrors and the PDs
  No interest to have wall that cannot deform
  The acceptable level of deformation to be defined by various constrains, but deformation up to O(cm) in general tolerable
Comments:
  This is true both in a “pressurized vessel” and when working at “atmospheric pressure”
    By the way, there are two approaches to “atmospheric pressure”:
      Following the evolution of the atmospheric pressure
      Fixed at 1 bar
      In any case, the pressure in the vessel is not a value, it is a field due to the hydrostatic pressure of the heavy gas
How to obtain the fixed mirror and PD position?
2 approaches:
  A fully rigid vessel
    Thicker material with ~ uniform distribution
  A rigid structure along the vessel edges and “skins” closing the walls
    Less material with limited dead-areas corresponding to the structure elements
S. Dalla Torre, 31 May 2021

## Slide 2
GASEOUS RICH VESSEL, general considerations (cont.)
Mirror and PD fixation, critical and less critical aspects
MIRRORs (less critical)
  Supported by a very rigid and mechanical precise mirror-wall structure
    with rotation degrees of freedom for each mirror to allow for the most critical alignment: the angular alignment
    Everything (= mirrors, supports) is immersed in the gas  no force causing displacement or deformations
PDs (more critical)
  Sitting on a portion of wall; P different (internal vs external) makes this aspect very critical
  A possible approach (not the only one!):
    Reinforce the vessel wall where the photondetectors and their windows are placed
    Easier if PDs out of detectors acceptance: more material there can be tolerated
S. Dalla Torre, 31 May 2021

## Slide 3
GASEOUS RICH VESSEL, how to progress?
Experts suggest the typical material (thickness, material nature) needed in the two hypothesis for given pressure hypothesis (P = 1 bar 3 bar)
  A fully rigid vessel
  A rigid structure along the vessel edges and “skins” closing the walls
Assuming the material initial data,
simulation of the effect concerning the detector performance (within PID group)
S. Dalla Torre, 31 May 2021