## Slide 1
Estimated number of ‘MIP’ equivalents per layer:
10 GeV in shower max position ~ 5 MeV energy deposited in 3 mm thick scintillator, 5 / (0.6) ~ 10 particles,
Usually scale with energy so 1 MIP eq/GeV per layer
After coils average become 0.5 MIP eq/GeV per layer
Pattern recognition (‘showers’ separation) ??? Looks like very tough task.
Discussions on role of bHCal and configuration of bECal continues (last two meetings).
From Jarda’s MC for hadron endcap
BECal
SC 3T Magnet
BHcal
Thick SC Magnet between Ecal and Hcal. Example, Complications for calorimeters in barrel region

## Slide 2
WScFi Ecal, I int. length + 20 cm steel between ecal and hcal (Fe/Sc 20/3 mm). Example, 6 GeV pi-
Without coils 18.7%
With Coils 32.7%
At lower energies expect even more degradation (next Mon. calor meeting).
Can tails be handled with what is before coils (Ecal, or Ecal + something) is a ?
Clear that coils will have big impact on energy measurements,
But what bHcal will be used for?
Pattern recognition (neutral hadrons identification).
Questions were asked:
Inclusive, is not inclusive if veto on neutral?
Importance of knowing efficiencies?
Long Ecal (1.9 interaction length) – cost is quite high, justifiable?
Will it give needed purity? What is required?
Accept – energy measurement will be significantly compromised
Physics WG should formulate questions:
Inclusivity?
Efficiency and purity of identifying neutral hadrons?
Justification for longer (more expensive bECal to improve energy resolution.
Proposal vise we should not expect optimized system, but well defined pass to do such optimization and identified Manpower.

## Slide 3
Zhiwan Xu (UCLA)
1.8 WScFi (hECAL) + 20 cm dead Fe +
4.5 int. length Fe/Sc (20/3) (hHcal)
Energy resolution 27% flat from 1-10 GeV
Compare to
37% flat in case of 1 int. length long Ecal.
Should we put in model 1.8 long becal?