## Slide 1: Athena DAQ: Planning and Strategy

## Slide 2
Clock Distribution
Front End Boards
(on/near detector)
Front End Processors
(Electronics in DAQ room)
DAQ Network /
Computing (COTS)
Tape (SDCC)
Components and Terminology:
Front End Boards
(on/near detector)
Front End Boards
(on/near detector)
(etc…)
Detector
Detector
Detector
DAQ
Detectors
Detector /
DAQ
DAQ
SDCC /
DAQ/
Software

## Slide 3
Clock Distribution:
Consists of:
  Custom boards
  Optical links (e.g. lpGPT ecosystem)
Function:
  distribute clock,
  synchronize detector timing with bunch structure,
  synchronize BX (and hence events) between detectors
  share other information between detectors
    bunch polarization
    “prescaling”
Attainable specs:
  100Mhz clock rate (variable within reasonable parameters due to beam energy)
  1ps clock jitter
  Specialized solutions for detectors needing better clock jitter?
Interfaces:
  EIC
  Front End Boards (FEB)

## Slide 4
Front End Boards (FEB):
Consists of:
  Specific to detector
    Integrated + boards near detector
    SiPM + FPGA &/or ASICS near / on detector
    ASICS on detector
Function:
  ADC conversion
  Zero-suppression / other data compression
  Multiplex channels
  Assemble time frames
Attainable Specs:
  Capable of streaming “maximum luminosity” in normal mode
  Not, in general, capable of streaming black events
  Need better definition than this!
Interfaces:
  Clock Distribution
  DAQ computing &/or Front End Processors (FEP)
    eg lpGPT ecosystem, up to 20gbps
  Run mode configuration &/or slow controls

## Slide 5
Front End Processors (FEP):
Consists of:
  Custom Electronics in DAQ room
  FPGA based boards
Function:
  Data Compression
  Event finding / selection
Tradeoffs:
  Interesting Ideas
    FPGAs are well suited to Neural Nets / ML algorithms
    May be capable of very high performance
  But… complex
    Custom electronics which becomes quickly obsolete
    Harder to program and adapt
    ML algorithms can be tricky to verify
    Likely need capability to run in passthrough mode
    Can be mimicked in CPUs
We need a model for cost vs performance for FEP vs CPU based solutions to determine which detectors might benefit from or need FEP capabilities, and to determine whether they are a requirement or a luxury

## Slide 6
FEB/FEP interface to DAQ:
Consists of:
  Physical Level
    Fiber protocol (eg lpGPT ecosystem)
  Logical Level
    Headers to define data source, time frames, and data types?
    do we specify meaning of time frames?
    synchronize time frames?
This interface needs to be well defined before any FEB/FEP electronics designs can be finalized

## Slide 7
DAQ Network and Computing:
Consists of:
  Commercial Off-the-shelf Hardware / Networks
Function:
  Transport data
  Additional data compression
  Format data
  System control and configuration
  Track datafiles and configuration information
  Event Selection and tagging and accounting (HLT)
  QA
  Monitoring
  Logging
Interfaces:
  FEB/FEP
  Software and Computing
    Events?
    Combine same time regions for all detectors in specific files?
    Time regions in multiple files split by detector?

## Slide 8
DAQ Network and Computing:
Other Related Components:
  Scalers
  Slow Controls
  Beam Parameters for analysis <-> feedback to collider from detectors