## Slide 1: Nuclear Data for Space Exploration – Part 1
Lee Bernstein
Department of Nuclear Engineering
UC-Berkeley
Nuclear Science Division
Lawrence Berkeley National Laboratory
August 17, 2021

## Slide 2: About me
Ph.D. in Nuclear Physics from Rutgers University (1994)
LLNL Post-doc → Staff (1994-2016)
  Worked at the intersection of basic and applied science
Joint Faculty Scientist at the UC Berkeley Dept. of Nuclear
  Engineering and the LBNL Nuclear Science Division.
I am the Bay Area Nuclear Data Group Leader where I lead a group
  of 16 researchers and students who work to address the nuclear data
  needs of the applied and basic science community.
Background in low energy nuclear structure, nuclear reactions and plasma physics
I’ve been part of a nuclear data outreach effort to the nuclear energy, isotope production, counterproliferation and space communities through a series workshops and meetings including NDNCA (2015)1, NDREW (2018)2 and WANDA (2019, 2020, 2021) 3
As a new NSAC member I was asked to “provide expert advice in the field of nuclear science, as it relates to nuclear data needs of the applied and basic science and engineering with specialization in measuring low-energy nuclear properties and cross sections”
2 https://info.ornl.gov/sites/publications/Files/Pub111600.pdf
3 https://nucleardata.berkeley.edu/wanda/index.html
1 https://bang.berkeley.edu/events/ndnca

## Slide 3
We decided that a “tag team” approach is the best way to show the way that RHIC can address nuclear data needs for space exploration
Introduction:
  The space environment and the role of shielding
  Dose and the importance of stopping powers
  The nuclear data evaluation process
Particle Transport:
  The transport code universe
  Reaction modeling from 10-3 – 1010 eV
  The role of the US Nuclear Data Program
The role of RHIC
  The STAR fixed target station
  The type of data that can be provided
  How RHIC can help provide the high-energy “Source term” for space shielding applications
Dan Cebra
(UC Davis)
STAR fixed target program leader
National Nuclear Data Center Group Leader
Dave Brown
(BNL)
Lee Bernstein
(UC/LBNL)
UC/LBNL Nuclear Data Group Leader

## Slide 4: Nuclear Data is central to Space Exploration
Nuclear Data
Elemental ID using neutron-induced g-rays3,4
Nuclear Propulsion
Energy Production
Dose/Shielding Calculations for
Electronics4 and Humans5
TOPAZ2
KRUSTY1
Passive (n,xg)
Cosmic rays
Fast neutrons
Natural
Radioactivity
Active (DT) g-rays
1https://www.nasa.gov/directorates/spacetech/kilopower
2Thermionics Quo Vadis? an assessment of DTRAs advanced thermionics research and development program. Washington, D.C. National Academy Press. (2001).
3C. Romano et al., WANDA 2020 Final Report. ORNL/TM-2020/1617 (2020).
4P. Peplowski (JHUAPL) numerous

## Slide 5
Daniel Gomez Toro. Temporal Filtering with Soft Error Detection and Correction Technique for Radiation Hardening Based on a C-element and BICS. Micro and nanotechnologies/Microelectronics. Télécom Bretagne; Université de Bretagne Occidentale, 2014. English. tel-01191520
We are shielded from the Galactic Cosmic Ray Background by our atmosphere and the earth’s magnetic field
What is this Galactic Cosmic Ray Background comprised of?

## Slide 6
The GCR background spans a huge mass and energy range covering virtually all of Nuclear Physics
The GCR includes nuclei as heavy as 56Fe and E/A up to 50 GeV
  For reference, Ebinding(56Fe) ≈0.5 GeV
  The range of 1 GeV proton in Al is > 1 m.
It’s even worse near the gas giants where their magnetic field meets the solar wind.
These high-energy particles create cascades of hundreds of secondary, tertiary etc. particles
  The shielding itself can contribute to the variety of secondary particles produced.
  Charged secondary particles deposit a portion of their energy more locally than neutrons
The solar system beyond the atmosphere and the earth’s magnetic field is a tough neighborhood!
Space exploration requires appropriate shielding over a wide range of energy
T.C. Slaba et al.
Life Sciences in Space Research 12 (2017) 1–15

## Slide 7
What is the effect of the GCR on electronics?
GCRs can cause single event upsets (SEU) in transistors that can cause temporary or permanent failures.
The likelihood of an SEU increases with dose density.
GCR heavy ions cause a local, dense ionization column
Secondary protons and neutrons can induce a nuclear reaction that creates a recoiling residual nucleus
The imparted dose depends on the stopping power of the recoiling nuclei.
M. Lauriente, A. L. Vampola, "Spacecraft anomalies due to radiation environment in space," NASDA/JAERI 2nd International Workshop on Radiation Effects of Semiconductor Devices for Space Applications, Tokyo, Japan, March 1996.

## Slide 8
Ion stopping powers at higher energies are given by the Bethe-Bloch Formula
Good Agreement
E (MeV/u)
P. Sigmund, A. Schinner. NIMB 382 (2016) 15–25
…the credibility of SRIM (the primary stopping power code used) predictions may decrease dramatically in regions of the Z, Ztarget, E parameter space that is unsupported by experimental data.
Poor Agreement
Ionization potential (energy loss to electrons)

## Slide 9
Energy deposition from charged particles in a material
is quantified by the Linear Energy Transfer (LET)
Linear Energy Transfer (LET) is the ratio of energy transferred by a charged particle (dElocal) to target atoms along its path (dx). Units are energy/thickness, e.g., MeV/cm or MeV/mg/cm2
Energy loss in Si
As the energy of an ion → 0 the stopping power increases, leading to a Bragg Peak where the highest dose is deposited
LET (MeV/mg/cm2
Higher-Z ions have shorter ranges and higher dose in their Bragg Peaks
Energy (MeV/u)
LET (MeV/mg/cm2
*P. Sigmund, A. Schinner. NIMB 382 (2016) 15–25
“…the credibility of SRIM (the primary stopping power code used) predictions may decrease dramatically in regions of the Z, Ztarget, E parameter space that is unsupported by experimental data.”*

## Slide 10
Recently Osheroff et al., showed that the LET in AlGaN electronics is dominated by recoiling high mass nuclei
J.M. Osheroff et al. IEEE Transactions on Nuclear Science Volume: 68, Issue: 5, May 2021

## Slide 11
NASA uses “Cocktail” beams of multiple heavy-ions to uniformly dose electronics to test their radiation hardness for use in spacecraft
The LBNL 88-Inch cyclotron*
Mercury Messenger
Curiosity, Spirit & Opportunity Rovers Mars)
Galileo (Jupiter)
Cassini/Huygens (Saturn/Titan)
New Horizons (Pluto )
These are integral tests and don’t add to our understanding of the GCR or the secondary particles it creates
Pioneer (Venus)
E/A=20 MeV
70
60
50
40
30
20
10
0
Ion LET (MeV/mg/cm2)
0 100 200 300 400 500 600 700 800
Range in Si (µm)
* https://cyclotron.lbl.gov/base-rad-effects

## Slide 12
Human radiation damage depends on Dose Equivalency
Normal Background Dose/day on earth: 10 µSv
Lowest annual dose linked to cancer: 100 mSv
DOE Limit for Life Saving activities: 250 mSv
Acute dose causing symptoms: 400 mSv
10 minutes next to the Chernobyl Core: 50 Sv

## Slide 13
The effects of shielding* for projectile-like fragments (Z>8)
*T.C. Slaba et al. Life Sciences in Space Research 12 (2017) 1–15
rAl=2.7 g/cm3
rPE=0.97 g/cm3
Adding shielding decreases dose from heavy ions
Link to cancer
Life saving activities

## Slide 14
The effects of shielding* from neutrons and ions
*T.C. Slaba et al. Life Sciences in Space Research 12 (2017) 1–15
rAl=2.7 g/cm3
rPE=0.97 g/cm3
…but adding shielding increases the dose from neutrons!
Link to cancer
Life saving activities
“Variation in model results… is mainly a result of differing nuclear reaction and fragmentation cross sections, affecting both primary and secondary ion transport”*
This large variation necessitates expensive margins in shielding

## Slide 15
The effects of increasing the lateral size of the shields
*T.C. Slaba et al. Life Sciences in Space Research 12 (2017) 1–15
rAl=2.7 g/cm3
rPE=0.97 g/cm3
(rr)Al =60 g/cm2
0.3 mm H2O
Link to cancer
Life saving activities
Thicker lateral dimension leads to proportionally fewer “hard”, forward-focused neutrons
e.g., ds/dw matters too

## Slide 16
30 cm of tissue self-shielding* from neutrons and ions
*T.C. Slaba et al. Life Sciences in Space Research 12 (2017) 1–15
rAl=2.7 g/cm3
rPE=0.97 g/cm3
(rr)Al =60 g/cm2
30 cm H2O
±25%
This large variation necessitates expensive margins in shielding
“Variation in model results… is mainly a result of differing nuclear reaction and fragmentation cross sections, affecting both primary and secondary ion transport”*
Link to cancer
Life saving activities
ds/dq
matters
too

## Slide 17
The nuclear energy community have addressed nuclear data needs via experiment-guided modeling called evaluation
A sensitivity study is performed for a specific application performs to determine what new experiments are needed.
Published experimental data (including uncertainties) are compiled into databases (EXFOR).
Physics-based theoretical models are adjusted to best reproduce differential measurements (cross section vs. energy, fission yields etc.) and produce an evaluated data library
These values are used to model integral benchmarks (critical assemblies etc.) for validation.
NASA has already started this process!
Compilation
Compilation

## Slide 18
Norbury et al.* have shown that large gaps exist in experimental data needed for shielding optimization
“All” projectiles signify He, C, O, Si, Fe
This is where STAR @ RHIC can really help!
*J.W. Norbury et al.
Radiation Measurements 47 (2012) 315e363
And now onto Dave…
This work contains 64 plots showing the total, charge-changing, elemental and isotopic cross sections needed