## Slide 1: Sub-femtosecond bunch length diagnostic
G. Andonian
BNL ATF Users Meeting 2015
Status Report AE62
October 1-2, 2015

## Slide 2: Motivation
Characterize bunch profile of sub-ps pulses
  Machine performance optimization
  Understand beam variations in emittance, current
Bunch length measurement techniques currently limited to ~few fs
  Coherent radiation interferometry (ATF experience)
  Electro-Optical sampling
  RF Deflector
Femtosecond resolution required for investigation on ultra short pulses
  Microbunching instability of COTR
  Single-spike SASE FEL beam
  Properties of attosecond x-ray production
  Temporal properties of echo-enabled FELs

## Slide 3: Schematic Description
Laser (TEM10 mode)/e-beam interaction in planar undulator
  Angular modulation of beam
  Dependent on longitudinal bunch coordinate
RF deflector provides vertical streak to observe modulation for long bunches
Angular modulation (“sweep”) observable on distant screen (x’ -> x)
  Resolvable with standard optics
Scheme provides enhanced resolution over RF deflector alone.
  “Attoscope”
e-beam
laser
undulator
deflector
screen

## Slide 4: “Attoscope”: optical scale longitudinal diagnostic
Andonian, et al. PRSTAB 14, 072802 (2011)
TEM10
TEM10 mode
Energy modulation
Panofsky-Wenzel theorem
Angular modulation
Sub-fs diagnostic uses a higher-order mode IFEL interaction coupled to a transverse RF deflecting mode.

## Slide 5: Illustrative example
Echo enabled FEL at SLAC
  D.Xiang, et al. PRL 105, 114801 (2010)
Beam modulation at laser wavelength scale
  (~3fs)
Experiment observation by indirect methods
  Limit on resolution of TCAV (<10fs)
Attoscope provides enhanced resolution
  ~100as
Phase Space -
With laser
modulation
deflector
only
“Attoscope”
(deflector + laser mod)
Simulations with Elegant

## Slide 6: AE62 experiment @ BNL ATF (Current Project)
ATF has long history w/ CO2 laser e-beam interactions (IFEL, ICS)
Parameters (simulation)
  E= 44 MeV, Q= 500pC, en = 1mm-mrad
  lu=4cm, N= 10, B0= 0.67T
  l = 10.6 um, PL = 300GW
  Vd = 10MV, Ld = 46cm
TEM10 laser mode
  Simple Michelson style interferometer
Undulator
  Designed/built at Radiabeam
Deflector
  AE37 experiment
Angular modulation (top) and beam distribution at screen (bottom)
Simulations performed with Elegant

## Slide 7: Undulator
N=10, B0=0.67T, L=40cm
Complete design, engineering, fabrication, validation at RadiaBeam
  Hall probe scan
  Pulse wire scan
Undulator final tuning at ATF
Field map
CAD model with alignment
Installed on BL2
Pole fabrication
F. O’shea

## Slide 8: Laser Mode Converter
RadiaBeam Bench
ATF Expt Hall
TEM10 mode
w0= 1.1mm
= 10.3µm
pyrocam
I. Pogorelsky
M. Polyanski
A. Ovodenko

## Slide 9: AE62 Timeline Overview
Experimental stages
  0. Feasibility (August 2014 – #AF62)
    Testing optics, undulator, transport, etc.
  1. Test for interaction (February 2015 - #AE62)
    no deflector
    Observable is increase in beam angular modulation
  2. Full “attoscope” with deflector (coming soon)
✔
✔
ID1
IPOP2
Attoscope
Undulator
IPOP3
IPOP6
Ge
Wafer
IQ1
IQ2
IQ3
IQ4
laser
e-beam
Beamline 2 layout for February 2015 Run

## Slide 10: Results from run
Laser off
(380 µm rms)
Laser on
(500µm rms)
Approximate TEM10 mode with two TEM00 modes at a small angle & out of phase
e-beam transverse profile monitor (IPOP6)
Preliminary results:
Effect of TEM10 laser evident even at “low” energy (~100mJ)
Spreading in horizontal (~25%)
“Butterfly” shape also seen in simulations
Prelim analysis
Next steps
  x-band deflecting cavity !
  Prebuncher + chicane
Laser at focus
~1 mm
x (pixels)

## Slide 11: AE62 Summary
Promising results from February run
  Observed angular modulation of beam in interaction
Analysis with full simulations ongoing
Benefit from Rubicon experience immediately prior
  Synchronization, alignment, etc.
Next run(s)
  Request: 2-3 weeks
    Reestablish laser conditions
    Realign/retune undulator
  Deflecting cavity commissioning (not included)
Acknowledgements:
  M. Harrison, A. Murokh, F. O’Shea, A. Ovodenko (RadiaBeam)
  J. Duris, P. Musumeci, J. Rosenzweig, Y. Sakai (UCLA)
  M. Babzien, M. Fedurin, K. Kusche, R. Malone, I. Pogorelsky, M. Polyanski, C. Swinson (BNL ATF)
Support from DOE SBIR Award # DE-SC0007701

## Slide 12: Back up material

## Slide 13: BL2 scheme
ID1
IPOP2
Attoscope
Undulator
IPOP3
IPOP6
Ge
Wafer
IQ1
IQ2
IQ3
IQ4
laser
e-beam

## Slide 14: Experiment
Use TEM00 mode first
Synchronize laser/e-beam (Ge wafer)
Observe e-beam energy spectrometer (IFEL interaction)
  Vary e-beam energy
  Vary laser power (1GW-10GW-100GW)
    Observe profile on IPOP4 or IPOP5
THEN
Use TEM10 mode
Observe beam profile downstream
  Look for increase in e-beam horizontal divergence
Vary timing
Vary laser power (500MW- 1GW-10GW-100GW(?))

## Slide 15: “Old” simulations
Only TEM10 mode v. laser power (no deflector)
Does not include effects of transport
1 GW
10 GW
100 GW