## Slide 1: ANSYS Structural Analyses of sPhenix Magnet Coil at Full Current John Cozzolino July 10, 2015

## Slide 2
ANSYS FE Structural Analysis of sPhenix Coil
  2d axisymmetric steady-state FE analysis of complete coil
    Includes external aluminum bobbin and G-10 end fillers
    Geometry and forces taken from Wuzheng Meng’s magnetic model – 6/17/2015
      Coil center is shifted 3cm north relative to iron
      Coils divided into 24 blocks, each with corresponding radial and axial pressures due to the Lorentz forces at maximum current
    Thermal stresses from cool-down to 4K included
    Mechanical properties vs. temperature are included
      Coil properties E and CTE adjusted for percentage of insulation vs. conductor (Ref Ansaldo Dwg# 620RM07142, pg. 1)
        Radial direction 2.0% insulation (all coils)
        Axial direction 4.7% (middle coils)
        Axial direction 8.1% (end coils)
    All connections (contacts) are bonded
    Tensile and shear stresses are studied throughout the coil
      Shear stress limit: 30 MPa (4350 psi)
      Tensile stress limit: 30 MPa

## Slide 3
Labels on 24 Solenoid Coils (Not to Scale)
W. Meng
Z
(solenoids/yoke/poles common Axis)
(Yoke axial ctr.)
3.0 cm
Rout=155.06cm
Rin=150.98cm
Coil-package ctr.
Z=0

## Slide 4
 | Coils Ave. Ctr. | (MPa) | (PSI) | (MPa) | (PSI) | (MPa) | (PSI)
 | Zc (cm) | Inner | Inner | Outer | Outer | Inner+Outer | Inner+Outer
Coils 3b +7b | -165.10 | 0.7867 | 114.07 | 0.0032 | 0.46 | 0.7899 | 114.53
Coils 3a + 7a | -152.38 | 0.8978 | 130.19 | 0.0149 | 2.17 | 0.9128 | 132.35
Coils 4 + 8 | -133.30 | 0.9708 | 140.77 | 0.0751 | 10.89 | 1.0459 | 151.66
Coils 5 + 9 | -107.85 | 1.0461 | 151.68 | 0.1502 | 21.77 | 1.1962 | 173.45
Coils 6 + 10 | -82.40 | 1.0286 | 149.15 | 0.1677 | 24.32 | 1.1964 | 173.47
Coils 1 + 2 | -33.34 | 0.4864 | 70.53 | 0.1534 | 22.24 | 0.6398 | 92.76
Coils 11 + 12 | 39.34 | 0.4863 | 70.51 | 0.1532 | 22.22 | 0.6395 | 92.72
Coils 16 + 20 | 88.40 | 1.0275 | 148.98 | 0.1664 | 24.13 | 1.1939 | 173.12
Coils 15 + 19 | 113.85 | 1.0426 | 151.18 | 0.1463 | 21.21 | 1.1889 | 172.40
Coils 14 + 18 | 139.30 | 0.9004 | 130.55 | 0.0693 | 10.05 | 0.9697 | 140.61
Coils 13a + 17a | 158.38 | 0.9004 | 130.55 | 0.0180 | 2.61 | 0.9184 | 133.16
Coils 13b +17b | 171.10 | 0.7944 | 115.19 | 0.0095 | 1.38 | 0.8039 | 116.57
Radial Pressure (outward-force per unit area) Table (W. Meng):

## Slide 5
 | Coils Ave. Ctr. | Fz (N) | Fz(Lb) | Fz (N) | Fz(Lb) | Fz (N) | Fz(Lb) |  |  | 
 | Zc (cm) | Inner | Inner | Outer | Outer | Inner+Outer | Inner+Outer |  |  | 
Coils 3b + 7b | -165.10 | 1.23E+06 | 2.771E+05 | 1.22E+06 | 2.73E+05 | 2.45E+06 | 5.505E+05 |  |  | 
Coils 3a + 7a | -152.38 | 7.84E+05 | 1.761E+05 | 7.84E+05 | 1.76E+05 | 1.57E+06 | 3.520E+05 |  |  | 
Coils 4 + 8 | -133.30 | 1.01E+06 | 2.258E+05 | 1.03E+06 | 2.30E+05 | 2.03E+06 | 4.560E+05 |  |  | 
Coils 5 + 9 | -107.85 | 4.10E+05 | 9.196E+04 | 4.47E+05 | 1.00E+05 | 8.57E+05 | 1.924E+05 |  |  | 
Coils 6 + 10 | -82.40 | -2.97E+05 | -6.675E+04 | -1.96E+05 | -4.41E+04 | -4.94E+05 | -1.108E+05 |  |  | 
Coils 1 + 2 | -33.34 | -3.33E+05 | -7.479E+04 | -3.98E+05 | -8.93E+04 | -7.31E+05 | -1.641E+05 |  |  | 
Coils 11 + 12 | 39.34 | 3.32E+05 | 7.449E+04 | 3.96E+05 | 8.89E+04 | 7.28E+05 | 1.634E+05 |  |  | 
Coils 16 + 20 | 88.40 | 2.96E+05 | 6.638E+04 | 1.94E+05 | 4.36E+04 | 4.90E+05 | 1.100E+05 |  |  | 
Coils 15 + 19 | 113.85 | -4.10E+05 | -9.212E+04 | -4.49E+05 | -1.01E+05 | -8.59E+05 | -1.928E+05 |  |  | 
Coils 14 + 18 | 139.30 | -9.91E+05 | -2.225E+05 | -1.01E+06 | -2.27E+05 | -2.00E+06 | -4.490E+05 |  |  | 
Coils 13a + 17a | 158.38 | -7.71E+05 | -1.730E+05 | -7.69E+05 | -1.73E+05 | -1.54E+06 | -3.457E+05 |  |  | 
Coils 13b + 17b | 171.10 | -1.22E+06 | -2.749E+05 | -1.21E+06 | -2.71E+05 | -2.43E+06 | -5.462E+05 |  |  | 
 |  |  |  |  | Total Fz = | 7.00E+04 | 1.57E+04 |  | (with 3 cm Shift) | 
 |  |  |  |  |  | (N) | (Lb) |  |  | 
Axial Force Table (W. Meng):

## Slide 6
Full Geometry
FE Mesh (Lead End)
Aluminum Bobbin
Outer Coil
Inner Coil
G-10 Filler

## Slide 7
Radial Deflection @ Cool-down Followed by Max Current (LE View)

## Slide 8
Axial Deflection @ Cool-down Followed by Max Current (LE View)

## Slide 9
Equivalent Stress in Aluminum Bobbin @ Cool-down & Max Current (LE View)

## Slide 10
Lead End Max Shear and Tensile Stresses @ Full Power

## Slide 11
Non-Lead End Max Shear and Tensile Stresses @ Full Power

## Slide 12
Lead End Axial Compressive Stresses at Cool-down & Full Power (MPa)

## Slide 13
Non-Lead End Axial Compressive Stresses at Cool-down & Full Power (MPa)

## Slide 14
Summary & Conclusions
  Cool-down and Lorentz forces will not yield the aluminum bobbin.
    Assuming 5083-0 (annealed) YP= 110 MPa (16 kpsi)
  Tensile stresses at the coil ends exceed the allowable limit (30 MPa) at maximum operating current.
    Based on the maximum principal stress (σ1)
  Shear stresses at the coil ends are at the allowable limit (30 MPa) at maximum operating current.
  Axial compressive stresses at the coil ends do not exceed the yield point of 99.5% pure aluminum (~30 MPa).