## Slide 1
Athena DAQ WG report
EICUG Meeting August 4th, 2021
Conveners:
Jeff Landgraf (BNL), Alexandre Camsonne (JLAB)

## Slide 2
Clock Distribution
(Front End Boards
on/near detector)
Front End Processors
(Electronics in DAQ room)
DAQ Network /
Computing (COTS)
Tape (SDCC)
Front End Boards
(on/near detector)
Front End Boards
(on/near detector)
(etc…)
Detector
Detector
Detector
Athena DAQ Overview
We envision a triggerless streaming DAQ system following the outline described in the Yellow Report

## Slide 3
Clock Distribution:
Function:
  Distribute a synchronized clock,
  Synchronize detector timing with bunch structure,
  Tag data with BX to synchronize detector data
  share other information between detectors
    bunch polarization
    “prescaling”
Promising Technology:
  lpGPT ecosystem
Attainable specs:
  100Mhz clock rate (variable within reasonable parameters due to beam energy)
  ~5ps clock jitter

## Slide 4
Front End Boards (FEB)
Detector | Readout Technology | Channel Count
Silicon Tracking | Si MAPS | 200M
GEM/MMG Layer | GEM | 217K
Cylindrical MPGD * | GEM | 60M? (calculated from baseline)
HP-DIRC | MAP/MT | 100-330k
ECAL | SiPM | 1.7K
HCAL | SiPM | 24K
HCAL imaging | Si MAPS | 480M
dRICH | PMT/SiPM | 350K
mRICH | PMT/SiPM | 330K
B0 | Si MAPS | 32M + 320K
Off-Momentum | AC-LGAD (eRD24) | 750K
Roman Pots | AC-LGAD (eRD24) | 500K
ZDC | LGAD + ASIC eRD27 | 225+366
TOF | AC-LGAD | 15M
The collider performance:
  ~500KHz of collisions
  ~15M tracks per second
  ~60-100Gbps zero suppressed data
  ~15 KB/event
  ~100 bytes/bunch crossing
The Athena Detector current baseline:
  More than 500M channels
Challenging data compression scheme
  Noise reduction
  Zero suppression
  Background elimination

## Slide 5
Front End Processors (FEP):
Consist of:
  FELIX boards
  Crates with FPGA based boards (ATCA, open VPX)
Function:
  Aggregation of links from the FEBs
  Data Compression
  Event finding / selection
For processing there are tradeoffs:
  Pro
    Low Latency
    Deterministic timing
    Well suited to Neural Nets / ML Algorithms
  Cons
    Harder to program and adapt than CPUs
    Quickly become obsolete

## Slide 6
DAQ Network and Computing:
Consists of:
  Commercial Off-the-shelf Hardware / Networks
Function:
  Final data compression
  Format and transport data
  System control and configuration
  Event Selection and tagging, tracking and accounting
    High Level Trigger
    Scalers, counters databases
  QA
  System control and configuration
Strongly Advocate for a streaming model which
  Builds events as early as possible