## Slide 1: Athena Calorimetery WG
erhtjhtyhy
Paul E Reimer
Oleg Tsai
Vladimir Berdnikov
This work is supported in part by the U.S. Department of Energy, Office of Nuclear Physics under contract No. DE-AC02-06CH11357.
From DD4HEP Geometry Viewer

## Slide 2: Calorimeter WG: Endcaps
NECal
  Crystals are now 55 cm for 20 X0
    Already in DD4HEP
  Some passive material missing between NE & NHCal
PECal
  Tungsten SciFi
  DD4HEP description needs memory optimization to run efficiently

## Slide 3: Calorimeter WG: Barrel
BHCal
  layer steel + scintillator design
  10cm square pad size (as above)
  Somewhat orphaned?
BECal—imaging
  implemented with 6 tracking layers
  optimization of the number tracking layers and the spacing between them is ongoing.
BECal
  Pb/SciFi calorimeter
  Readout on ends

## Slide 4: Barrel-Positive Endcap Interface
How much room is needed for
  BECal support structure
  BECal readout
  DRICH
  Utilities
  . . .
Possible solution:
  Extend PECal radially outward?
  Would this work with the supporting structure for the BHCal/flux return steel?
Not up-to-date

## Slide 5: Material Budget Before ECal’s
ECal can’t measure energy that it never sees.
Material between interaction and Ecal
  1.5 < |η| < 2.5 this is around 0.75 to 0.10 X0
  |η| < 1 minimum of 0.04-0.05 X0
See presentation by Alexander Bazilevsky at https://indico.bnl.gov/event/12911/contributions/53748/attachments/36834/60612/ATHENA_EMCal_Material.
Yellow Report Tab 8.20: Electron and photon minimum E = 0.05 GeV