## Slide 1: PID Update for Global Design/Integration
TK Hemmick, F Geurts, R Preghenella

## Slide 2: Reminder of Baseline Configuration
Negative direction:
  Projective mRICH
  Principle concern(s)
    Response (trapped light)
    Material thickness (can we do less material)
Barrel
  DIRC
  Principle concern(s)
    Support/Integration
Positive direction:
  dRICH
  Principle concern(s)
    Optics (coupled directly to detector location)

## Slide 3: mRICH in Backward Region
Implemented as a pseudo-projective array:
  Detector envelope ~planar in Zed.
  Individual modules tilted toward nominal collision point.
Advanced stage of implementation in DD4HEP
Cherenkov Photons in DD4HEP
Concern:
Calorimeter Group concerned about material
  Not yet evaluated “globally”.
  Nonetheless simulations are “optimistic”

## Slide 4: Requested Alternative Implementation:
Monolithic geometry
  Thinner due to no walls.
  Support very likely thinner (note: too thick before support!)
Optics options:
  Lens array:
    Focused but sometimes split and non-circular rings
  Proximity:
    How much zed-gap to achieve required performance.

## Slide 5: dRICH
Performance in brief (too brief)
  Single Photon Resolution (linear)
      Chromatic: n(l)
      Emission: emission point vs detection
      Pixel: Sensor pixel & focal length
      Magnetic Field: Smears ring
      Track Resolution: WITHIN radiator
    Aerogel dominated by irreducible contribution (chromatic/scattering)
    Gas limited by Emission even in “less constrained” JLEIC design.
  Photon Count (improves as SQRT(n))
Simulation Result(s)
  Magnetic field contributions
    Backing away more impactful than solenoid-vs-Helmholtz
    Implications for interface location.
  More detail:
    Ayk contributions on additional slides
JLEIC Design
1 mrad

## Slide 6: A few trials…
Note(s)
  Simple implementation very useful for optics
  Likely p.e. count is over-estimated.
  Pretty small gaps
Need detailed understanding of the focal plane
How thick is the focal plane?
Separate cooling for sensors & electronics?
Use gaps between focal plane segments?

## Slide 7: Other…
Without planar mirror, detection >25 degrees very tough.
With planar mirror even more restricted.

## Slide 8: Beyond Baseline
Proposed GridPIX in the B-2.0
  Last Silicon @ R=18.5cm
  First mMEGAS @ R=50cm
Sandwich with plausible services gaps to avoid overlaps.
  Likely need larger gap on Silicon side than on mMEGAS side.
Similar for LGAD (~matches cost document)
9/14: Trk mtg
GridPIX
DR = 31.5 cm…GridPIX comfortable using ~20 cm
LGAD
LGAD