## Slide 1: FUDGE: LLNL nuclear data infrastructure
Presented at CSEWG
Bret Beck
Nov 2021

## Slide 2: Overview of FUDGE
For Updating Data and Generating Evaluations (FUDGE)
Use to read/write, plot, modify and process GNDS data
  Processing for Monte Carlo and multi-group transport.
User interface is python 3.6+.
  Computationally intensive stuff written in C and C++.
    E.g., heating cross sections, multi-grouping distributions.
    Users do not interact directly with the C and C++ codes, the python interface handles that.
FUDGE is like a toolkit but we are writing many scripts that are included in the bin directory
FUDGE can convert ENDF-6 (and LLNL ENDL) files into GNDS, and GNDS to ENDF-6.

## Slide 3: FUDGE processing example for transport codes
FUDGE command to process a GNDS file for deterministic and Monte Carlo transport at 3 temperatures (MeV/k)
Output (i.e., processed) file contains
  evaluation data
  Reconstructed cross sections (if needed)
  Coulomb + nuclear elastic m cutoff (if needed)
  average product data (needed for energy deposition - KERMA)
  pdf/cdf data for distributions (e.g., P(E’|E))
  heated cross sections (at 3 temperatures in example above)
  Common grid heated cross section for Monte Carlo (ditto)
  multi-group data (ditto)
  TNSL data, if present, are processed
bin/processProtare.py -mc -mg -t 2.58522e-08 -t 1e-07 -t 1e-4 gnds.file.xml
URR processing is done separately, still needs to be integrate in.

## Slide 4: GNDS 2.0 support in FUDGE
GNDS 2.0 has not been officially released but it is most likely complete except for a few minor requests.
FUDGE is up-to-date to handle GNDS 2.0
  Except for TNSL (see Caleb) and that’s because the specification are still being tweaked.
Internally, FUDGE looks a lot like GNDS 2.0
  I will show examples later
Since GNDS 2.0 is not finalized, FUDGE writes the format as ‘2.0.LLNL_4’.
  We have generated ‘2.0.LLNL_4’ file for ENDF/B-VIII.0 that the OECD/NEA will make available (see Michael Fleming)

## Slide 5: FUDGE creates many “nodes” automatically
For example, in GNDS 2.0 the top node “reactionSuite” has the following child nodes:
All of these are automatically created by the “reactionSuite” constructor (i.e., “__init__”) except for the “resonances” node and I will try to fix that.
All child nodes but “PoPs”, “resonances”, “sums” and “resonances” have an ”add” method to add an object.
Adding an instance to reactions example
  reactionSuite.reactions.add( reaction )
externalFiles styles PoPs
resonances reactions orphanProducts
sums productions incompleteReactions
fissionComponents applicationData

## Slide 6: GNDS 2.0 documentation node support in FUDGE
The documentation node in GNDS 2.0 allows one to record a lot of information (thanks mainly to Dave Brown).
Child nodes are: authors, contributors, collaborations, dates, copyright, acknowledgements, keywords, relatedItems, title, abstract, body, computerCodes, experimentalDataSets, bibliography and endfCompatible.
All child nodes are automatically created by the documentation constructor
Next slide show how to populate title and abstract nodes.

## Slide 7: Documentation example
from xData.Documentation import documentation
doc = documentation.Documentation( doi="12.23134/8821.322" )
doc.title.body = "This is the title."
doc.abstract.body = "Pythagoras' theorem is $a^2 + b^2 = c^2$."
doc.abstract.markup = "latex"
print( doc.toXML() )
<documentation doi="12.23134/8821.322">
<title><![CDATA[This is the title.]]></title>
<abstract markup="latex">
<![CDATA[Pythagoras's theorem is $a^2 + b^2 = c^2$.]]></abstract></documentation>
Note, only nodes that have been populated are written to a file.

## Slide 8: GNDS 2.0 map file supported in FUDGE and GIDI+
<map library="Example" format="2.0">
<protare projectile="n" target="O16" evaluation="fromJoe"
path="fromJoe/n-008_O_016.xml"/>
<protare projectile="n" target="U235" evaluation="fromJoe"
path="fromJoe/n-092_U_235.xml"/>
<protare projectile="n" target="U235" evaluation="Ian"
path="fromIan/n-092_U_235.xml"/>
<protare projectile="n" target="U238" evaluation="Ian"
path="fromIan/n-092_U_238.xml"/>
<TNSL projectile="n" target="OinBeO" evaluation="ENDF/B-8.0"
path="tsl/tsl-OinBeO.xml">
standardTarget="O16" standardEvaluation="ENDF/B-8.0"/>
<import production.map></map>
A map file supports nesting which is used by EMU.

## Slide 9: LLNL also has multi-group boundaries and flux files
Multi-group boundaries format uses GNDS <group> node to store the label and boundaries for a group. /path/to/FUDGE/bin/addMultigroup.py -h
Flux stored as f(T,E,mu) using a GNDS 3d function. /path/to/FUDGE/bin/addFlux.py -h
<group label="LLNL_gid_23">
<grid index="0" label="energy" unit="MeV" style="boundaries">
<values>2.0908e-6 2.0908e-4 1.8817e-3 .010245 .07002 0.27097 .7527 15.754</values>
</grid></group>
<XYs3d label="LLNL_fid_1">
<axes>
<axis index="3" label="temperature" unit="MeV/k"/>
<axis index="2" label="energy_in" unit="MeV"/>
<axis index="1" label="mu" unit=""/>
<axis index="0" label="flux" unit="1/s"/></axes>
<XYs2d outerDomainValue="0.0">
<Legendre outerDomainValue="0.0"><values>85</values></Legendre>
<Legendre outerDomainValue="21.0"><values>85</values></Legendre></XYs2d></XYs3d>

## Slide 10: Plotting example for ‘n + U230’ via pyQt5 and matplotlib
from fudge import map as mapModule
map = mapModule.Map.readXML( 'ENDF-VIII.0/all.map' )
protare = map.findAllOf('n', 'U230')[0].protare()
crossSections = []
for reaction in protare.reactions:
crossSection = reaction.crossSection.toPointwiseLinear( lowerEps=1e-7 )
crossSection.plotLegendKey = str( reaction )
crossSections.append( crossSection )
crossSection.multiPlot( crossSections, rangeMin = 1e-5, xylog = 3,
title='n + U230', xLabel='Neutron energy [eV]', yLabel='Cross section [b]' )
Plot is interactive

## Slide 11: Check for missing gamma data in ENDF-VIII.0
from fudge import map as mapModule
from fudge.productData.distributions import unspecified
map = mapModule.Map.readXML( 'ENDF-VIII.0/all.map' )
neutrons = map.findAllOf( 'n' ) # First argument is projectile
for mapProtare in neutrons:
protare = mapProtare.protare()
for reaction in protare.reactions:
for product in reaction.outputChannel.products:
if product.id == 'photon':
distribution = product.distribution[0]
if isinstance(distribution, unspecified.form ):
print( product.toXLink() )
This example ignores nesting of products, but the code I used did include nesting.

## Slide 12: FUDGE scripts
We are developing scripts to make it easier to examine and process GNDS files.
Some examples include:
  processProtare.py: Processes for Monte Carlo and multi-group transport
  peek.py: Prints each reaction and brief information about each reaction's products.
  temperatures.py: List all temperature data in a GNDS file
  checkGNDS.py: Check the physics in a GNDS file (e.g., positive cross sections, normalize distributions)
  diffGNDS.py: Does a partial diff of two GNDS files
  buildMapFile.py: Creates a map file from a list of GNDS files
  checkMap.py: Check a map file and all it reference

## Slide 13: Some of what are we working on in FUDGE
Improving URR probability table building
  We are working with BNL on this (Dave Brown and Matteo Vorabbi)
  Currently, not automatic in FUDGE
Adding a multi-group sums node to reduce load time for deterministic transport codes
  Initially, this will go under the “applicationData” node
Additional ACE support
  Currently supports GNDS to ACE for neutrons transport including TNSL
Update codes for GPUs where possible and beneficial (e.g., heating cross sections, calculating multi-group transfer matrices)

## Slide 14: FUDGE refactoring
We have been doing some needed refactoring of FUDGE
Latest release includes most of the refactoring but still have more to do
Hope to complete refactoring by January 2022 and do another release
That said, anyone interested in FUDGE should get the latest release and play with it since a few small changes should be needed to update scripts for the January release

## Slide 15: Other talks related to FUDGE
Caleb Mattoon will be talking on TNSL data and FUDGE
  Talk Wednesday at 10:00 am EST
  “TNSL Implementation and Testing in FUDGE”
Kyle Wendt will be talking on EMU
  Talk today at 17:35 EST
  “An Uncertainty Quantification Toolkit for GNDS Formatted Libraries”
  Evaluated Means and Uncertainties (EMU)
  Generates realizations from mean and covariance data
  Uses FUDGE to read/write and modify data.
  Also generates processed files

## Slide 16: GIDI+
A collection of packages for transport codes to read GNDS files
  Mainly written in C++
GIDI+ consists of the following packages:
  PoPI: Property of Particles Interface
    Reads PoPs data
  GIDI: General Interaction Data Interface
    Read in a GNDS reactionSuite file
    Supports map files
    Includes support for multi-group data including collapsing
    Currently, only reads GNDS data needed by transport codes
  MCGIDI: Monte Carlo GIDI
    For use in Monte Carlo transport codes
    Extracts needed data from a GIDI instance
    Has cross section, energy deposition, etc. lookup functions by temperature and energy
    Has reaction, distribution sampling functions.
  plus other packages rarely called directly by transport codes

## Slide 17: What are we working on in GIDI+
Decreasing load times
  ‘lazy reading’
  Summed data for deterministic transport codes
Direct sampling of elastic TNSL data
  from S(E,T) for coherent elastic
  from DebyeWaller - W’(T) – for incoherent elastic
Updating the version in GEANT4
  Current version is many years old and does not read GNDS
  We have funding to work on improving diagnostic gammas
    Dave Brown and BNL leading effort
Add physical unit support
  Already in FUDGE

## Slide 18: Code releases
We are releasing all codes under https://github.com/LLNL
  FUDGE
    https://github.com/LLNL/fudge
    Version 5.0
    Python 3.6+
    Pip install – instructions on github site
    BSD license (will switch to MIT license)
    GNDS format is 2.0.LLNL_4 which should be the same as 2.0 if there are no further changes to GNDS 2.0 specifications (except for TNSL data)
  GIDI+
    https://github.com/LLNL/gidiplus
    Version 3.22.??
    C++11
    GNDS format is 2.0.LLNL_4 (and 2.0?)
Releasing all codes under MIT license, except currently FUDGE

## Slide 19: Final comment
Latest releases of FUDGE and GIDI+ will be available in a few days.
Plan to do another release around 1 Jan. 2022.
If you find any issues with FUDGE or GIDI+ please let us know
We plan to also release EMU (see Kyle Wendt)
We need you to look at the latest 2.0* including
  The specification document
  the NEA files
  What FUDGE is doing (i.e., it is doing something wrong)

## Slide 20
Disclaimer
This document was prepared as an account of work sponsored by an agency of the United States government. Neither the United States government nor Lawrence Livermore National Security, LLC, nor any of their employees makes any warranty, expressed or implied, or assumes any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, apparatus, product, or process disclosed, or represents that its use would not infringe privately owned rights. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise does not necessarily constitute or imply its endorsement, recommendation, or favoring by the United States government or Lawrence Livermore National Security, LLC. The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States government or Lawrence Livermore National Security, LLC, and shall not be used for advertising or product endorsement purposes.

## Slide 21: GIDI+ main user packages
PoPI
  Properties of Particle Interface
  C++ API to read and allow access to GNDS PoPs data
GIDI
  General Interaction Data Interface
  C++ API to read and access to GNDS data
  Developed to give access for transport codes
  Follows outline of GNDS
  Has Map and Protare classes
MCGIDI
  Monte Carlo General Interaction Data Interface
  C++ API for use in Monte Carlo transport codes
  Extracts data from a GIDI::Protare
  Stores data in more suitable way for Monte Carlo transport
  Cross section look up by temperature and projectile energy for host code
  Samples a reaction for a protare
  Samples outgoing particle data for a reaction

## Slide 22: GIDI+ (or gidiplus)
To use GIDI and MCGIDI requires additional packages. GIDI, MCGIDI and these additional packages are dubbed GIDI+.
  pugixml-1.8
    Third party XML parser
    Written in C++
  statusMessageReporting
    Handles message passing between C packages
    Written in C
  numericalFunctions
    Supports 1d numerical functions including addition, multiplication
    Written in C
  PoPI
  GIDI
  MCGIDI
statusMessageReporting and numericalFunctions are also used by FUDGE.

## Slide 23: PoPI C++ API
Property of Particles Interface (PoPI)
Implements the PoPs part of GNDS
Uses strings for particle IDs as defined in GNDS
  (e.g., “O16”, “n”, “U235”, “u235_e6”)
Current LLNL PoPs files
  pops.xml (currently only defines ground state nuclei)
  metastables_alias.xml (e.g., “Am242_m1” for “Am242_e2”)
  LLNL_alias.xml (e.g., “92235” for “U235”)

## Slide 24: Simple PoPI example
PoPI::Database pops( "pops.xml" );
pops.addFile( "metastables_alias.xml" )
PoPI::Particle const &O16 = pops.get<PoPI::Particle>( "O16" );
// O16 = pops.particle( "O16" );
std::cout << "O16 -> " << O16_3.ID( ) << std::endl;
std::cout << "mass = " << O16_3.massValue( "amu" ) << std::endl;
O16 -> O16
mass = 15.9949

## Slide 25: GIDI C++ API
General Interaction Data Interface (GIDI)
A C++ API for reading a GNDS reactionSuite.
  Uses PoPI to read the PoPs part.
Retrieving and collapsing multi-group data for use in deterministic codes (or Monte Carlo but that is better handled by MCGIDI).
Protare is a virtual class. Actual classes are ProtareSingleton, ProtareComposite and ProtareTNSL.
Support reading/writing GNDS 1.10 and 2.0(?) but, like FUDGE, uses 2.0 internally.

## Slide 26: Simple GIDI example
GIDI::Map map( “test.map”, pops );
GIDI::Construction::Settings construction( GIDI::Construction::e_all,
GIDI::Construction::e_nuclearAndAtomic );
GIDI::Protare *protare = map.protare( construction, pops, PoPI::IDs::neutron, "O16" );
GIDI::Styles::TemperatureInfos temperatures = protare->temperatures( );
GIDI::Settings::MG settings( protare->projectile( ).ID( ), label, true );
GIDI::Vector crossSection = protare->multiGroupCrossSection( settings, particles );
(venv-3.7.2) # temperatures.py ~/GIDI_plus/GIDI/Test/Data/MG_MC3Ts/neutrons/n-008_O_016.xml
/g/g16/beck6/Git/GIDI_plus/GIDI/Test/Data/MG_MC3Ts/neutrons/n-008_O_016.xml
temperature 0.0 K: eval
temperature [K] heated griddedCrossSection URR_probabilityTables heatedMultiGroup SnElasticUpScatter
----------------------------------------------------------------------------------------------------------------------------------------------
300.1 heated_000 MonteCarlo_000 MultiGroup_000
1.16e+04 heated_001 MonteCarlo_001 MultiGroup_001
1.16e+06 heated_002 MonteCarlo_002 MultiGroup_002
typedef std::vector<Styles::TemperatureInfo> TemperatureInfos;

## Slide 27: MCGIDI C++ API for GNDS
Monte Carlo GIDI (MCGIDI)
A C++ API for Monte Carlo transport codes
Can do LLNL model A and B (MCNP) upscatter for outgoing particles
Supports broadcasting for MPI and GPUs
Implemented in LLNL’s Monte Carlo transport code Mercury

## Slide 28: Simple MCGIDI example
double energy = 14.1, crossSection, reactionCrossSection;
MCGIDI::DomainHash domainHash( 4000, 1e-8, 10 );
MCGIDI::Protare *MCProtare = MCGIDI::protareFromGIDIProtare( *protare, pops, MC
particles, domainHash, temperatures, reactionsToExclude );
int hashIndex = domainHash.index( energy );
crossSection = MCProtare->crossSection( URR_infos, hashIndex, temperature, energy );
reactionCrossSection = MCProtare->reactionCrossSection( ir, URR_infos, hashIndex,
temperature, energy );
int reactionIndex = MCProtare->sampleReaction( URR_infos, hashIndex,
temperature, energy, crossSection, rng, rngState );
reaction->sampleProducts( MCProtare, energy, input, products );