## Slide 1: TN update plans and advances for 16O and 9Be
Cross Section Evaluation Working Group
Evaluations Committee
G. Hale & M. Paris (LANL/T-2)
2021-11-18
LA-UR-21-31398

## Slide 2
Outline
Thermonuclear/charged-particle evaluation updates
n+9Be status & plans
n+16O progress report

## Slide 3
Thermonuclear/charged-particle reactions
Detailed in earlier Charged-particle session 2021-11-17
Evaluation updates & new evaluations
  p-001_H_001.endf
  p-002_He_004.endf
  d-001_H_003.endf
  d-002_He_003.endf
  d-003_Li_006.endf
  t-002_He_004.endf
  a-006_C_013.endf

## Slide 4
n+9Be evaluation

## Slide 5
Light-element R-matrix evaluation
R-matrix formalism

## Slide 6
n+9Be New evaluation
Added data: elastic, (n,𝛼), (n,n1)
NA

## Slide 7
n+9Be Integrated Cross Sections

## Slide 8
9Be(n,n)9Be Differential Cross Sections

## Slide 9
9Be(n,n1)9Be* Differential Cross Sections
              Summary of new evaluation:
10Be analysis has produced a consistent set of cross sections and angular distributions that are in agreement with most of the experimental data at energies up to 5 MeV. Extensions above that energy were based on the experimental data alone.
Level assignments for the overlapping resonances near En=2.7 MeV have the opposite parity (4-,3+ → 4+,3-).
Excited states of 9Be make important contributions to the (n,2n) cross section (MT=16 → 24 in the new evaluation).
Testing/benchmarking: (M. Herman, LANL) and thick-target angular neutron yields (Y. Danon, RPI) on the following slides

## Slide 10
Comparison to previous ENDF/B Integrated cross sections

## Slide 11
Testing/benchmarks Pencil-beam study
K. Parsons/LANL

## Slide 12
Testing/benchmarks Lab spectra
Theoretical model expectation (G. Hale/LANL)
Lab elastic diff. scattering cross section excitation function (b/sr) at 26° as a function of E, the incident lab neutron energy (MeV).
Outgoing neutron TOF spectrum at 26° vs.
t= 2236/sqrt(E) in ns. Incident energy (top axis), the first two resonances give structures at about 2400 and 2800 ns.
2-
s-wave
3-
2+
1-
destructive
4+,3-
1-
1-
4+,3-
2+
3-
1-
destructive

## Slide 13
Outgoing neutron TOF spectrum at 26° vs.
t= 2236/sqrt(E) in ns. Incident energy (top axis), the first two resonances give structures at about 2400 and 2800 ns.
Testing/benchmarks Lab spectra
Quasi-integral simulation in MCNP (Y. Danon/RPI)
3-
2+
3-
4+,3-
1-
1-
1-
4+,3-
2+
3-
1-
destructive

## Slide 14
Testing/benchmarks Pulsed Be spheres
MCNP simulations (D. Neudecker/LANL)
  Due to change (n,2n) & (n,n’) evident near elastic peak
  (n,2n) should probably be (has not been) reduced by (n,n’)

## Slide 15
Perturbative criticality study M. Herman & W. Haeck (LANL)

## Slide 16
Krusty testing J. Favorite (LANL/XCP-7)
Case | Benchmark | ENDF/B-VII.1 | ENDF/B-VIII.0 | ENDF/B-VIII.1
keff |  |  |  | 
1 | 1.00065 | 1.00315 | 1.00043 | 1.00259
2 | 1.00345 | 1.00597 | 1.00325 | 1.00551
3 | 1.00017 | 1.00291 | 1.00017 | 1.00240
4 | 1.00048 | 1.00300 | 1.00033 | 1.00250
5 | 1.00189 | 1.00441 | 1.00174 | 1.00393
C–E |  |  |  | 
1 |  | 0.00250 | -0.00022 | 0.00194
2 |  | 0.00252 | -0.00020 | 0.00206
3 |  | 0.00274 | 0.00000 | 0.00223
4 |  | 0.00252 | -0.00015 | 0.00202
5 |  | 0.00252 | -0.00015 | 0.00204
"Krusty detailed models compared with the benchmark, ENDF/B-VII.1, and
ENDF/B-VIII.0. We nailed it with ENDF/B-VIII.0. The new cross sections are
a little better than ENDF/B-VII.1 but not nearly as good as ENDF/B-VIII.0."

## Slide 17
n+16O evaluation

## Slide 18
ENDF/B history
6.8, 7.1, 8.0
ENDF/B-VI.8 (2001 April): LANL(Chadwick, Hale, Young), KAPL(Caro, Lubitz)
  Below 3.4 MeV*: R-function + optical model (OPTIC code; Caro)
  3.4 < En < 6.25: LANL R-matrix (multichannel; EDA)
    Data: n+16O (total) [Johnson75, Larson80], 16O(n,el) ang.[Lane60,…],
    16O(n,𝛼0) [inverse Walton et al.], 13C(𝛼,n), 13C(𝛼,el) excit. fn
  En > 6.25
    6.25  20: subtraction of non-elastic (MT=3) from total
    Inelastic (MT51, …, 57)
      16O(n,x𝛾) Nelson, Chadwick, Michaudon & Young NSE99
  MT800: Bair&Haas73 without renormalization
    6.220: factor of 1.5 “bring into rough agreement” (n,𝛼0) of Davis ‘63
  MT801-803: inferred from (n,𝛼𝛾) [Nelson99]
ENDF/B-VII.1 (2005 Dec.): VI.8+Page+Kawano+Young
  MT=800: 32% reduction (n,𝛼0) 2.48.9 MeV
    “assuming Harissopulos05 are definitive”; “Ha05 is 100% correct, BH73 100% wrong norm”
ENDF/B-VIII.0 (2016 Dec.): VII.1+Hale+Kawano+MWP
  Re-evaluation of Ha05 by Giorginis et al. (CIELO)
JENDL-4.0 (2010)
  16O(n,𝛼tot) < 6.5 MeV ~ ENDF/B-VII.0
*all incident neutron lab energies [MeV]

## Slide 19
ENDF/B comparisons 16O(n,𝛼0)13C [MT=800]
6.8, 7.1, 8.0
Three regions
  < 5.2 MeV
  5.2  6 MeV
  > 6 MeV
Trends
  7.1 < 6.8/8.0
  ~Equivalent
  7.1 < 6.8 < 8.0

## Slide 20
17O Preliminary evaluation
Preliminary results
Configuration: channels, R-matrix parameters
Observed data in data deck
  Channels: (n,n0), (n,n2), (𝜶,n0), (𝜶,n1), (𝜶,n)
  Types: total, integrated, differential, polarization [Ay, Pn]
New data
  Ciani et al. (2021) (𝜶,n0)
  Brandenburg & Meisel (2021) (𝜶,n)
  Febbraro, DeBoer et al. (2020) (𝜶,n0), (𝜶,n1)
17O system channel/pars
# channels: 45
  J𝝅=1/2±, ..., 11/2±
# parameters
  E𝜆: 81 level energies
  𝛾𝜆,c: 322 reduced widths
# Normalizations
  nM: 95 norm scales
  EM: 4 shift factors

## Slide 21
17O Preliminary evaluation
Preliminary results: (𝜶,n0)
preliminary
preliminary
preliminary
preliminary

## Slide 22
17O Preliminary evaluation
Preliminary results: (𝜶,n1)
preliminary
preliminary
preliminary
preliminary

## Slide 23
17O Preliminary evaluation
Preliminary results: low energy

## Slide 24
Comparison LENZ(2017) data vs. ENDF/B-VIII.0
16O(n,𝛼0)13C excitation functions
S. Kuvin & H.Y. Lee (LANL)
Angular convolution
No energy resolution broadening
LENZ2017 acceptance
vs. angle

## Slide 25
17O Preliminary evaluation scope
Preliminary results

## Slide 26
ENDF/B-VIII.0 16O(n,𝛼0)13C [MT=800]
Comparison with New Evaluation “8.1”
preliminary

## Slide 27
ENDF/B-VIII.0 16O(n,𝛼0)13C [MT=800]
Ratio of New Evaluation to ENDF/B-VIII.0

## Slide 28
Preliminary new evaluation
vs. OU(2021) & Bair & Haas(1973)

## Slide 29
Outlook
n+9Be
  the added inelastic data is well represented – why isn’t it performing better?
    Formatting? EDAf90 ENDF-6 correct?; ENDF-6  ACE correct?
    Is (n,2n) properly represented?
      9Be(n,2n)8Be* + 9Be(n,n’)9Be* vs. 9Be(n,2n)𝛼𝛼
  ENDF/B-VIII.1 release push to Feb. 2024
    re-assess available data
    push to higher energies
    update the evaluation & covariances
n+16O
  Complete the evaluation to En ~ 9 MeV (maybe 10 MeV)
    add missing data
    Investigate normalization of the (n,ntot) Cierjacks’ ‘68 & ‘83 datasets
  13C(𝛼,n0)16O is currently too high everywhere
    Note that (n,ntot) and (n,𝛼x) are tightly correlated by unitarity
  Perform a complete normalization/covariance study