## Slide 1: Update on short-lived and cumulative fission product yields from the NPML Collaboration
J.T. Harke, B. Bandong LLNL
T.A. Bredeweg LANL
B. Pierson, J.Friese PNNL
November 2021
Notes: 5 minutes!

## Slide 2: Multi-Lab multi-disciplinary collaboration
LLNL
J.T. Harke
B. Bandong
S. Burcher
S. W. Padgett
J. Goodell
J. Church
P. Zhao
N. Gharibyan
N. Harward
R.A. Henderson
K. Roberts
P. Yap-chiongco
G. Slavik
LANL
T. Bredeweg
S. Hanson
I. May
J. Goda
D. Hayes
J. Hutchinson
J. Walker
PNNL
J. Friese
B. Pierson
L. Greenwood
S. Stave
A.M. Prinke
L.A. Metz
S. Herman
N. Uhnak
M. Haney
Oregon State University
A.S. Tamashiro
C. Palmer
T. Palmer
S. Reese
S. Menn
L. Minc

## Slide 3: Introduction
Motivation:
There have been few short-lived fission product yield studies since the publication of the England and Rider report in 1993 (28 years). The yields in the England and Rider report are a collection of results from experiments occurring from the 1950s through to the early 1990s.
Integral cross-section measurements in unperturbed fast fission neutron fields are rare but crucial data for a range of applied fields (criticality safety, reactor operations, etc…)
Approach:
Project is conducting the first set of self consistent irradiations of major actinides in nearly 30 years using:
Long irradiations with fission chambers for an absolute fission basis estimate of yields
Long irradiations of high purity mixed foil sets for cross-section measurements
Prompt (< 60 μs) fission neutron bursts for relative fission yield measurements
High quality nuclear data essential to data evaluation and modeling;
Improve nuclear data libraries
Provide valuable nuclear data references for the nuclear science community

## Slide 4: Neutron Sources
Flattop (NCERC)
Fast/fission Spectrum
Horizontal (“traverse”) glory hole
1013 fissions/g on samples
Godiva IV (NCERC)
Fast/fission neutron spectrum
Super-Prompt Critical Operations
Vertical glory hole for samples
1-4 1016 Total Fissions / burst
D-T Generator (PNNL)
Thermo D711 neutron generator
Low scatter facility at PNNL
Max neutron flux of n/cm2/s
New D-T source at LLNL Jan-2022
Cumulative FPY Task
Days to weeks post irradiation
Short-Lived FPY Task
Hours to days post irradiation
Cumulative FPY Task
Days to weeks post irradiation
Operations conducted at the NCERC include both subcritical and critical experiments with the ability to measure a wide variety of nuclear properties.

## Slide 5: Time scales of isotopes we can investigate
Fission product isotopes cover a wide range of time scales from microsecond to day++ half-lives.
We can currently make measurements:
At the 10s of minutes time scales by whole gamma counting
Hours/days by performing radiochemistry and beta/gamma counting
11.5 s
40.8 s
285 d
17.3 m
3.15 m
15.2 m
50.5 d
23.4 m
2.36 d
2.4E4 y

## Slide 6: Short-Lived Fission Product Yields (SLFPY)
Photo & Model of Godiva
Godiva Irradiation Pulse Width
Godiva Neutron Fluence-energy Distribution & Covariance Matrix
Nuclear Data Sheets 155, 86 (2019).
Nuclear Data Sheets 163, 249 (2020).
Temporal Assay of 134I
Fabricate High Quality Targets
Pulse Irradiate at NCERC
Acquire 𝛾 spectral data
Publish Fission Yields in Nuclear Data Sheets for NNDC
Symmetric Temporal Spectral Analysis (LLNL)
Asymmetric Temporal Spectral Analysis (PNNL)
Evaluate Neutron Fluence & Fissions

## Slide 7: Np237 Data Time Dependent Spectra Example
Currently, we can retrieve the sample from Godiva ~30-40 minutes after the burst mode operation. Then begin measuring gamma-ray spectra at about 1 hour.
Fit a peak in each in time bin and plot the intensity versus time (decay curve)
  Use half-life and -ray energy to identify isotope
Use decay curve to extract the activity of the isotope immediately after irradiation
Courtesy Sean Burcher

## Slide 8: Technical Approach: identifying gamma rays Time dependent gamma ray spectra from 45 minutes to 7 days post-irradiation
8
8
Counts per hour
Persistent line
Short half-life
Grow-In daughter product
List mode data taken with high resolution HPGe detectors to perform the gamma-ray spectroscopy is essential to unfolding the very complex spectra obtained from fission products.

## Slide 9: Np237 Results : Example 93Y
Observed 3 ‘clean’ -rays from the decay of 93Y
Extrapolate Decay Curve fits back to irradiation time :
  Correct for DAQ livetime, detection efficiency, and self-attenuation
Courtesy Sean Burcher

## Slide 10: Results for 237Np FPYs
Fission Product yields for 45 unique isotopes/isomers have been measured
  Using 191 different -rays
  Isomer Yields
Half-lives ranging from 10s of minutes to a few days.
Use multiple -rays from each decay if possible
  Reduces sensitivity to systematic uncertainties introduced by potentially imprecise nuclear data

## Slide 11: Results for 237Np FPYs : Investigating Nuclear Data
Using multiple -rays can highlight areas where current evaluated branching ratios may be incorrect
Example: 129Sb
  Using the 761.3 keV -ray to measure FPY would produce a different result
  The other 3 observed -rays produce a consistent value for FPY
Indicates that there could be an issue with the branching ratio for the 761.3 keV -ray
  In this case it appears that the ENSDF/B VIII.0 FPY value was measured using the 761.3 resulting in an inaccurate FPY

## Slide 12: Past Results from 235U, 238U, 239Pu
 | ENDF VII.0/B |  | Small Target |  |  | Large Target |  | 
Isotope | FY | ± | FY | ± | Ratio | FY | ± | Ratio
Kr-85m | 0.59 | 0.01 | 0.58 | 0.03 | 0.98 | 0.62 | 0.03 | 1.05
Rb-89 | 1.72 | 0.07 | 1.69 | 0.08 | 0.98 |  |  | 
Y-93 | 3.82 | 2.45 | 3.58 | 0.29 | 0.94 | 3.36 | 0.25 | 0.88
Y-94 | 4.22 | 0.06 | 4.13 | 0.19 | 0.98 |  |  | 
Mo-101 | 6.67 | 0.27 | 6.37 | 0.29 | 0.96 |  |  | 
Ru-105 | 5.36 | 0.21 | 5.51 | 0.25 | 1.03 | 5.52 | 0.25 | 1.03
Rh-107 | 3.22 | 0.52 | 3.19 | 0.16 | 0.99 |  |  | 
Sb-127 | 0.50 | 0.16 |  |  |  | 0.530 | 0.02 | 1.06
Sn-128 | 0.79 | 0.51 | 0.64 | 0.03 | 0.81 | 0.75 | 0.07 | 0.94
Sb-129 | 1.45 | 0.12 | 1.49 | 0.07 | 1.03 | 1.32 | 0.06 | 0.91
Sb-131 | 2.89 | 0.32 | 1.87 | 0.09 | 0.65 |  |  | 
Te-131 | 3.11 | 0.50 | 4.72 | 0.74 | 1.52 |  |  | 
Te-131m | 0.92 | 0.41 | 1.52 | 0.08 | 1.66 | 1.28 | 0.06 | 1.39
I-131 | 3.88 | 0.04 | 3.18 | 0.23 | 0.82 | 4.09 | 0.19 | 1.06
Te-132 | 5.15 | 0.10 | 5.49 | 0.25 | 1.07 |  |  | 
I-133 | 6.91 | 4.42 | 6.28 | 0.30 | 0.91 | 6.83 | 0.32 | 0.99
Te-134 | 4.79 | 0.29 | 3.60 | 0.16 | 0.75 | 3.46 | 0.23 | 0.72
I-135 | 6.08 | 0.24 | 5.84 | 0.26 | 0.96 | 5.92 | 0.27 | 0.97
Xe-138 | 4.71 | 0.09 | 4.36 | 0.22 | 0.93 |  |  | 
Cs-139 | 5.37 | 0.43 | 4.36 | 1.06 | 0.81 |  |  | 
Ba-139 | 5.61 | 0.11 | 5.88 | 0.39 | 1.05 | 6.44 | 0.55 | 1.15
Ba-140 | 5.32 | 0.07 | 5.66 | 0.70 | 1.06 | 5.02 | 0.23 | 0.94
Ba-141 | 5.08 | 0.30 | 4.90 | 0.22 | 0.97 |  |  | 
Ce-141 | 5.15 | 0.14 |  |  |  | 4.57 | 0.21 | 0.89
Ba-142 | 4.48 | 0.49 | 3.82 | 0.21 | 0.85 |  |  | 
La-142 | 4.75 | 0.07 | 5.17 | 0.23 | 1.09 | 5.12 | 0.23 | 1.08
Ce-143 | 4.34 | 0.02 | 3.59 | 0.17 | 0.83 | 4.09 | 0.18 | 0.94
Ce-146 | 2.42 | 0.10 | 1.81 | 0.11 | 0.75 |  |  | 
Nd-147 | 1.99 | 0.03 |  |  |  | 1.77 | 0.09 | 0.89
Pr-147 | 1.99 | 0.06 | 2.01 | 0.14 | 1.01 |  |  | 
Nd-149 | 1.24 | 0.02 | 1.23 | 0.06 | 0.99 | 1.18 | 0.06 | 0.95
Pm-151 | 0.78 | 0.01 |  |  |  | 0.73 | 0.05 | 0.93
Sm-153 | 0.43 | 0.03 |  |  |  | 0.43 | 0.02 | 1.01
235U FY
238U FY
Preliminary 239Pu FY
Highlighted in GREEN are improved measurements

## Slide 13: Integral Measurement 237Np(n,)238Np Cross Section
-rays from the decay of 238Np were observed in the time dependent spectrum
Activity of 238Np was used to determine the amount of 238Np produced during the irradiation

## Slide 14: NCERC Flattop assembly irradiation and modeling to evaluate the 9Be(n,g)10Be cross section at fission energies Courtesy of Jack Goodell, Jennifer Church and Bryan Bandong
High-fidelity model of the Flattop assembly and experimental configuration simulated using MCNP6.2
9Be(n,g)10Be integral cross section determined by total neutron fluence and the 10Be/9Be ratio
Neutron fluence estimates determined by 197Au(n,g)198Au analysis
10Be/9Be ratio measured by accelerator mass spectrometry
Preliminary 9Be(n,g)10Be integral cross section results do not agree with current evaluated libraries
CAMS assay
*From Corey Keith - LANL
Foil Configuration
MCNP Visualization of the Flattop Model
9Be(n,g)10Be or 10Be production: JANIS-NEA/EXFOR
*X-error bars represent width of neutron distribution; symbol at average neutron energy
= Total fluence (n/cm2) from 198Au fluence estimates
[1]
[1] Wallner et al. Phys Rev C 99, 015804 (20129)
Simulated neutron fluence softens and decreases with distance from center of the assembly
LLNL Center for Accelerator Mass Spectrometry (CAMS)
CENDL-3.2
BROND-3.1
JEFF-3.3
ENDF/B-VIII.0
TENDL-2019
JENDL-4.0u
EAF-2010
1 µb
100 µb

## Slide 15: We are aiming to return to Oregon State University Jan-2022 to perform the short time scale U238 irradiations
Rabbit shuttle injection station
OSU TRIGA reactor pulsed

## Slide 16: Reports with compendia of results for SLFPY
“Interim Report on Fission Product Yields from the Irradiation of Np237 using the Godiva Critical Assembly”, S. Burcher et al. Sept. 2020 LLNL-TR-1023214
“Report on Short-Lived Fission Product Yields from Pu239”, S. Padgett et al. LLNL-TR-799578 Dec 2019
“Interim Report on Short-Lived Fission Product Yields from U238”, J.T. Burke et al. LLNL-TR-738508 Sept 2017
“Interim Report on Short-Lived Fission Product Yields from U235”, J.T. Burke et al. LLNL-TR-704065 Sept 2016
“Improved Cumulative Fission Yield Measurements with Fission Spectrum Neutrons on 235U,” Nuclear Data Sheets, 155, 86–97, Jan. 2019, doi: 10.1016/j.nds.2019.01.005
“Improved Cumulative Fission Yield Measurements with Fission Spectrum Neutrons on 238U,” Nuclear Data Sheets, 163, 249–260, 2020, doi: 10.1016/j.nds.2019.12.006.

## Slide 17: Cumulative Fissions Product Yields and the R-Value
An R-value is the ratio of the yield of a FP () to the yield of 99Mo () in an unknown, relative to the same FP ratio from thermal fission ( =th) of 235U ().
Developed in the late 40’s such that a number of calculational inputs cancel out, such as .
G.P. Ford and A.E. Norris, LA-6129 (1976)
H.D. Selby, et al., Nucl Data Sheets 111, 2891 (2010)
M.B. Chadwick, et al., Nucl Data Sheets 111, 2923 (2010)
J. Laurec, et al., Nucl Data Sheets 111, 2965 (2010)
Notes: The fission product mass distribution is a function of the fissioning nucleus and the neutron energy causing fission

## Slide 18: Execution
Target preparation
  Actinides for FPY measurements by:
    Direct counting
    Radiochemistry
  Stacked foils for integral cross-section measurements in- and ex-core
Irradiation at NCERC & Other (NNSS/DAF)
Sample assay @ NCERC
  LANL/LLNL counting facilities (HPGe coincidence)
Sample shipping (from NNSS/DAF to labs)
  Assay by gamma & beta
  Post assay of list-mode data
Outlier | ENDF/B | LANL | PNNL
111Ag (b) | 1.76 | 2.76 | n/a
111Ag (g) | 1.76 | n/a | 3.30
136Cs (b) | 0.69 | 2.22 | n/a
136Cs (g) | 0.69 | n/a | 2.47
153Sm (b) | 1.08 | 1.28 | n/a
153Sm (g) | 1.08 | 0.95 | 1.20

## Slide 19: Cumulative Fission Product Yield Sample Preparation
Sample preparation (can involve more than one lab)
  Select stock material and determine/verify chemical and isotopic composition
  Actinides, e.g. 233U, 235U, 238U, 237Np, 239Pu, in 100s of milligram quantities
  Geometric characterization of all target foils (mass and dimensions)
  Sample containment prior to shipping (containment of Pu samples is part of the NPML)
Sample shipping NCERC
  Current experimental activities involve multiple actinide (SNM) samples

## Slide 20: Cumulative Fission Product Yields: Previous work
Experimentally determined R-values for 235U in the center position of Flattop compared to R-values calculated from ENDF/B-VII.1 fission product yields for 0.5 and 14 MeV incident neutrons.
The lower panel shows the absolute difference between the experimental values determined by b counting (black circles) and g counting (red circles) and ENDF/B-VII.1.
Previous measurements on the Flattop assembly
235U, 238U, 233U, 237Np and 239Pu (no fission chambers)
235U, 237Np (prototype fission chambers)
Outlier | ENDF/B | LANL | PNNL
111Ag (b) | 1.76 | 2.76 | n/a
111Ag (g) | 1.76 | n/a | 3.30
136Cs (b) | 0.69 | 2.22 | n/a
136Cs (g) | 0.69 | n/a | 2.47
153Sm (b) | 1.08 | 1.28 | n/a
153Sm (g) | 1.08 | 0.95 | 1.20

## Slide 21: Results For Experiments #4253 and 4256 (HEU)
Comparison of current R-value results with R-values calculated from ENDF/B-VII.0 cumulative fission product yields for fission of 235U from 0.5 (fission) and 14 MeV neutrons.
Difference, , between R-values determined from the high-power run (H) and those calculated for ENDF fission (n = ENDF) and from the low-power run (n = L).
There is very good agreement between both data sets and ENDF for peak yield fission products, where we expect to see little fluctuation with incident neutron energy. However, differences can be seen in the valley and high mass wing.

## Slide 22: Results For Recent Experiments #4510 (PNNL DU), #4512 (LANL DU)
Irradiation of DU at NCERC on Flattop in April 2021, samples split between LANL and PNNL.
Comparison of R-values determined through whole A-solution or radiochemical separations performed by LANL and PNNL on a DU compared ENDF.V.III.0
There is excellent agreement between the two laboratories and calculated ENDF values with some notable improvements to R-value uncertainties
  91Y, 136Cs
LANL 4512 DU
PNNL 4510 DU ENDF DU

## Slide 23: Fission Chamber Performance
Pulse height spectra from the Mark II fission chamber
Benchtop testing with 252Cf
Testing at MIT with 235U
Both using P-10 fill gas
Data taken with an Amp-Tek MCA8000D Pocket MCA
100V/90PSI
235U(n,f)
300V/90psi
235U(n,f)
Light
Heavy
Alphas
MIT Nuclear Reactor Laboratory
Data taken with a CAEN DT5781 Desktop MCA
Heavy
Light
Notes: Benchtop testing with 252Cf (~3500 Bq alpha at time of measurements) reference foils
~23 hour acquisition
MIT NRL testing with U(93) reference foils
~1 hour acquisition

## Slide 24: Results
MIT FC Tests 9-13-21 (½ gap)
The red curve is “zero” threshold. The black curve is the same settings used during the Flattop irradiation in April.
Need to confirm with 252Cf, then correct detector efficiency for the high threshold.
Isotope | Beta or gamma | R | ±% | Atoms/g target | ±% | Notes
89Sr | B | 0.921 | 2.4 | 3.15E+10 | 2.2 | 
91Y | B | 0.888 | 4.6 | 3.75E+10 | 4.5 | 
95Zr | G | 0.973 | 3.8 | 4.58E+10 | 3.0 | Beta analysis - within one s
97Zr | G | 0.986 | 3.8 | 4.27E+10 | 3.1 | Beta analysis - within one s
99Mo | B | 7.24E+11 | 2.2 | 4.43E+10 | 2.2 | R- value column used to report fissions/g target
111Ag | B | 2.79 | 2.9 | 3.52E+08 | 2.8 | 
115Cd | B | 3.15 | 3.8 | 2.65E+08 | 3.7 | 
115mCd | B | - | - | - | - | Too few counts to fit beta data with confidence
136Cs | G | 2.28 | 5.7 | 9.81E+07 | 5.2 | 
137Cs | G | 1.07 | 3.6 | 4.81E+10 | 2.8 | 
140Ba | B | 0.904 | 2.7 | 4.07E+10 | 2.5 | Beta analysis - within one s
141Ce | - | - | - | - | - | Incomplete analysis
143Ce | - | - | - | - | - | Incomplete analysis
144Ce | - | - | - | - | - | Incomplete analysis
147Nd | B | 0.927 | 6.9 | 1.51E+10 | 6.8 | A beta 'no absorber' measurement, within 1 s of the beta 'with absorber and gamma measurements
153Sm | B | 1.33 | 10.7 | 1.29E+09 | 10.6 | High uncertainty driven by low gravimetric yield
156Eu | B | 1.59 | 6.3 | 1.72E+08 | 6.2 | 
161Tb | - | - | - | - | - | Analysis not attempted
Radiochemistry Results (R-values)
HEU Low-power Irradiation
+

## Slide 25: Fission Product Yield Evaluations
Data from this and other projects will feed into a new FPY evaluation that will happen over the next few years.
Regular interactions with another NA-22 funded multi-lab project “Evaluation of Energy Dependent Fission Product Yields”
  LANL (leading lab) develops FPY models and produce the final FPY data files
  BNL compiles experimental FPY data and produces a set of recommended FPY values, performs FPY data validation calculations
  LBNL performs measurements of energy-integrated and differential CNAA (Cyclical Neutron Activation Analysis) using the intense neutron source by the LBNL cyclotron, and data interpretation by the FIER code
  PNNL develops a new Bragg curve-based fission TPC (Time Projection Chamber) analysis in collaboration with LANL and LLNL
  LLNL develops theories and methods to calculate primary fission fragment yields, and performs FREYA calculations for prompt decay
The theory effort draws on the experimental results of several experimental activities funded by federal agencies through the Nuclear Data Interagency Working Group

## Slide 26
Thanks for your time and attention.
Contact info for team members who can help with questions:
harke2@llnl.gov - SLFPY
toddb@lanl.gov – CFPY/rad-chem
friese@pnnl.gov – CFPY/rad-chem
bandong1@llnl.gov - AP
bruce.pierson@pnnl.gov - SLFPY
church4@llnl.gov – AP
tonchev2@llnl.gov – SLFPY – mono-energetic TUNL