## Slide 1
nHCAL
TBD
cHCal TBD
ANL
We need to figure out how many layers in HCals sufficient for ‘good’ (need to be defined) identification of neutral hadrons. bECal configuration is very important for that.
(Different versions of the detector, bECal dense post-imaging part of the detector)
plot efficiency of identification of NH vs number of layers
vs thickness of layers, i.e. 2 cm Fe, 4 cm Fe <- Cost reduction
study dependency of efficiency vs registration threshold. <- Requirements on LY
find optimal method of combining ECal and Hcal clusters for hadrons. (weighted sum)
Check reconstruction in dd4hep
Study effects of noise, digitization etc.
Please let us know if you are interested to work on this. Contact Paul, Vladimir or Oleg.
Open Calorimetry Tasks.
Barrel Hcal and nHcal need to be optimized.
The main functionality of these two detectors is to identify neutral hadrons.
Thick magnet coils beween bEMCal and bHCAL. Sufficient to instrument about 2 interaction length only for bHCal.
Both HCals implemented in dd4hep as a sandwich 2 cm thick Fe, 5 mm thick Sc.
Granularity 10 cm x 10 cm.
Single particle data files were generated

## Slide 2
Open Calorimetry Tasks. Barrel Calorimeters.
We want to design ATHENA calorimeters with ML/AI capabilities in mind. <- generally requires high granularity and segmentation, but this need to be optimized vs cost.
Barrel Calorimeter System
bECAL hybrid, Imaging layers + WScFi (GLUEX/KLOE type)
bHCal KLM Type. Re-using Sc. Tiles from STAR BEMC, and read each tile separately with SiPM.
Optimization need to be done for the whole system, for all probes we are interested.
Example e/h will benefit from better resolution of bECal which require large sampling fraction -> lead to smaller number of interaction length before coils. For jet measurements it will be better to have as ‘thick’ as possible Ecal -> small sampling fraction.
Granularity of WScFi section beyond imaging layers need to be optimized for neutral hadron pattern recognition/ shower separations.

## Slide 3
Possible optimization tasks for Barrel ECAL
Optimization of the clustering parameters for imaging calorimeter layers - Efficiency of clustering as a function of energy and angle for different particle types (electron, gamma, + pions) for different clustering algorithm parameters (min nb of hits, min Energy, distance to neighbor). (observables to study: number of clusters, energy of cluster, phi, eta, threshold energy for particles to reach the barrel).
Optimization of the clustering parameters for ScFi calorimeter layers - same as above for ScFi clusters
Improving the energy correction for em showers in Barrel - energy calibration: looking at energy response from electrons, photons with different energies with the current energy correction and extracting correction factors as a function of energy (e.g., energy losses in ScFi layers), eta, maybe particle type. These new energy correction parameters are not implemented into the reco algorithms yet, so this would be the input for the implementation.
Optimizing parameters for the merging clusters from ScFi and Img clusters - clusters are merged based on their phi position and energy reconstructed from ScFi and Img clusters (observables to study: number of merged clusters for different Delta Energy, Delta Phi as a function of energy, angle, particle type; studying typical differences between reconstructed energy, cluster phi, number of clusters from ScFi and Img layers and applying it to the algorithm). The simplified algorithm is currently implemented, and this studies will be an input to improve it.