## Slide 1: Effects of ion-electron focusing on cooling performance, ion heating and lifetime
D. Kayran, A. Fedotov, P. Inacker, K. Mernick, S. Seletskiy, He Zhao, others
APEX workshop
November 9, 2021
BNL

## Slide 2: Motivation:
In high energy bunched electron coolers, the electron bunches are typically much shorter than the hadron bunches
In order to more equally redistribute cooling several electron bunches per one hadron bunch is considered
For example,
  At LEReC we used 30-36 bunches between equally distributed along the 10 ns rms ion bunch
  a schema of using two electron bunches located at +/- rms length of the proton bunch is proposed to pre-cool protons at energy 25 GeV for EIC
Hadron bunch intensity is higher than electron bunch intensity. Hadron space charge focusing to the electron bunch could be significant during interaction on the cooling section
Due to non uniform longitudinal distribution different parts of the ion bunch effect differently to the different electron bunches
This experiment is important to learn how to optimize the cooling of high-intensity high-energy ions (or protons) by finding the proper balance between cooling/heating/lifetime
Time structure of two electron bunches synchronized with a single proton bunch
*A. Fedotov., Low energy cooling for Electron Ion Collider. BNL-220686-2020-TECH EIC-HDR-TN-01 https://technotes.bnl.gov/PDF?publicationId=220686
Electron angles in the cooling section produced by beam emittance and proton space charge for cooling at 23.8 GeV for two possible electron bunch profiles. *)

## Slide 3: Some system limitations:
LEReC pulse selection system cannot produce the MB or gap length shorter than 9b (<12.6 ns)
  If shorter (5b) MB is desirable It requires significant development time (may be after RHIC run at this energy)
We could compare 36b vs 20b with the about the same bunch charge 30pC*36*56%=35pC*20*88%
Or 10b-10g-10b (49% efficiency) vs 10b (~100% efficiency)
  In order to run 10b in the center we can shift 10-10-10 configuration by 10b then the second MB of 10b will not interact with RHIC bunches
  Could be done through LLRF laser-timing pet page.
36 bunches, interaction efficiency ~56%
10b-10g-10b, interaction efficiency ~49%
20 bunches, interaction efficiency ~88%
10b-10g-10b (shifted by10), interaction efficiency ~50%
Proposed for the APEX

## Slide 4: APEX on June 24, 2021
Before APEX time prepare necessary laser pulse structure
RHIC was setup to use only 9MHz due to limited time we used only parabolic RHIC longitudinal profile
In pulsed mode check MB energy distribution (energy spread) of all configurations: 36b, new 20b and 10b-10g-10b.
At low intensity conduct cooling/heating/lifetime measurements for 20b, 10b-10g-10b and 10b-10g-10b shifted
Using regular parabolic ion bucket with close to nominal RHIC operation intensity, optimize CS solenoids to reduce overfocusing of e-bunches setting at the rms size of the ion.
  Compare results for : centered position vs 10ns shifted position cooling efficiency
http://www.cadops2.bnl.gov/elogs/entryList.jsp?DATABY=day&ELOG=LEReC&DATE=06/24/2021&DIR=none#1481294
We used about 2 hours 6pm-7:45pm
In green is shown longitudinal area of 50.4 nsec covered by LEReC nominal operation (36b per 1 MB)

## Slide 5: Experiment timeline
Bunch pattern setup,
bunch quality measurements
in pulsed mode
6mA, 20b
12mA, 20b
12mA
10b10g10b
12mA/2
10b centered
IBS only
IBS only
IBS only
Back to nominal 12mA, 36b

## Slide 6: Laser/timing system setup
36b
20b
10b10g10b gap is centered
10b10g10b one half of the MB is centered
Magenta trace: IR laser photodiode envelope signal. It defines LEReC CW operation bunches time structure.
Green trace: Green laser photodiode signal.
Cyan trace: Yellow Cooling section BPM signal to check RHIC vs LEReC bunches longitudinal alignment
Yellow trace: GunFCT signal. It shows 0 since no LEReC beam was generated during the setup shutter was closed.

## Slide 7
36 bunches, interaction efficiency ~43%
10b-10g-10b, interaction efficiency ~31%
20 bunches, interaction efficiency ~68%
10b-10g-10b (shifted by10), interaction efficiency ~46%
APEX June 24, 20219 MHz only
36 bunches, interaction efficiency ~56%
10b-10g-10b, interaction efficiency ~49%
20 bunches, interaction efficiency ~88%
10b-10g-10b (shifted by10), interaction efficiency ~50%
Original Propose for the APEX 9MHz +28MHz

## Slide 8
Time
For the same average laser power (or beam current) the individual bunch charge using 20b/MB is 1.8 times higher then during optimum operation using 36b/MB.
As a result, beam quality was not as good as at the optimized LEReC operation condition
We didn’t have time to optimize beam quality for the higher than nominal operation charge. Instead, we decided to proceed with APEX studies.
Nominal 36b per MB, 1.2 nC
20b per MB, 2 nC
Energy
Energy
Time
Time
Longitudinal phase space measurements
APEX settings
20b per/ MB, 1.2 nC
Energy
Time

## Slide 9: Heating, cooling comparison for different LEReC bunch time structure
20b
10b10g10b gap is centered
FWHM bunch Length
WCM
Transverse bunch size Size
H-jet
Weaker cooling
Heating
Cooling
Heating
Cooling
Heating
IBS
IBS
We used ion bunches at low intensity and LEReC at average current of 12 mA (it corresponds to 1.3 nC per MB or 64pC per single bunch )
10b10g10b 10b is centered
Cooling

## Slide 10: Recombination signal observations
cooling
heating
cooling
heating
No LEReC
Recombination signal 3 times stronger in case of 20b
20b
10b10g10b
10b centered
10b10g10b and 10b in the center give the same recombination signal
cooling
cooling
heating
10b-10g-10b, efficiency ~31%
10b-centerd efficiency ~46%
20 bunches, interaction efficiency ~68%
10b10g10b
Matched/mismatched energy
4keV

## Slide 11: Closer look to the last two settings
10b10g10b
Half of the MB (10b) centered
10b-10g-10b, interaction efficiency ~31%
10b (centered), interaction efficiency ~46%
Heating
Cooling
Cooling
Heating
IBS
Cooling and heating rates are comparable for these two cases

## Slide 12: Measure rates
10b10g10b, 12 mA
10b centered, 12 mA
20b, 12mA
20b, 6 mA
Observation:
Energy Unmatched (4keV) LEReC bunch has:
significant effect on transverse ion bunch size growth (“heating” previous talk)
Cooling by using hollow MB is weaker then regular 20b pattern due to less effectively LEReC/RHIC bunches overlapping
Transverse cooling is less efficiently in case of using 10b with offset vs 10b centered to theion bunch.
Ions at smaller longitudinal amplitude less likely interacts with electrons

## Slide 13: Cooling rates
LEReC current | MB charge | MB pattern | Overlapping efficiency | Effective charge | [min] | 
 |  |  |  |  | Trans. | Long.
6 mA | 645 pC | 20b | 68% | 438.7 pC | 18.2 | 14.6
12 mA | 1290 pC | 20b | 68% | 877.4 pC | 9.7 | 7.3
12 mA | 1290 pC | 10b10g10b | 31% | 400.0 pC | 19.7 | 12.9
12 mA | 1290 pC | 10b centered | 46% | 593.5 pC | 16.6 | 19.1
LEReC current | MB charge | MB pattern | Overlapping efficiency | Effective charge |  | 
 |  |  |  |  | Trans. | Long.
6 mA | 645 pC | 20b | 68% | 438.7 pC | 18.2 | 14.6
12 mA | 1290 pC | 20b | 68% | 877.4 pC | 9.7 | 7.3
12 mA | 1290 pC | 10b10g10b | 31% | 400.0 pC | 19.7 | 12.9
12 mA | 1290 pC | 10b centered | 46% | 593.5 pC | 16.6 | 19.1
Transverse cooling is more efficient for centered pattern (long or short MBs)
Longitudinal cooling is more efficient for hollow MB

## Slide 14: Plans
10b-10g-10b, interaction efficiency ~1%
20 bunches, interaction efficiency ~26%
10b-10g-10b (shifted by10), interaction efficiency ~25%
During run 2022 only 28 MHz is available.
Expected Ion bunches are 3 times shorter (<5 ns RMS) than it was during the run 2021
14nsec
14nsec
28 nsec
Setup RUN22 with 28MHz only
Then MB length (numbers of pulses per MB) should be reduced in order to have good setup for the “two bunches” experiment or “short bunch at the sigma distance from the center”
Significant modification of the laser pulse picking system is needed in order to produce shorter MBs (~5b per MB )
We might consider such modification after all other LEReC relative experiments are finished

## Slide 15: Summary
We were able to cool ions using significantly shorter MBs than length of the ion bunches in two configurations : 2 short MBs at the edges of the Ion bunch and one short MB aligned with center of the ion bunch
Cooling rate is well correlated with effective overlapping charge
As expected, cooling was stronger when we use the same intensity long MB due to better bunches overlapping

## Slide 16: Back-up slides

## Slide 17: Beam loading effect difference: normal 36b per MB vs hollow MB (by K. Mernick)
Using just 9MHz cavity, we cannot compensate hollow MB energy spread as effective as in case of the normal 36b per MB.
For this pattern, we would really need a combination of harmonics (9, 18, 28 MHz) to compensate the beam loading well.