## Slide 1: Broad band impedance measurement
Michael Blaskiewicz
RHIC APEX meeting 22 Oct 2021

## Slide 2: Outline
Why we need these measurements.
Previous longitudinal impedance measurements
Previous transverse impedance measurements
This proposal
We need these measurements to help design the EIC.
Both the longitudinal and transverse impedances of RHIC are significantly larger than the design values and the values in the two rings are quite different.
While we plan on doing a careful impedance budget for the EIC we need to make sure we do not miss anything important.

## Slide 3: RHIC longi impedance
Larger slopes for low lying modes ascribed to collective effects.
For longi measurements see: M. Blaskiewicz, J.M. Brennan, K. Mernick, IPAC2015, p746 (2015).

## Slide 4: RHIC transverse impedance
Transverse Measurements in N. Biancacci et. al. IPAC2014, p1730 (2014).
They found 14MΩ/m for rigid bunch mode at injection in blue ring, 3 MΩ/m in yellow.
Beam transfer functions were measured at injection at 250 MHz in blue ring with much help from K. Mernick and the operations crew.
Data are shown.
The emittance changed with intensity
keeping ΔQsc fixed, so Zsc was varied
in sims.
Best fit gave 10 MΩ/m which was
4 or 5 times bigger than Zsc= 0 result.
Variation of amplitude with intensity
is not understood.
10 .vs. 14 seems OK.
For EIC used a resonator
10MΩ/m, fres=5GHz, Q=2

## Slide 5: This proposal
Notice that the resonator model has three parameters.
All previous measurements have constrained the impedance at low frequency, yielding a single number.
Frequency information would be valuable.
It is likely that the broad band impedance has a frequency scale of GHz, so variations might be observable over the bandwidth of the stochastic cooling system.
Space charge is a big complication, so measurements at high energy are preferred.

## Slide 6: Specifics
Use Gold or similar heavy ion so stochastic cooling is set up.
Fill RHIC with 4 or 5 adjacent bunch trains of different intensity.
Accelerate to top energy, probably rebucket. This might require work on the beam feedback systems.
Gate the stochastic cooling pickup/kicker to each train.
Measure open loop beam transfer functions with the least upstream filtering possible. However, without SC we have limited time to work so doing measurements over short intervals with cooling nominally on is attractive.
There are 16*6=96 cavities, each with its own BTF. This is a lot.
I need to work with K. Mernick to find out how much surgery is required on the stochastic cooling system to do this and find a compromise that makes it reasonable.
The other theorists and I need to do some estimates of the signals we expect before using any beam time.
I suspect the experiment will take a few shifts.