## Slide 1
Progress on AE85
A Multiatmosphere CO2 Amplifier Optically Pumped by a 4.3 mm Fe:ZnSe Laser
Funded by DOE HEP Accelerator Stewardship Program 2020-2023
SERGEI TOCHITSKY-PI, Dana Tovey, Jeremy Pigeon, Chan Joshi
Department of Electrical Engineering, UCLA
Igor Pogorelsky, Mikhail Polyanskiy
Brookhaven National Laboratory, USA
Sergei Mirov et al
University of Alabama at Birmingham

## Slide 2
Motivation
  Long-wavelength Infrared range is attractive for particle acceleration and radiation generation. At present we experience a Renaissance of mid-IR ultrafast lasers mainly based on OPA and OPCPA in nonlinear crystals pumped at 1-2 mm.
  CO2 laser is efficient and is able to store a great deal of energy within the active medium. The shortest pulse demonstrated so far is ~2 ps and all high-power picosecond systems operate in a single-shot regime limited by electrical discharge stability in a >10 atm molecular gas.
  In AE85 experiment funded by the DoE grant, we study potential of Optically Pumped CO2 laser technology for production of ≤1 ps pulses at a high-repetition rate. A collaborative effort of UCLA/BNL (gas lasers) built around the state-of the art mid-IR solid-state lasers developed at UAB.
ATF User’s 2021

## Slide 3
10.4
10.6
10.8
11
0
0.2
0.4
0.6
0.8
1
Normalized Gain
1atm
10.4
10.6
10.8
11
Wavelength (
m
m)
CO
2
Gain Spectrum
10atm
10.4
10.6
10.8
11
20atm
Recipe for success: High-gain CO2 laser
Population of 001 level Maximized
Population of 100 level Minimized
Optically Pumped CO2 Laser
Normalized Ampl..
Wavelength (mm)
~1.2THz
CO2 Molecule
ATF User’s 2021

## Slide 4
Modeling of Picosecond Pulse Amplification
4.3 mm
Fe:ZnSe
Laser
10-15 atm
Isotope CO2
Amplifier
10 mm pulses
300-500 fs
10 GW
10 mm
300 fs
OPA
Seed
Feasibility study of a compact GW class CO2 amplifier and gain dynamics.
D. Tovey et al. Appl. Opt., 58, 5756, 2019, J Appl. Phys. 128, 103103, 2020
ATF User’s 2021

## Slide 5
Group of Prof. S. Mirov
Tunable 3.9-5 mm Fe:ZnSe source for
Optical Pumping of the CO2 laser at 3 Hz
ATF User’s 2021

## Slide 6
Optically Pumped High-pressure CO2 Laser
High pressure CO2 cell
Dichroic mirror
(T = 99% for 4 μm,
R = 99.5% for 10 μm)
NaCl window
Focusing lens
Dichroic mirror
4.3 μm pump pulse
10 μm cavity
Detector
10 μm filter
ATF User’s 2021
9.3 mm
4.3 μm pump
9.3 mm
10 μm lasing
15 atm

## Slide 7
  Measurements of lasing and gain of a high-pressure optically pumped CO2 laser
  >10% efficiency near 10 atm
  >10% small signal gain
  Can be scaled to 1 KHz – limited by gas dynamics
High-pressure optically pumped CO2:
Lasing up to 15 atm pressure
Neptune Laboratory
ATF User’s 2021
With >35 mJ absorbed in the multiatmosphere CO2 cell, >3 mJ in a 10 mm pulse. Dana Tovey et al, Optics Express, 29, 31455 (2021).

## Slide 8
OPO Source Pumped by Nd:YAG
CO2 Cell
Amplification
Q-switched
Nd:YAG
OPO
4 μm pulse:
~50-100 mJ, 10 ns
1064 nm
OPO
2128 nm
4.256 mm
ATF User’s 2021
CO2 Cell
Amplification
Q-switched
Nd:YAG
OPO
1064 nm
1.43 m signal
4.15 mm idler
With >350 mJ, 100 MW/cm2 pump, SNLO predicts ~100 mJ, 1.43 mm signal, 30mJ 4.15 mm idler.

## Slide 9
1431 nm pumping
10 µm lasing sequence bands
4149 nm pumping
10 µm lasing regular band
CO2 Vibrational Energy Levels
Main difficulty: absorption is ~200x stronger at 4149 nm
Two-color Pumping Scheme for OP CO2 Laser
ATF User’s 2021

## Slide 10
ATF User’s 2021
Two-color Pumped OP CO2 Laser: Modeling
OPCO2 amplifier:
--1.43 µm pump: 1.5 J/cm2 fluence (2 meters)
--4.15 µm pump: 0.45 J/cm2 (10 cm)
15 atm total pressure (CO2+He)
3 atm CO2+12 atm He 10 cm-long OP cell
Dielectric mirrors R=99.8% at 1.43 mm
4.15 mm Idler
1.43 mm Signal

## Slide 11
ATF User’s 2021
High Gain OP CO2 Amplifier

## Slide 12: Experimental Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 
Laser* Only (in Laser Rooms) | 1 week | 1 week
Laser(s)* + Electron Beam |  | 
CY2022 Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 
Laser* Only (in FEL Room) | 2022-2023 5-6 weeks | 4 weeks
Laser(s)* + Electron Beam |  | 
* Laser = Near-IR or LWIR (CO2) Laser
Time Estimate for Remaining Years of Experiment (including CY2022)

## Slide 13
Summary
We have made important and necessary steps in AE85 experiment, a CO2 Laser only, funded by DOE Accelerator Stewardship Program
  Demonstrated efficient 10 mm lasing in a 15 atm CO2 cell optically by a ~50 mJ Fe:ZnSe laser. The measured gain lifetime ≤1 ms indicates that regenerative amplifier is durable.
  Next step in 2022 will be developing at UCLA a 100 mJ, 1.43+4.15 mm laser system based on NdYAG laser pumped single OPO. Design and build a 5-10 cm long cell and experiment at ATF with amplification of ~0.5 ps pulses using the CPA scheme.
  We request 2 weeks in 2022 (CO2 laser only) using front end with the CPA capability and may be the 10 mm CO2 regen.
ATF User’s 2021

## Slide 14: 2021 Activities & Impacts Associated with this Experiment (feel free to add pages as necessary)
Invited Talks:
  S. Tochitsky et al, “High-pressure CO2 laser optically pumped at 4.3 mm,” Directed Energy Annual Symposium, Albuquerque, NM, March 2021, paper 21-symp-049.
Manuscripts (books, conference and journal articles, other; please include works submitted by not yet accepted):
  Dana Tovey et al, “10 µm lasing in multi-atmosphere CO2 optically pumped by a tunable 4.3 µm laser”. CLEO 2021, Optical Society of America, STh2L.6.
D. Tovey, J. J. Pigeon, S. Ya. Tochitsky, G. Louwrens, D. Maryshkin, V. Fedorov, K. Karki, S. Mirov, I. Ben-Zvi, and C. Joshi, “Lasing in 15 atm CO2 cell optically pumped by a Fe:ZnSe laser”Optics Express, 29, 31455-31464 (2021).
J. J. Pigeon, D. Tovey, S. Ya. Tochitsky, G. Louwrens, D. Maryshkin, V. Fedorov, K. Karki, S. Mirov, I. Ben-Zvi, and C. Joshi, “Resonant nonlinear refraction of mid-IR light in CO and CO2 gas” Phys. Rev. A (2021).
S. Tochitsky and C. Joshi, “Long-Wave Infrared filamentation in air: lasers and high-field phenomena” chapter in Light Filaments: Structures, challenges and applications, ed. J.C. Diels, IET, UK, 2021
Theses awarded
  D.T. Tovey “ A compact CO2 amplifier optically pumped by a tunable 4.3 um Fe:ZnSe laser” M.Sc. 2021