## Slide 1
AE-95 Report: Optical diagnosis of Self-Modulated CO2-laser driven plasma wakes
R. Zgadzaj, James R Welch, M. C. Downer - University of Texas at Austin
M. Babzien, M. Fedurin, P. Kaur, R. Kupfer, K.Kusche, M. Polyanskiy, C. Swinson,
I. Pogorelsky, M. Palmer - Brookhaven National Lab, Accelerator Test Facility
I. Petrushina, L. D. Pinto de Almeida Amorim, M. Flament, P. Iapozzuto, Y. Jing,J. Yan, S. Kongtawong, P. Kumar, R. Samulyak, N. Vafaei-Najafabadi, V. Litvinenko - Stony Brook University
C. Zhang, W.B. Mori, C. Joshi -
University of California Los Angeles
This work is supported by the following grants:
AFOSR-MURI* grant FA9550-16-1-0013 Multi-Institution, UT lead PI - MC Downer
DoE grant DE-SC0011617 PI - MC Downer
DoE grant DE-SC0014043 PI - V. Litvinenko, CoPI – MC Downer
Rafal Zgadzaj ATF Users Meeting 2022 02 21

## Slide 2
Vision: Quasi-mono-energetic LWFAs based on large, controlled mid-IR laser-driven bubbles
λdrive= 0.8 µm (UT)
25 TW, 30 fs
injection with ∆E/E ~ 0.1% from external linac or µm-focused ionizing laser
ne/n0
ne/n0
λdrive= 10 µm
25 TW, 500fs
ne = 2e19cm-3
ne = 1 1016cm-3
AE-95 ATF Users Meeting 2022 01 18-21
simulations courtesy G. Shvets
Large blowout region
Precise and controllable injection from ATF Linac (or laser ionization AE88)
Detailed optical visualization of plasma wave structure AE95
Detailed radiographic visualization of plasma wave field AE93

## Slide 3
Vision: Quasi-mono-energetic LWFAs based on large, controlled mid-IR laser-driven bubbles
ne(ρ,ξ)/N0
ρ = kpr
ξ = kp(z – ct)
Self-Modulated LWFA
ne (cm-3)
τ (ps)
ATF CO2
Laser pulse
P (TW)
4
~1018
0.5
CO2 driver
laser
Probe
AE95
simulations:
N. E. Andreev et al.,
PR-STAB 6, 041301 (2003)
e-
Probe
55MeV, <200fs
AE93
<2
<1018
>2
Self-injected,
accelerated
Electrons
AE-95 ATF Users Meeting 2022 01 18-21

## Slide 4
nm
Jet backing pressure (atm)
Mean Thomson shift (nm)
ne= 5 1017 cm-3
Pcr = 0.4 TW
λp = 47 µm
ne = 1.8 1018 cm-3
Pcr = 0.1 TW
λp = 25 µm
0
1
2
4
8
12
0
0
10
-10
-20
-30
20
30
0
0.5
1.0
1.5
2.0
ne (1018 cm-3)
Notch filter blocking region
collective Thomson shift (nm)
CO2 laser pulse
drives SM-LWFA
ne-dependent probe spectral shifts 0.5TW, 4ps, λ=10.6µm CO2 laser pulse drives SM-LWFA
“red
zone”
upper ne
limit:
CO2 laser
reflection
from jet
4 ps, λ = 0.532 µm pulse probes wake via forward collective Thomson scatter as ne , ∆t and PCO2 vary.
Lower limit:
Notch filter
J. Welch, “Self-modulated laser wakefields driven by a CO₂ laser,”
Doctoral Dissertation, UT Austin, August 2019.
ATF solved this problem with the addition of the plasma filter in the FEL room
New narrower notch filter will be used in the future runs to reach lower densities.
AE-95 ATF Users Meeting 2022 01 18-21

## Slide 5
Onset of self modulation is observed near P/Pcrit ~ 1
~P/Pcrit
wavelength[nm]
Blocked by interference filter
Pump and Probe difference frequency
~1
Edge of notch filter blocking region has been moved closer to the probe wavelength, 532nm, by slight rotation.
ne ~ 1.3 1018cm-3
Leaked Probe spectrum
Stokes side band
AE-95 ATF Users Meeting 2022 01 18-21

## Slide 6
Probe-pump delay (∆t) shows wake decays 90% in ~10 ps, remnants visible at ∆t > 25 ps
6.67
520
525
530
535
540
544
0
-6.67
anti-Stokes
Stokes
ne = 1.5 × 1018 cm-3
notch filter
13.33
20
26.67
λprobe [nm]
∆t [ps]
average Stokes/
anti-Stokes amplitude
Probe duration deconvolved
sideband
amplitude
(arb. u.)
J. Welch, “Self-modulated laser wakefields driven by a CO₂ laser,” Doctoral Dissertation, UT Austin, August 2019.
Spectral structure
observed around
∆t ≈ 0
Simulation: Prabhat Kumar SPACE 1 code
K. Yu, R. Samulyak, “SPACE code for beam-plasma interactions,” Proc. IPAC, 728 (2015)
AE-95 ATF Users Meeting 2022 01 18-21
Cheng, R. Samulyak
SPACE code

## Slide 7
Ionization front seeds the forward Raman instability
PRE-IONIZED PLASMA
DYNAMIC IONIZATON
Simulations using SPACE1 code: P. Kumar, R. Samulyak, Stony Brook University
K. Yu, R. Samulyak, “SPACE code for beam-plasma interactions,” Proc. IPAC, 728 (2015)
P. Kumar, et al., “Simulation study of CO2 laser-plasma interactions and self-modulated wakefield acceleration”, Phys. Plasmas 26, 083106 (2019);
3D parallel, relativistic particle-in-cell code for simulating EM fields, relativistic particles, plasma & atomic processes
On-axis Ex
On-axis Ex
0
1.5
0.2
1.3
Z [mm]
-0.1
0
0.1
-0.1
0
0.1
x[mm]
x[mm]
Z [mm]
-12
0
-14
0
ne[1017cm-3]
ne[1017cm-3]
1064nm PROBE SPECTRUM
Probe spectral side bands have equal amplitudes
AE-95 ATF Users Meeting 2022 01 18-21

## Slide 8
First Demonstration of SM-LWFA in the mid-IR with upgraded CO2 laser
CCD w/objective
H2 gas jet 4mm length
ne ~ 5e16 to 5e17/cc
From CTS probe measurement
slit
Magnet
0.25T
B
Lanex
Al foil
20micron
Steel slit
CO2 laser pulse: ~2ps, 0.5J to 5J
Ref mask
AE-95 ATF Users Meeting 2022 01 18-21
Pump: w0 =20micron , 2ps, 4J
1.2 mm H2 jet, ne=7.5 1017cm-3
[1] R.A.Fonseca et al., NCS 2331, 343 (2002)
[2] K. Yu, R. Samulyak, “SPACE code for beam-plasma interactions,” Proc. IPAC, 728 (2015)
SPACE2 code
Simulation: Prabhat Kumar

## Slide 9
Example measurement of electron spot at increasing laser energy
3.2J 1.4 x 1017cm-3
1.7J 1.4 x 1017cm-3
2.4J 1.4 x 1017cm-3
1.1J 1.4 x 1017cm-3
4.8J 1.4 x 1017cm-3
CCD w/objective
H2 gas jet 4mm length
ne ~ 5e16 to 5e17/cc
From CTS probe measurement
Lanex
Al foil
20micron
CO2 laser pulse: ~2ps, 0.5J to 5J
~0.3 rad
AE-95 ATF Users Meeting 2022 01 18-21
~4J 0.9 x 1018cm-3

## Slide 10
AE-95 ATF Users Meeting 2022 01 18-21
Plasma Density [cm-3]
Laser Energy [J]

## Slide 11
Future plans
CCD
e- beam
CO2 and CTS Spectrum, mode, polarization and wavefront measurement
CO2 pulse
2TW, 2ps
532nm -> 800nm probe
Radiographic
imaging CCD
YAG xtl
H2 jet
Lanex
magnet
Extension of CTS probe range with narrower badwidth of Notch filter.
Change of probe wavelength to the Ti:Sapp generated 800nm, and subsequently to larger wavelengths (Thomson scattering, transverse shadowgraphy, frequency domain interferometry). Short pulse 800nm probe will increase temporal resolution. Moving toward longer wavelengths allows stretching optical probing sensitivity toward lower plasma densities.
Continued study of electron spectra, profiles, charge, together with optical plasma probe ( and radiographic field measurement AE93)
Conversion of setup to longitudinal injection scheme when this would become possible
Faraday rotation measurement of magnetic fields associated with SM-LWFA. Additionally, this diagnostic is more sensitive at lower densities than observation of refractive index changes, and is sensitive to presence of injected charge.
Ultimate goal is to transition to blowout regime characterization when the CO2 upgrades allow this.
Thank you!
AE-95 ATF Users Meeting 2022 01 18-21

## Slide 12
Products
J. Welch, “Self-modulated laser wakefields driven by a CO₂ laser,”
Doctoral Dissertation, UT Austin, August 2019.
P. Kumar, et al., “Simulation study of CO2 laser-plasma interactions and self-modulated wakefield acceleration”, Phys. Plasmas 26, 083106 (2019)
Kumar, P., et al., “Evolution of the self-injection process in long-wavelength
infrared laser-driven wakefield accelerators,” Phys. Plasmas 28,
013102 (2020).
R.Zgadzaj, et al., “Terawatt CO2-laser-driven plasma acceleration of electrons,” in preparation

## Slide 13
Parameter | Units | Typical Values | Comments | Requested Values
Beam Energy | MeV | 50-65 | Full range is ~15-75 MeV with highest beam quality at nominal values | 
Bunch Charge | nC | 0.1-2.0 | Bunch length & emittance vary with charge | 
Compression | fs | Down to 100 fs (up to 1 kA peak current) | A magnetic bunch compressor available to compress bunch down to ~100 fs. Beam quality is variable depending on charge and amount of compression required. NOTE: Further compression options are being developed to provide bunch lengths down to the ~10 fs level | 
Transverse size at IP (s) | mm | 30 – 100 (dependent on IP position) | It is possible to achieve transverse sizes below 10 um with special permanent magnet optics. | 
Normalized Emittance | mm | 1 (at 0.3 nC) | Variable with bunch charge | 
Rep. Rate (Hz) | Hz | 1.5 | 3 Hz also available if needed | 
Trains mode | --- | Single bunch | Multi-bunch mode available. Trains of 24 or 48 ns spaced bunches. | 
Electron Beam Requirements

## Slide 14
CO2 Laser Requirements
Configuration | Parameter | Units | Typical Values | Comments | Requested Values
CO2 CPA Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 9.2
Note that delivery of full power pulses to the Experimental Hall is presently limited to Beamline #1 only. | Peak Power | TW | 2 | ~5 TW operation is planned for FY21 (requires further in-vacuum transport upgrade). A 3-year development effort to achieve >10 TW and deliver to users is in progress. | 2
 | Pulse Mode | --- | Single |  | Single
 | Pulse Length | ps | 2 |  | 2
 | Pulse Energy | J | ~5 | Maximum pulse energies of >10 J will become available in FY20 | 5
 | M2 | --- | ~2 |  | ~2
 | Repetition Rate | Hz | 0.05 |  | 0.05
 | Polarization |  | Linear | Adjustable linear polarization along with circular polarization will become available in FY20 | Linear and circular

## Slide 15
Ti:Sapphire Laser System | Units | Stage I Values | Stage II Values | Comments | Requested Values
Central Wavelength | nm | 800 | 800 | Stage I parameters should be achieved by mid-2020, while Stage II parameters are planned for late-2020. | 800nm
FWHM Bandwidth | nm | 20 | 13 |  | 13nm
Compressed FWHM Pulse Width | fs | <50 | <75 | Transport of compressed pulses will initially include a very limited number of experimental interaction points. Please consult with the ATF Team if you need this capability. | 75fs
Chirped FWHM Pulse Width | ps | 50 | 50 |  | 50ps
Chirped Energy | mJ | 10 | 200 |  | 10mJ
Compressed Energy | mJ | 7 | 100 |  | 5mJ
Energy to Experiments | mJ | >4.9 | >80 |  | 5mJ
Power to Experiments | GW | >98 | >1067 |  | 
Other Experimental Laser Requirements
Nd:YAG Laser System | Units | Typical Values | Comments | Requested Values
Wavelength | nm | 1064 | Single pulse | 
Energy | mJ | 5 |  | 
Pulse Width | ps | 14 |  | 
Wavelength | nm | 532 | Frequency doubled | 532nm
Energy | mJ | 0.5 |  | 0.5mJ
Pulse Width | ps | 10 |  | 2-3ps

## Slide 16: Special Equipment Requirements and Hazards
Electron Beam
  Please indicate any special equipment that you expect to need, including (but not limited to) the transverse deflecting cavity, shaped bunch using mask technique, plasma capillary discharge system, bolometer/interferometer setup etc.:
CO2 Laser
  Please note any specialty laser configurations required here: polarization control
Ti:Sapphire and Nd:YAG Lasers
  Please note any specialty non-CO2 laser configurations required here: Doubled Yag and Ti:Sapphire laser beams at LWFA chamber
Hazards & Special Installation Requirements
  Large installation (chamber, insertion device, etc.):N
  Cryogens:N
  Introducing new magnetic elements: Spectrometer magnet <1T
  Introducing new materials into the beam path: N
  Any other foreseeable beam line modifications: Compressor for electron beam

## Slide 17: Experimental Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 0
Laser* Only (in FEL Room) |  | 0
Laser* + Electron Beam | 80 | 240
CY2022 Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only | 0 | 0
Laser* Only (in FEL Room) | 0 | 0
Laser* + Electron Beam | 240 | 720
* Laser = Near-IR or LWIR (CO2) Laser
Time Estimate for Remaining Years of Experiment (including CY2022)