## Slide 1: Hadron PID Considerations in ePHENIX concepts For seeding the discussion on eRD14 integration options
Jin Huang
Brookhaven National Lab

## Slide 2: Evolution of the PHENIX experiment
~2000
2017→2020
~2025
Time
Current PHENIX
sPHENIX (+fsPHENIX)
An EIC detector
14y+ operation 100+M$ investment
Broad spectrum of physics (QGP, Hadron Physics, DM)
140+ published papers to date
Last run in this form 2016
Comprehensive central upgrade base on BaBar magnet
Rich jet and beauty quarkonia physics program → nature of QGP
fsPHENIX : forward tracking, Hcal and muon ID → Spin, CNM
Path of PHENIX upgrade leads to a capable EIC detector
Large coverage of tracking, calorimetry and PID
Open for new collaboration/new ideas
Documented: http://www.phenix.bnl.gov/plans.html
RHIC: A+A, spin-polarized p+p, spin-polarized p+A
EIC: e+p, e+A
arXiv:1501.06197 [nucl-ex]
arXiv:1402.1209 [nucl-ex]

## Slide 3: sPHENIX – quick summary and look “forward”
sPHENIX: major upgrade to the PHENIX experiment aim for data @ 2020
Physics Goals: detailed study QGP using jets and heavy quarks at RHIC energy region
Baseline consists of new large acceptance EMCal+HCal built around recently acquired BaBar magnet. Additional tracking also planned
Detailed performance simulation. Simulation/analysis software open access: https://github.com/sPHENIX-Collaboration/coresoftware
Very positive DOE scientific review Apr 2015.
Forming new scientific collaboration: https://www.bnl.gov/lajudr2015/
Nov 2015: Cost schedule review
Dec 2015: first collaboration meeting as new scientific collaboration
A good foundation for future detector upgrade
Baseline detectors for sPHENIX
sPHENIX MIE, arXiv:1501.06197 [nucl-ex]

## Slide 4: In EIC era: concept for an EIC Detector
RICH
GEM
Station4
EMCal
HCal
GEM
Station2
R (cm)
HCal
p/A
EMCal
GEMs
EMCal & Preshower
TPC
DIRC
η=+1
η= 4
-1.2
GEM
Station3
GEMs
Station1
η=-1
e-
Aerogel
z (cm)
ZDC
z≈12 m
Outgoing
hadron
beam
Roman Pots
z≫10 m
R (cm)
z ≤ 4.5m
BBC
-1<η<+1 (barrel) : sPHENIX + Compact-TPC + DIRC
-4<η<-1 (e-going) : High resolution calorimeter + GEM trackers
+1<η<+4 (h-going) :
  1<η<4 : GEM tracker + Gas RICH
  1<η<2 : Aerogel RICH
  1<η<5 : EM Calorimeter + Hadron Calorimeter
Along outgoing hadron beam: ZDC and roman pots
LOI: arXiv:1402.1209
Working title: “ePHENIX”
Review: “good day-one detector”
“solid foundation for future upgrades”

## Slide 5: Recent evolving of ePHENIX with sPHENIX
New HCal
Support Ring
GEM (η<1.22)
Forward Cal (η<1.1)
Gas RICH
1.4<η<4
New SPACAL
DIRC & e-EMC
Available under GitHub/EIC-Detector: coresoftware-eic/macros/Fun4All_G4_ePHENIX.C
Aerogel
1.2<η<2
Field map/balance in COMSOL
(N. Feege, SBU)

## Slide 6: Tracking and PID detectors
IP
p/A
e-
e-going GEMs
-4.0<η<-1
TPC
-1<η<+1
h-going GEMs
1<η<2
TPC
GEMs
eGEM
RICH
gas RICH
1<η<4
Fringe field
1.5 T main field
Fringe field
Geant4 model of detectors inside field region
DIRC
-1<η<+1
Aerogel RICH
1<η<2
Tracking
TPC+DIRC
η
p/A
e-
Calorimeters (H-Cal cover η > -1)
AeroGel&Gas RICHs
AeroGel RICH?
Space for Aerogel RICH
-3<η<-1
TOF?

## Slide 7: Hadron PID Overview
Hadron PID Coverage
One configuration for hadron PID
10 x 250 GeV beam
IP
p
e-
DIRC
-1.2<η<+1
Gas RICH
1<η<4
Aerogel RICH
1<η<2
TPC
GEMs
eGEM
RICH
Mirror
DIRC
  Based on BaBar DIRC design plus compact readout
  Collaborate with TPC dE/dx for hadron ID in central barrel
Aerogel RICH
  eRD11 modular design should work well
  Collaborate with gas RICH to cover 1<η<2
  PID in e-going direction for higher e-beam
Gas RICH: eRD6 single gas radiator
TOF solution: next few slides
SIDIS x-Q2 coverage with hadron PID in two z-bins

## Slide 8: Coverage of each subsystem quantized in SIDIS kinematic space coverage (x, Q2, z)
IP
p
e-
DIRC
-1.2<η<+1
Gas RICH
1<η<4
Aerogel RICH
1<η<2
TPC
GEMs
eGEM
RICH
Mirror
Missing PID coverage, IF any single subsystem is removed
Evaluated for one possible configuration

## Slide 9: Another PID detector configuration Full detector TOF solution, eRD10
H-going TOF
Replacing/compliment AeroGel
1<η
p
e-
Barrel TOF
Replacing/compliment DIRC
-1<η<1
e-Going TOF
η<-1
Full detector ToF system to cover
low-mid momentum range PID

## Slide 10: Gas RICH - The Design
R (cm)
Z (cm)
RICH Mirror
RICH Gas
Volume (CF4)
η=1
η=2
η=3
η=4
Entrance
Window
Focal plane
HBD detector
spherical
mirror
center
IP
Hadron ID for p>10GeV/c require gas Cherenkov
  CF4 gas used, similar to LHCb RICH
Beautiful optics using spherical mirrors
Photon detection using CsI−coated GEM in hadron blind mode - thin and magnetic field resistant
Active R&D:
  Generic EIC R&D program
  recent beam tests by the stony brook group
Beam test data
StonyBrook group
Courtesy : EIC RD6 TRACKING & PID CONSORTIUM
Fermilab T-1037 data
Ring size (A.U.)

## Slide 11: Field effect - distortion for RICH
Field calculated numerically with field return
Field lines mostly parallel to tracks in the RICH volume with the yoke
We can estimate the effect through field simulations
A RICH Ring:
Photon distribution due to tracking bending only
R
Dispersion
ΔR <2.5 mrad
R < 52 mrad for C4F10
RICH
EMCal
η~1
η~4
Aerogel
track

## Slide 12: Field effect – Radius uncertianty of RICH Ring
Quantify ring radius error
In the respect of PID: minor effect
Ring radius ± 1σ field effect (for worst η=1)
π
K
p
Field effect has very little impact for PID

## Slide 13: H-going side - performance
RICH
EMCal
η~1
η~4
Aerogel
track
Purity
Gas RICH PID purity at η=4 (most challenging region w/ δp)
AeroGel RICH PID eff.

## Slide 14: Summary
“ePHENIX” concept based on sPHENIX upgrade
Evolving concepts of full detector hadron PID
  H-going: AeroGel RICH (medium momentum range) + Gas RICH (high-p range)
  Barrel : TPC (low momentum range) + DIRC (medium momentum range)
  E-going: AeroGel RICH
  Full detector TOF solution also considered
Fringe field
1.5 T main field
Fringe field
Tracking
TPC+DIRC
p/A
e-
Calorimeters (H-Cal cover η > -1)
AeroGel&Gas RICHs
AeroGel RICH?
TOF?

## Slide 15: Extra Information

## Slide 16: Use of calorimeter for EIC physics
Electron identification (e-EMC, barrel EMC)
Electron kinematics measurement (e-EMC, barrel EMC)
DIS kinematics using hadron final states (barrel EMC/HCal, h-EMC/HCal)
Photon ID for DVCS (All EMC)
Diffractive ID (h-HCal)
High momentum track energy measurement (h-HCal)
Electron purity
after EMCal PID
Fraction of DIS event
with good electron ID
DIS kinematics survivability
Electron kinematic method
Purity
0
1
From Sasha and Karen using parameterized performance