## Slide 1
We got few urgent requests:
Brian’s regarding parameterization of energy resolution and acceptances
Thomas’s – acceptance
Thomas’s need for R&D
BHcal
pHcal
Eta = 1.06
Eta= 1.2
To Brian, which of two
Numbers you want us to give you?
i.e. how to handle overlapped regions?

## Slide 2
Sub-system | Readout Unit | Minimal Practical | Maximum Energy YR Inclusive | Instrumented Rapidity Range | Energy resolution Stochastic (a) | Energy Resolution Constant (b)
n-EMCal PWO | Tower | 2.5 MeV | 20 GeV | -4 to -2.3 | 2% | 1%
n-EMCal SC Glass | Tower | 2.5 MeV | 20 GeV | -2.3 to -1.5 | 2.50% | 1.60%
n-Hcal (KLM type) (10 layers) | Scint. Tile (individual tile) | 300 MeV | 20 GeV | -4 to -1 | 70% | 5%
p-EMCal | Tower (sum all fibers) | 5 MeV | 100 GeV | 4 to 1.2 | 10% | 2%%
p-Hcal | Tower (sum 51 tiles) | 300 MeV | 100 GeV | 4 to 1 | 40% | 6%
b-Hcal (KLM Type) (5 layers) | Scint. Tile (individual tile) | 300 MeV | 10 GeV | -1 to 1 | N/A | 37%
b-Ecal (ScFI part) | Sub-Layer (one light guide) | 2.5 MeV | 50 GeV | -1.5 to 1.2 | 5.50% | 1%
b-Ecal (Si layers) | Pixel | 2.5 MeV |  | -1.5 to 1.2 | N/A | N/A
nHcal, numbers for resolution are from WA1, 5% constant term is a guess.

## Slide 3
Needs for R&D:
nECal – targeted eRD105 R&D for ScGlass, ongoing for PWO (SiPM readout)
nHCal – not needed
bECal – costed small prototype (ScFi part)
bECal – imaging, prototype costed 6 layers ½ length
bHCal – not needed
pHCal – targeted eRD107
pECal – targeted eRD106
R&D for SiPMs – part of sensors targeted R&D