## Slide 1: Center for Linac Isotope Production (CLIP) proposal light ion accelerator
December 09, 2021
D. Raparia

## Slide 2: Outlines
Motivation
Considerations
Light Ion Linac
Summary

## Slide 3: Acknowledgements
CLIP team

## Slide 4: Motivation
  Increase proton energies to 600 MeV or higher
    BLIP can irradiate up to 5 100-gram Th targets producing approximately 10 Ci of Ac-225
    increase in beam energy allowing more targets to be irradiated.
    Increase in beam energy could result in even higher Ac-225 production from Th as well as Ra-225 for generator production of Ac-225 free of Ac-227
    Allow for more spallation target irradiations
    Neutron source for isotope production
  Utilize fast neutrons for isotope production
  Higher energy allow more fast neutrons for radiation damage studies.

## Slide 5: Motivation
Light Ion linac energies up to 60 MeV/u
  To reach the energies and current of light ions which are not available elsewhere for a variety of applications
  Nuclear reaction cross section measurements
  Allow for alpha emitter production unique capability (Rn-211,At-211, Pt-193m, Pt-195m, Sn-117m)

## Slide 6: Li-7 beam application for isotope production
Production of radiotherapeutic alpha emitter At-211 (T1/2=7.21 h)
  Pseudo generator approach via 211Rn route
    209Bi(7Li, 5n)211Rn(T1/2=14.6 h) 211At
    The excitation function approaches 650 mb at 53 MeV (7.6 MeV/u). The thick target saturation yield was 5.5 μCi/nA.
Another route (more popular )
209Bi(4He,2n)211At

## Slide 7: Requirements
Ion:
m/q <2.3
Energy 60 MeV/u
Av. Beam Current 200 𝛍A
Beam Power 84 kW

## Slide 8: Light Ion Linac

## Slide 9: Light Ion Linac
Options
Room temperature , Superconducting , or combinations
- Wide range of experience with RT RFQ and IH up to several MeV/u
- Higher energy, superconducting linac
- Transition energy RT to SC (depends on peak current, Space charge)
Pulse or CW
- Limited experience with RT CW operation
Higher current ion source for light ions (Laser, EBIS, ECR)
What is riskier, high peak current IS (Li) or CW RFQ (RT) ?

## Slide 10: Considerations
This facility will an isotope production facility
Ion energies range 5 MeV to 60 MeV/u
Reliability is priority within the irradiation time
Maintainability

## Slide 11: Proposed Design for Light Ion Linac
ECR (Li)
ECR (H,D)
Switcher
RFQ (162.5 MHz)
IH (162.5 MHz)
HWR
HWR
HWR
HWR
162.5 MHz bG 0.25
20 keV/u
1000 keV/u, 2.83m
11 MeV/u, 8. m
60 MeV/u
ECR (He)
Peak beam current 2 mA
Beam pulse length 3 ms
Repetition rate 100 Hz
45∘
-45∘
22.5∘

## Slide 12: Ion Sources and LEBT (20 keV/u)
ECR sources could be used for the light ions
IONS | source | Frequency | current | Emittance
H, D | ECR | 2.5 GHz | 2 mA | <1 pi mm mr
He, Li | ECR | 14-18 GHz | 2 mA | <1 pi mm mr
Li oven and ECRIS

## Slide 13: Low Energy Beam Transport (LEBT)
LEBT
-Magnetic switchyard to inject the beam from either source into the RFQ.
-To provide mass to charge separation big angles (-45⁰, +22.5⁰, and +45⁰) to RFQ
- Adjustable water-cooled slits all three lines expected total power several hundred Watts
TRACE2D showing one branch at 45 deg

## Slide 14: RFQ: 1 MeV/u
Parameters |  | 
ions | <2.3 | M/Q
Frequency | 162.5 | MHz
Ein | 20 | keV/u
Eout | 1000 | keV/u
Length | 2.82 | m
Ave. Radius | 5.6 | mm
Vane Voltage | 90 | kV
power | ~ 180 | kW
Transmission | 98 | %
current | 5 | mA
emittance | 0.7 | 𝚷 mm mr
RFQ parameters
PARMTEQM simulation for Li+++

## Slide 15: Current limits and phase advances
Transverse and longitudinal
phase advance along the RFQ.
Transvers and longitudinal
Current limits through the RFQ

## Slide 16: RFQs
BNL Polarized RFQ 200 MHz
750 keV
BNL EBIS RFQ 100 MHz, 300 keV/u, M/Q ~ 6
BNL high intensity RFQ 200 MHz
750 keV
PIP IT RFQ 162.5 MHz, 2.1 MeV

## Slide 17: Medium Energy Beam Transport (MEBT)
90 cm long,
RFQ will have Crandall Cell
Five controllable knobs and buncher position
TRACE3D calculations for the MEBT

## Slide 18: IH Linac: 11 MeV/u
Paramweter | Values | Units
Ions | <2.3 | M/Q
Ein | 1 | MeV/u
Eout | 10.8 | MeV/u
Freq | 162.5 | MHz
Section | 2 | 
# of Gap | 63 | 
Length | 7.8 | m
Power | ~1.5 | MW
Transmission | 100 | %
Emittance | 0.9 | 𝚷 mm mr
Proven technology BNL, CERN, GSI

## Slide 19: IH Linac at BNL
IH Linac
RFQ
BNL EBIS IH Linac
Ion | D-U
Q/M | .16-0.5
Energy | 2 MeV/u
Current | 1.5 emA
Pulse Length Rep. Rate | 10 s 5 Hz
Emittance | 0.7  mm rad (nor, 90%)
Energy Spread | 1.8 keV/amu
BNL EBIS Preinjector

## Slide 20: Medium Energy Beam Transport-2 (MEBT2)
3 meter long (space for transition )
Six degree of freedom
TRACE3D calculations for the MEBT 2

## Slide 21: SC Sections
Parameters | Value
E in | 10.8 MeV/u
E Out | 60 MeV/u
Freq | 162.5 MHz
RR | cw
Cryomodule | 4
Cavity /(CM) | 6
Solenoid/(CM) | 3
Cavity type | HWR
𝛃G | 0.25
Eacc | 10.5MV/m
Length | 25 m
PIP II 162.5 MHz HWR

## Slide 22: Transit Time Factor
The transit time factor and energy gain for the two-cell cavity is given by
Chart: T(Beta)
| 0.16409283988326143 | 0.16977060816643752 | 0.17610027291643887 | 0.18301675459311043 | 0.19042746933312849 | 0.19822286330877711 | 0.20628839378422223 | 0.21451505625222367 | 0.22280666003814376 | 0.23108347365008308 | 0.23928288089317484 | 0.24735808613905835 | 0.2552758400365705 | 0.26301388567986411 | 0.2705585382197116 | 0.27790259169911208 | 0.28504360879519769 | 0.2919825753562178 | 0.29872286969757417 | 0.3052694883703857 | 0.31162847349604916 | 0.31780649476247075 | 0.32381054814936405 | 0.32964774172050815 | 0.33532514578608746 | 0.34084969031613355 | 0.34622809681821115 | 0.35146683519209948 | 0.35657209855572397 | 0.36154979088747141 | 0.3664055237031183 | 0.37114461900082663 | 0.37577211645659264 | 0.38029278340433958 | 0.38471112654098183 | 0.38903140459551672 | 0.39325764142066277 | 0.39739363912665948 | 0.40144299099481567 | 0.40540909399458563 | 0.40929516079067191 | 0.41310423117203465 | 0.41683918286727822 | 0.42050274173406027 | 0.4240974913263455 | 0.42762588185444694 | 0.43109023856013656 | 0.43449276953373506 | 0.43783557300273096 | 0.44112064412271962 | 0.44434988130165959
T(beta) | 0.3933 | 0.45566 | 0.51885 | 0.58047 | 0.63833 | 0.69079 | 0.73684 | 0.77612 | 0.80879 | 0.83534 | 0.85644 | 0.87283 | 0.88525 | 0.89435 | 0.90071 | 0.90484 | 0.90715 | 0.90799 | 0.90765 | 0.90636 | 0.90431 | 0.90166 | 0.89853 | 0.89503 | 0.89125 | 0.88724 | 0.88307 | 0.87877 | 0.8744 | 0.86998 | 0.86553 | 0.86107 | 0.85662 | 0.85219 | 0.8478 | 0.84345 | 0.83914 | 0.83489 | 0.8307 | 0.82657 | 0.8225 | 0.81849 | 0.81455 | 0.81067 | 0.80686 | 0.80312 | 0.79944 | 0.79583 | 0.79228 | 0.7888 | 0.78538
Transit time verse normalized particle
velocity.
Chart: 
| 0.2 | 0.21 | 0.22 | 0.23 | 0.24 | 0.25 | 0.26 | 0.27 | 0.28000000000000003 | 0.28999999999999998 | 0.3
# Cavity | 32 | 31 | 30 | 28 | 27 | 26 | 26 | 26 | 26 | 26 | 27
Design b VS # of cavity to reach 60 MeV/u

## Slide 23: HWR Cavity
Parameter | HWR | UNITS
Frequency | 162.5 | MHz
bG | 0.25 | 
Length bl | 0.46155 | m
Eacc | 14.8 | MV/m
Phase | -20 | deg
EPeak | 68 | MV/m
BPeak | 72.5 | mT
Epeak/Eacc | 4.9 | 
Bpeak/Eacc | 6.9 | 
R/Q | 256 | Ohm
 |  | Ohm
# of cavities | 24 | 
HWR Design
162.5 MHz HWR cavities ,
(EPeak =68 MV/m, BPEAK =72 mT ,
O. Masahiro

## Slide 24: Cryomodule
4.3.8.XII.
 | 2K | 4.5K | 30-50K | LN2 Shield
 | W | W | W | W
SRF modules | 200 | 230 | 750 | 
Cryo-Distribution |  | 50 | 50 | 1000
Total | 200 | 280 | 800 | 1000
Cryogenic Load Requirements

## Slide 25: SC Sections
Input Phase Spaces
X, Y profiles
𝚫E and 𝚽 Profiles
Output Phase Spaces
TraceWin Simulation
Accelerating field

## Slide 26: Space for future upgrade 100 MeV/u
Two cryomodule / 6 cavity (beta=0.4)
External quadrupole
Input phase space
Output phase space
Transverse and Longitudinal
Profiles

## Slide 27: Final Focus and Switch Yard
17 meters space for switch yard , final focus and raster
+/-30 deg switching dipole
Final focus triplet
8 meters space for raster
Beam size 8 mm
Switching magnet
10 meter

## Slide 28: Summary
Light ions
Light ions 60 MeV/u (m/q ~ 2.3), max beam power 28 kW
Use existing technologies
Considerations for high reliability and maintainability
New tunnel and RF gallery
Three target stations