## Slide 1: Lithium ECRIS for CLIP
Dec 2021
M. Okamura

## Slide 2
High performance ECRIS for He2+ and Li3+ beam.
209Bi(4He, 2n)211At
209Bi(7Li, 5n)211Rn
Li3+ beam
He2+ beam
Do we have enough technologies for the ion source?
High current Li3+ and He2+ beams are required.
Journal of Radioanalytical and Nuclear Chemistry (2020) 323:921–926

## Slide 3
Without ECRIS, a new isotope facility cannot be realized in BNL.
Why ECRIS??
At CAD, we have world class ion sources. However,,
 | Li3+ capability | He2+ capability | High current | CW like operation
EBIS | ✔️ | ✔️ |  | 
LIS | ✔️ |  | ✔️ | 
OPPIS |  |  |  | 
H- magnetron |  |  | ✔️ | ✔️
ECRIS | ✔️ | ✔️ | ✔️ | ✔️
No great Li ECRIS in the world.
Lithium is a chemically active material.
Why is the R&D required??
Prototype test is indispensable.

## Slide 4: Target species:
RFQ input energy : 20 keV/u
Duty factor : 10 %
Emittance : 0.2 pi mm mrad nor. rms
 | Mass | Charge | Total Energy (keV) | Column Voltage (kV) | Peak Current (mA)
H+ | 1 | 1 | 20 | 20 | 2
D+ | 2 | 1 | 40 | 40 | 2
He2+ | 4 | 2 | 80 | 40 | 2
Li3+ | 7 | 3 | 140 | 46. 7 | 2

## Slide 5
Microwave Frequency | Magnetic field
2.45 GHz | 875 Gauss
10 GHz | 3.6 KGauss
14 GHz | 5.0 KGauss
18 GHz | 6.4 KGauss
28 GHz | 1.0 T
ECR condition
For Proton
Frequency Choice
Species / charge state | Ionization energy
H+, D+ | 13.6 eV
Li3+ | 122.4 eV
He2+ | 54.4 eV
C4+ | 64 eV
C5+ | 392 eV
O5+ | 113 eV
Ar7+ | 124 eV
For He & Li
Plasma temperature
Better emittance
Geller’s scaling laws
Beam emittance is proportional to the magnetic field strength at the extraction.
High field -> Large emittance
He2+ can be provided from a higher frequency ECRIS

## Slide 7
For H+ and D+, Taylor type ECR works good.
NIMA 309 (1991) 37-42
2.45 GHz (same frequency to a kitchen microwave)
Two axial solenoid magnets
No transverse confinement magnet
2 kW provides more than 10 mA
Proton fraction more than 90%

## Slide 8
Permanent magnet 2.45 GHz ECR is getting popular now.
TUCOCK02 Proceedings of ECRIS2010, Grenoble, France
Commercial solution is available
Pantenik Monogan M-1000
Proton ECRIS can be fabricated in house or purchased.

## Slide 9
There have been no mA class Electron Cyclotron Resonance Ion Source for Li3+ beam.
Lithium is classified as an alkali metal on the Periodic Table.
At 300°C, lithium has a significantly high enough vapor pressure to cause ppm level contamination in a vacuum system.
Temp. (°C) for Given Vap. Press. (Torr) | 10-8: 227 10-6: 307 10-4: 407
How to control lithium vapor pressure?
How to manage lithium contamination?
ECR requirement range from E-8 to E-6.
Temperature range from 230 C to 310 C.

## Slide 10
Comparison with other alkali metals
Natural abundance of 7Li is 93 %. 7 % is 6Li which is not our interest.
Name | Lithium | Sodium | Potassium | Rubidium | Caesium
Atomic number | 3 | 11 | 19 | 37 | 55
Standard atomic weight (u) | 6.94 | 22.98 | 39.09 | 85.46 | 132.9
Electron configuration | [He] 2s1 | [Ne] 3s1 | [Ar] 4s1 | [Kr] 5s1 | [Xe] 6s1
Melting point (°C) | 180.54 | 97.72 | 63.38 | 39.31 | 28.44
Boiling point (°C) | 1342 | 883 | 759 | 688 | 671
Density (g·cm−3) | 0.534 | 0.968 | 0.89 | 1.532 | 1.93

## Slide 11
Li does not readily react with water-free 02 below 373 K, but reacts above 373 K to form an oxide (Li2O).
The reaction between metal Li and N2 is slow in the case of N2 without moisture, but when even a small amount of moisture is present, the exothermic reaction proceeds rapidly even at room temperature to produce nitride (Li3N).
This is highly corrosive to iron and steel (the melting point of Li3N itself is almost 1118 K).
Li and C react at high temperatures to form carbides (Li2C2). The reaction with H2 produces a stable solid compound (LiH: melting point 960 K, decomposition temperature ~1245 K), which is the most stable among alkali metal hydrides.
Li at room temperature easily loses its luster and turns black when it comes in contact with air containing moisture, and becomes a white powder if left for a long time, but this is thought to be due to the formation of compounds such as Li3N, LiOH, and LiOH-H2O first, and finally Li2CO3 powder.
From the standpoint of corrosion resistance, it is desirable to make the device out of Mo, Nb, Ta, Zr, Ti and W. Fe is also relatively safe, and SUS316 is used in fusion reactors as a non-magnetic material.
Notable chemical property of Li
Li feed line is kept between 200 C and 300 C.
Interior of the ion source should be made of Mo, Nb, Ta, or SUS316.

## Slide 12
Develop Li feeding system
Oven type: Internal or external
Laser ablation type
Laser
Lithium laser target at LIS

## Slide 13
Li evaporation test is in preparation

## Slide 14
To avoid Li condensation, all the surface will be kept above 200 C.
Based on the evaporation experiment, we will design temperature distribution in the ECRIS.
Heat insulator to protect PM
Hexapole is usually made of Nd magnet.

## Slide 15
18 GHz microwave needs 6.4 kG.
Nd2Fe14B is commonly used to form hexapole field for transverse confinement.
However, it is strongly recommended below 100 C to avoid irreversible demagnetization.
Choice of a different PM material.
Electrical magnet without core. (Core cannot be used because it will reduce the axial field of the solenoids.)
Good design to prevent thermal penetration to the hexapole magnet.
Solenoid mirror and cusp field

## Slide 16
300 mm
84 mm
Permanent magnet hexapole

## Slide 17
ID 80 mm
86
34.7
150
31.7
78.7 deg
24 deg
52 deg
156
2
60 deg
The simulation was conducted based on ANL's ECR design.

## Slide 18
Nd Magnet
Samarium-cobalt magnet
Alnico magnet

## Slide 19
Electromagnet can be used??
Same dimension as the PM model

## Slide 20
Typical water cool condition.
20X 10 % duty factor and 5 times of temperature rise.
Probably too extreme!

## Slide 21
TEST ECRIS is proposed
Design of microwave feed line
Design of plasma chamber
Design of beam extractor
Heat insulation
to permanent magnets
Avoid condensation
of lithium
Volume less than 0.5L
for investigating the feasibility and beam current.
Effect of a support gas will be also tested.

## Slide 22: 1.68 T at extraction aperture
30 kV- -3kV - 0
Z=400 means 100 mm
(Mesh uniti is 0.25 mm)
R=40 means 10 mm
(Mesh uniti is 0.25 mm)
r-r' |  |  |  |  | x-x' and y-y' |  |  | 
 | Erms | Erms_norm | E_tot_norm |  |  | Erms | Erms_norm | E_tot_norm
 | p mm mrad | p mm mrad | p mm mrad |  |  | p mm mrad | p mm mrad | p mm mrad
Li3+ | 6.795 | 0.021 | 0.103 |  | Li3+ | 3.398 | 0.010 | 0.052
Li2+ | 7.174 | 0.022 | 0.109 |  | Li2+ | 3.587 | 0.011 | 0.054
Li1+ | 3.805 | 0.012 | 0.058 |  | Li1+ | 1.903 | 0.006 | 0.029
Li3+: 2mA
Li2+: 2mA
Li1+: 2mA
Extraction aperture R=3mm

## Slide 23: 1.68 T at extraction aperture
ZEND=400 (100 mm)
R-rms ~5.6 mm

## Slide 24: 1 T at extraction aperture
r-r' |  |  |  |  | x-x' and y-y' | x-x' |  | 
 | Erms | Erms_norm | E_tot_norm |  |  | Erms | Erms_norm | E_tot_norm
 | p mm mrad | p mm mrad | p mm mrad |  |  | p mm mrad | p mm mrad | p mm mrad
Li3+ | 3.649 | 0.011 | 0.055 |  | Li3+ | 1.825 | 0.006 | 0.028
Li3+ | 2.048 | 0.006 | 0.031 |  | Li2+ | 1.024 | 0.003 | 0.016
Li3+ | 3.262 | 0.010 | 0.049 |  | Li1+ | 1.631 | 0.005 | 0.025

## Slide 25: 1 T at extraction aperture
ZEND=400 (100 mm)
R-rms ~5.6 mm

## Slide 26
Summary
Proton and deuteron ECRIS can be built or purchased.
mA class LI3+ ECRIS is a challenging task.
Li is chemically highly reactive. Needs to establish maintenance procedure.
Li vapor supply systems will be studied. External oven, internal oven or laser.
Hexapole magnet design must be experimentally confirmed.
Based on test ECRIS study, we will scall every design parameters.
He2+ can be delivered from the Li ECRIS.
Establish high current ECRIS for He2+ and Li3+ beams.