## Slide 1
Technical details on pfRICH
Geometry: proximity focusing, no mirrors
Aerogel: parameterizations based on CLAS12 data
3cm thick @ density 110mg/cm3 (effective <n> came out ~ 1.019)
Rayleigh scattering
Absorption length
Thin acrylic layer
~40cm long (air) expansion volume
SiPMs (S13361-3050AE-08 8x8 panels)
3.4 mm pitch
QE as given by Hamamatsu
85% geometric fill factor & 70% “safety factor” on top of it
ATHENA simulation environment
npsim, juggler IRT plugin, analysis scripts

## Slide 2
Acceptance
C2F6 dRICH 12 GeV pions
pfRICH 8 GeV pions
“Fast parameterizations for Deplhes provided”

## Slide 3
PID momentum limits pfRICH
Eta -2.0 to -2.4

## Slide 4
Separation pi-k e-pi for pfRICH as a function of momentum for eta -2.0 to -2.2

## Slide 5
Sigma_theta (mrad)
Mom (GeV)
Pi hypothesis
Theta difference and evolution of sigma theta

## Slide 6
Geometry Chris circulated

## Slide 7
Magnetic field is OFF... 3 positions in eta are used, with ranges given below; 3 positions in phi are also used: {-30,0,+30} degrees, so we see some half rings along dRICH sector boundaries. In the highest eta bin, only phi=0 is used. 100 particles are aimed at each position, to obtain enough stats to see clear rings. for pfRICH: etaMin_ = 1.6 etaMax_ = 3.8 20 GeV electrons for dRICH: etaMin_ = 1.5 etaMax_ = 3.4 20 GeV pions

## Slide 8
Pion kaon PID performance study
Identified pion /(identified pion +identified kaon)

## Slide 9
K+
p+
h = 3.0, p = 50 GeV/c
q (accepted) < 37.8 mrad
q (accepted) < 38.7 mrad
s ~ 0.4 mrad