## Slide 1: Modular RICH Simulation -- Aerogel thickness & Refractive Index
Cheuk-Ping Wong
Georgia State University
11-19-2015

## Slide 2: Update Aerogel Properties
We update aerogel properties: 1.) Thickness and 2.) Refractive Index base on Marco Contalbrigo’s report1.
In the report
  Aerogel thickness = 3cm
  Aerogel refractive index is in range 1.0477 to 1.0523
https://clasweb.jlab.org/wiki/index.php/2015_October_13_RICH_Project_Mid-term_Review

## Slide 3: In This Update
We change modular Rich detector dimension (see next slide) for flexible aerogel thickness
Compare simulation results between
  3cm and 2cm thick aerogel
  Different refractive indices
    refractive index ≈1.02 (a function of photon energy given by Hubert) which is what we usually use
    refractive index =1.0477
    refractive index =1.0523

## Slide 4: Updated Dimension of Modular RICH Detector in GEMC Framework
3cm Aerogel
2cm Aerogel
1cm Aerogel
Enlarged but fixed dimension of detector holder box

## Slide 5: Updated Dimension of Modular RICH Detector in GEMC Framework
Updated Dimension of Modular RICH Detector in GEMC Framework
Shift Fresnel lens, mirrors, photonsensor and readout to the left
z-position of these components is fixed (independent on the thickness of aerogel)

## Slide 6: Updated Dimension of Modular RICH Detector in GEMC Framework
================== 3 cm thick Aerogel ==================
Printing detector positions and sizes …
hold box position: ( 0.0, 0.0, 112.5 mm), half size in XYZ: ( 56.25 mm, 56.25 mm, 62.5 mm )
aerogel position: ( 0.0, 0.0, 69 mm), half size in XYZ: ( 55.25 mm, 55.25 mm, 15 mm )
fresnel lens position: ( 0.0, 0.0, 85.5 mm), half size in XY: ( 55.25 mm, 55.25 mm )
photon detector position: ( 0.0, 0.0, 158.5 mm), half size in XYZ: (44.2 mm, 44.2 mm, 1 mm )
readout position: ( 0.0, 0.0, 157.5 mm, and 163.5 mm )
=====================================================================

## Slide 7: Simulation Setup
Momentum range 0-15 GeV/c
1000 events
  Pion-
  Kaon-
Magnetic field off
Agel thickness
  3 cm
  2cm
Agel refractive index
  refractive index ≈1.02 (a function of photon energy given by Hubert) which is what we usually used
  refractive index =1.0477
  refractive index =1.0523
Thus, we have 2x2x3=12 sets of data

## Slide 8
Compare Simulation Results
with Different Refractive Indices

## Slide 9: Ring Radius vs Momentum
 | 2 cm thick Aerogel | 3 cm thick Aerogel
Pion |  | 
Kaon |  | 
Larger the refractive index, larger the Chenerenkov ring radius
-- 1.0523
-- 1.0477
-- 1.02

## Slide 10: Num. of Photon Hits per Event vs Momentum
 | 2 cm thick Aerogel | 3 cm thick Aerogel
Pion |  | 
Kaon |  | 
Number of photon hits per event increases with refractive index
-- 1.0523
-- 1.0477
-- 1.02

## Slide 11
Compare Simulation Results
with Different Aerogel Thicnkesses

## Slide 12: Ring Radius vs Momentum
 | Refractive index~1.02 | Refractive index=1.0477 | Refractive index=1.0523
Pion |  |  | 
Kaon |  |  | 
-- 2cm thick agel
-- 3cm thick agel
Ring Radius shifts up a bit when thickness of agel is increased

## Slide 13: Num. of Hits per Event vs Momentum
 | Refractive index~1.02 | Refractive index=1.0477 | Refractive index=1.0523
Pion |  |  | 
Kaon |  |  | 
-- 2cm thick agel
-- 3cm thick agel
Num. of Hits per Event increases with agel thickness

## Slide 14
Compare Simulation Results
with Different Incident Particles

## Slide 15: Ring Radius vs Momentum
 | Refractive index~1.02 | Refractive index=1.0477 | Refractive index=1.0523
2cm |  |  | 
3cm |  |  | 
-- Pion-
-- Kaon-

## Slide 16: Num. of Hits per Event vs Momentum
 | Refractive index~1.02 | Refractive index=1.0477 | Refractive index=1.0523
2cm |  |  | 
3cm |  |  | 
-- Pion-
-- Kaon-
It is hard to identify pion and kaon in high momentum region (roughly higher than 6 GeV/c) by looking at the plots on slide 14 and 15. However, it is hard to make conclusion at this point, and a sophisticated analysis using Likelihood Analysis is needed.

## Slide 17: Summary
In order to make the simulation result more reliable, we changed aerogel properties in simulation to fit the actual aerogel sample shown by Marco
Both ring radius and num. of hits per events increase with refractive index
Both ring radius and num. of hits per events increase with aerogel thickness
Maximum Likelihood analysis is needed to analysis the effect of refractive index and aerogel thickness on PID

## Slide 18: Next
Study Likelihood analysis
  Set agel thickness=3cm, refractive index=(1.0477+1.0523)/2=1.05
  then compare analysis results with Liang’s works
Delta ray electrons energy distribution