## Slide 1: PID Rapid Response Team
Roberto, Tom, Frank, Henry Klest
contacted: Monday 1:12pm due: “tomorrow at 11am”
First Result 10:32pm

## Slide 3: Back in the days of the Yellow Report: PID class
Simple way to make comparative overlays of PID performance.
Hemmick though it long dead.
Roberto dramatically upgraded this approach:
  Coded in detailed pfRICH, dRICH, DIRC, TOF response
Used to make the famous PID plot:

## Slide 4: Methodology
Function returns # sigma separation
Electron efficiency:
  Integral of Gaussian(0) from –inf to x
  x can be chosen for 90%, 95%, 98%
Pion efficiency:
  Integral Gaussian(sep power) from –inf to x
Modify original points by:
  new = original * (pion-eff/electron-eff)
  Original points retrieved by Data Thief
Note:
  PID classes reject particles that don’t reach the detector

## Slide 5
pfRICH
n=1.02
pthreshold=0.69 GeV/c
Cuts set at 90%, 95%, 98% electron efficiency
Background hits not included.
TOF
Analytical Response
DIRC
n=1.473
pthreshold=0.13 GeV/c
Tabulated from FullSim
-3.5<h<-2.0
0.0<h<1.0
FastSim results below 10-6 indicated by downward arrows