## Slide 1: PID Calibration, Cherenkov imaging devices​
The dRICH case is discussed (analogous for pfRICH and hpDIRC)​
C2F6
Cutaway rendering of the dRICH detector
  Assumptions:
    tracking and momentum measurement already calibrated
    aerogel support and mirror support (anchorage of the mirror center) are known (with ~1mm resolution, fully adequate).
    the relative position of the photosensors within each array is known with resolution better than 100 mm (fully adequate)
    Aerogel refractive index known (measured)

## Slide 2: PID Calibration, Cherenkov imaging devices​
C2F6
Cutaway rendering of the dRICH detector
  Each of the six dRICH sectors is independent calibrated
  parameters to be determined
    Mirror angular orientation (2 parameters);
    position in space and angular orientation of the sensor array (5 parameters);
    radiator gas refractive index n (1 parameter); not known a priory (depends on P, T and impurities)
     8 parameters in total: 7 for alignment + n
1 of the 6 sectors

## Slide 3: PID Calibration, Cherenkov imaging devices​
  Mass plot are produced
    The known particle masses used as constrains
    Best fit procedure using aerogel data and gas data together to extract the 8 calibration parameters
  Cross-check: by comparing the n-values for the 6 dRICH sectors
  Monitoring n-value (that continuously evolves with P, T and impurities):
    same procedure fixing the 7 alignment parameters (smaller statistics required making continuos monitoring practical)