## Slide 1: sPHENIX Beam Pipe Bake Jacket FDR
Chris Runyan 03/30/22

## Slide 2: Beam Pipe Heating Jacket Thermal/Mechanical Design Requirements
Not to exceed 1” total jacket thickness
Must reach 200°C minimum operating temperature
Must be capable of reaching 250°C test temperature
Surrounding INTT Carbon Fiber not to exceed 60°C to protect epoxy used in surrounding components
Custom cloth heating jacket fabricated by BriskHeat, same jackets used in STAR/others
Insulating layers:
  Inner layer – Silicone impregnated Beta cloth (Alpha composites)
  Middle layer – Fiberglass insulation (Pardus E-Mat 1200)
  Outer layer – Silicone impregnated facing (TCI Tufjac 1550)
Insulating cuffs protect the spider supports and flanges from heating appreciably to prevent differential CTE issues
Dan and Sumanta to cover installation/removal details
Assumed combined avg. density of .18 gm/cm^3

## Slide 3: Heating Jacket Layout – No Jacket
North
Side

## Slide 4: Heating Jacket Layout – With Jacket
North
Side

## Slide 5: Heating Jacket Layout

## Slide 6: ANSYS CFX CFD and Thermal Analysis

## Slide 7: CFD Analysis with ANSYS CFX, components and mesh
*Analysis was done with a jacket thickness of .5” for a large FOS, since fabricator quotes a maximum jacket thickness of 1”

## Slide 8: CFD Analysis, air velocity cross section/streamlines, midplane
Boundary Conditions
  Steady state
  Vertical symmetry
  Ambient air, no forced convection
Results
  Midplane velocity plot and streamline
  Natural convection due to thermal gradient
  Maximum velocity:
    .12 m/s

## Slide 9: CFD Analysis, steady state temperature at midplane, inlet air temp 25° C
Boundary Conditions
  Steady state
  Vertical symmetry
  200°C at beam pipe surface
Results
  Midplane temperature plot
  Thermal gradients indicate air temperature does not heat appreciably
  Maximum air temperature:
    68.57 °C
  Maximum air temperature near carbon fiber tube:
    43.71°C
  The air mass is warmer on the top due to gravity-buoyancy force

## Slide 10: CFD Analysis, carbon fiber temperature, with radiation, air temp 25° C
Monte-Carlo ray scattering model employed to simulate radiation heat transfer
  Very high emissivity (.8) used for both jacket and INTT carbon fiber support tube to assume worst-case scenario
As expected, maximum temperature occurs near the top of midsection where distance to ambient air inlets is maximized:
  Maximum temperature in INTT carbon fiber is 41.11°C
  Considering all conservative assumptions made for this analysis (.5” thk insulation, high emissivity), there is plenty of thermal margin

## Slide 11: Beam Pipe Jacket Specifications Document

## Slide 12: Al-Be Beam Pipe Jacket Sections
Spider Support
[Jacket 1 – Quantity =2 – Length = 58.25”]
2X Jackets for the mid section of beam pipe up to spider support on both sides and both jackets meet at the IP. Conforms to small diameter changes in beam pipe.
2” CF Flange 3.375” OD
[Jacket 2 – Quantity =2 – Length = 50.6163”] Jacket-covers from Spider Support over 1.7” to 2” transition to the first flange.
SOUTH END
1.7” to 2” Transition
IP
Spider Support
2” CF Flange 3.375” OD
NORTH END
1.7” to 2” Transition

## Slide 13: Al-Be Beam Pipe Jacket Sections
[Jacket 1 – Quantity =2 – Length = 58.25”]
2X Jackets for the mid section of beam pipe up to spider support on both sides and both jackets meet at the IP. Conforms to small diameter changes in beam pipe.
[Jacket 2 – Quantity =2 – Length = 50.6163”] Jacket-covers from Spider Support over 1.7” to 2” transition to the first flange.
Spider Support,
Thickness = .75”
BOTH NORTH AND SOUTH

## Slide 14: Al-Be Beam Pipe Jacket Sections
[Jacket 1 – Quantity =2 – Length = 58.25”]
2X Jackets for the mid section of beam pipe up to spider support on both sides and both jackets meet at the IP. Conforms to small diameter changes in beam pipe.
[Jacket 2 – Quantity =2 – Length = 50.6163”] Jacket-covers from Spider Support over 1.7” to 2” transition to the first flange.
Spider Support,
Thickness = .75”
BOTH NORTH AND SOUTH
[Spider Support Cuff – Quantity = 2]
Cuff surrounds spider support to insulate support and beam pipe through support section. Openings in cuff allow for mounting rods. Insulation only, no heater circuits.

## Slide 15: Al-Be Beam Pipe Jacket Sections

## Slide 16: Remaining Beam Pipe Jacket Sections

## Slide 17: Remaining Beam Pipe Jacket Sections

## Slide 18: Remaining Beam Pipe Jacket Sections

## Slide 19: Jacket Procurement

## Slide 20: Beam Pipe Jacket Procurement
Original beam pipe installation timeline required immediate procurement of BP jackets
  Vacuum group would like jackets before BP install, sometime in Summer ’22
  Jackets were split into two separate requisitions to speed up procurement
PO has been issued for Al-Be portion of beam pipe jackets, working on Requisition for remaining jackets
Total cost of all sPHENIX jackets: $26,157.60
Lead time: 17 Weeks ARO
Al-Be Jacket PO was dispatched on 03.07.22
  Should receive jackets 07.01.22
  Remaining jackets should “piggyback” onto first order to circumvent lead time
+
Jacket Total = $26,157.60

## Slide 21: BACKUP SLIDES

## Slide 22: INSTALLATION SUPPORT STEPS SOUTH SIDE

## Slide 23: Reach Distance to IP
South
Side
North
Side

## Slide 24: Reach Distance to IP
South
Side
North
Side

## Slide 25: Reach Distance to IP
*scaffolding and temporary
platform not pictured, old model
North
Side

## Slide 26: SOUTH SIDE STEP 1: DURING BAKE, TEMPORARY VERTICAL SUPPORT

## Slide 27: SOUTH SIDE STEP 2: ADD BELLOW CLAMP, THEN REMOVE TEMP. SUPPORT AND FIRST PERMANENT STANCHION SUPPORT

## Slide 28: SOUTH SIDE STEP 3: INTT INSTALL FROM SOUTH

## Slide 29: SOUTH SIDE STEP 4: REINSTALL TEMP. AND PERMANENT SUPPORTS, REMOVE BELLOW CLAMP

## Slide 30: SOUTH SIDE STEP 5: X-WING INSTALL

## Slide 31: SOUTH SIDE STEP 6: INSTALL STRAP SUPPORT/REMOVE TEMP. SUPPORT

## Slide 32: SOUTH SIDE STEP 7: MVTX INSTALL

## Slide 33: INSTALLATION SUPPORT STEPS NORTH SIDE

## Slide 34: NORTH SIDE STEP 1: DURING BAKE, TEMPORARY SUPPORTS

## Slide 35: NORTH SIDE STEP 2: INTT INSTALL FROM SOUTH