## Slide 1: IR layout and planned work at IR-6
E.C. Aschenauer (BNL)

## Slide 2: Perspective from Friends from Physics
Many interfaces and dependencies between EIC Experimental equipment and Interaction region at IP-6  need to define them better and better

## Slide 3: Progress: IR-Integration and Interfaces
Electrons
Space Constrains:
-4.5 m – IP – +5m not negotiable
50 cm space to 1st IR-magnet occupied by vacuum pumps, valves, …..
IP moved 81 cm towards ring inside compared to RHIC; y: 432 cm above floor
no installation possible in collider hall
RCS
9.5 long detector does not fit through the door
  Door-Size: 823 cm x 823 cm
  endcap hadron calorimeters need to stay in collider hall, if detector rolls in
  assembly hall
RCS to IP: radial distance 335.2 cm at a height of 372 cm from floor
  Maximum outer radius ~ 3.2 m
Fringe field requirements for solenoid
  the fringe field at both endcaps impacting the IR magnets: < 5 gauss
  and the fringe field radial along z to impact the RCS: < 0.007 Tm
Hadrons

## Slide 4: Progress towards CD-2
General Points:
make progress on the installation sequence of the accelerator and experimental equipment
  identify conflicts if any
  this needs to include the STAR R&R schedule
defining any anticipated changes in IR layout and optics impacting the experimental equipment acceptance and overall performance early (beam pipe size in y, …..)
define the requirements for a fast beam abort system from the experimental point of view
  what signals are needed from the detector to provide to the fast beam abort system
beam pipe bake-out and integration to keep vacuum in a as good shape as possible when breaking vacuum for detector maintenance.
  can we further optimize the pressure bump at forward side by pump placement refinement?
Ancillary Detectors and IR Integration
improve beam pipe design in the experiment and in the far forward and backward direction
  need a beam pipe design idea over the full +/- 40 m region
  important for integration of RPs, off-momentum, ZDC, low-Q2 tagger
    refine far-forward and backward detector requirements and needs, i.e. pressurized gas, cooling, ……..
Polarimetry and Luminosity
luminosity detector exit window design and overall lumi-detector integration
  are there any other measurements for the lumi-detector the collider needs  SR fan size and orientation?
next steps of lepton polarimeter integration  beam background SR and beam gas

## Slide 5: Progress towards CD-2
Magnet:
improve maximum fringe field requirements of detector solenoid at nearest forward and backward IR magnet locations and for the RCS
  improve detector solenoid compensation scheme
  define requirements for maximum multipole components induced by the detector solenoid in the magnet-free IR region that can be mitigated
Not IP-6 but a big concern
Placement of hadron polarimeters for p,d and He-3  H-jet + its taggers to veto He-3 breakup and pC, currently at IP-4 (RHIC location IP-12)
  IP-4 not optimal location, backgrounds, flexibility in beam optics needed for polarimeters
  Can we find space in IP-6 and IP-8 outside the hadron spin-rotators
    challenge tunnel height to fit H-Jet, need dipole next to H-Jet and pC should be very close to H-jet
  Requirements (space, optics, ..) well defined in official requirement-interface document

## Slide 6: Accelerator Focus
Detector Solenoid Compensation
  finalize ESR and HSR coupling corrections
Magnets
  B0pF 2K Design
  Spin rotator solenoids, 12T – Feasibility
  Skew quads hadrons  Detector solenoid compensation
  Dipole corrector B0ApF  Detector solenoid compensation
  Integration (vac., beampipe, BPMs, assembly)
Vacuum
  Central detector beampipe updates – Impact on physics simulations
  Removal and installation gymnastics for central chamber
  Cooling beampipe (Synrad)
Lattice
  Look at solutions for closing crab bump
MDPS
  Collimators & Absorbers – locations
  ESR & HSR aborts
    Location and Infrastructure
IR Instrumentation
  Orbit Correction near the IP
  eval. strategy for BPMs and corrector magnets design