## Slide 1
ATHENA Calorimetry R&D (EIC project R&D) O.Tsai (02.09.22)
eRD105 – Vladimir gave update on 02.02.22
eRD106 – pECal on hold
eRD107 – pHCal on hold
eRD110 – SiPMs on hold
https://wiki.bnl.gov/conferences/index.php/ProjectRandDFY22
It was an open meeting on 04.02.22 https://indico.bnl.gov/event/14715/ to find common ground between PID/Calorimetry (and between different EIC collaborations ATHENA,ECCE, Core have been shown). For calorimeters this is eRD110
Similarly, for eRD106, eRD107 idea is to call for open meeting in two weeks, and as it was in case of meeting for SiPMs have project to moderate it.

## Slide 2
SiPMs for calorimeters. Discussion 02/04/2022 O.Tsai (UCLA).
Disclaimer: materials have not been discussed within ATHENA calorimetry group, some results were shown in previous EIC generic R&D meetings/reports.
Questions:
where we are? – we are using SiPMs for STAR detector (R&Ds and real detectors) for past 10 years or so
where the technology has to improve? - current sensors can be used for EIC calorimetry applications as is*
what the prospects are? – I don’t expect breakthrough developments**, incremental improvements probably possible
where we can benefit from synergies? - little overlap with PID due to different requirements
what we need to focus on? – better define requirements/justifications, continue R&D (eRD105, eRD106, eRD107,eRD110)
*Related to ‘requirements’ for nECal and pECal
**SiPM noise due to radiation damages
Main concern is increase in noise with radiation.
Minor to No degradation of response due to rad damages. (backup slides)

## Slide 3
ATHENA, pEndCap high lumi n fluxes close to STAR pp 500 GeV for Forward Calorimeter System
EIC collision rate 500 kHz eP, vs STAR 5-6 MHz pp, but STAR FCS is ~ 7m from IP compare to EIC at 3.5 m
ATHENA n,bECal (Hcal) ~ 109 n(cm2year) (Plots from Y. Fisyak (BNL))
FCS uses more than 10k SiPMs
mostly S12572 -15 um pixels
some are S14160-3015PS
No cooling. 23 C in HCAL, 28 C in Ecal
ATHENA pECAL
STAR
Physics Runs
Pedestal Run
But, SiPMs and neutrons are not friends 
EIC generic R&D
2016/17
6m
2m

## Slide 4: Back to main concern, Noise. R&D 2017, Shashlyk S12572-15 four 3x3 mm SiPMs per tower.
Cosmic Muons with un-exposed SiPMs ENF ~ 1.7 MeV
SiPMs Degrade with exposure (details later in talk).
500 GeV pp (Run 17) was the worst case in terms of exposure.
Cosmic Muons with exposed (Run17) SiPMs, ENF – 10 MeV/tower
Hcal (6 SiPMs/tower) noise after exposure ~ 100 MeV (100 uA per SiPM)
N.B. S/N depends on over bias!
FCS 2022, pp 500 GeV. Feb. 3 2022 (~ 1/3 lumi delivered)
Ecal Noise ~ 3 MeV
HCal Noise ~ 16 MeV
How that related to EIC?

## Slide 5
Sub-system | Readout Unit | Minimal Energy YR Table 10.6 | Minimal Practical | Maximum Energy YR Inclusive | Signal Range
n-EMCal PWO | Tower | 50 MeV | 2.5 MeV | 20 GeV | 5-100k pixels
n-EMCal SC Glass | Tower | 50 MeV | 2.5 MeV | 20 GeV | 5-100k pixels
n-Hcal (KLM type) (10 layers) | Scint. Tile (individual tile) | 500 MeV | 0.1 MeV | 20 GeV | 10-200 pixels
p-EMCal | Tower (sum all fibers) | 100 MeV | 5 MeV | 100 GeV | 5-60k pixels
p-Hcal | Tower (sum 51 tiles) | 500 MeV | 300 MeV | 100 GeV | 50-20k pixels
b-Hcal (KLM Type) (5 layers) | Scint. Tile (individual tile) | 500 MeV | 0.1 MeV | 10 GeV | 10-200 pixels
b-Ecal (ScFI part) | Sub-Layer (one light guide) | 50 MeV | 2.5 MeV | 50 GeV | 90-40k pixels
b-Ecal (Si layers) | Pixel | 50 MeV | 2.5 MeV |  | 
Table 10.6 YR – requirements table. pEMcal – min. energy 100 MeV. EM cluster – side tower 5 MeV
For many reasons we want to keep SF in pECal (WScFi) at ~ 2.8% and not at 12%
Light Yield at 1000 p.e./GeV is possible with SiPMs (that will be close to previous example), BUT we need to move from 3x3 SiPMs to 6x6 SiPMs -> Noise may reach 2 x 10 MeV = 20 MeV Unless one start to cool SiPMs S/N what is listed in 10.6 not reachable.
And during discussions at ATHENA calor meetings it was not clear at all what is justification for 100 MeV minimal energy in pECal?
eRD106 is for pECal (tied with eRD107 pHCal).
Some requirements in YR looks tough,
eRD 105
eRD 106
Is it justified?

## Slide 6
Min Energy 50 MeV from -4 to +4,
Looks to me as made up….
For any sampling calorimeter at hadron endcap this is a tough requirements.
We need to clarify this:
What is justification?
What is requirement?
This goes beyond Calor group.
As an acation item from today’s meeting: put it on agenda for next calor meeting?
Need volunteer(s) to prepare it.

## Slide 7
SiPMs for calorimetry in eRD110 proposal.
Original plan was:
In FY22 plan was to develop needed FEEs for pECal for 6x6 SiPMs, and 16 ch board to match EMcal superblock (eRD106).
Production of these boards was assumed in FY23 (eRD106).
As part of eRD110 plan was to submit request in FY23 to buy needed SiPMs. Produce SiPM curry boards, get them exposed.
(possible to expose sensors only, then make boards, but as we learned with standard reflow soldering annealing is about 50%)
After that compare response of detector with fresh and exposed boards (same approach used for FCS).
All needed information (S/N) can be obtained with cosmics, no need to get to a test run. Although it was also planned a test Run late in FY23, where irradiated boards can be used as well.
We used RHIC/STAR to do SiPM/APD/calorimetry studies in 2016/17, which was very useful for both EIC and STAR FCS.
East side of STAR has plenty of space to do such studies until 2025.
STAR management was very supportive in the past and I expect if needed we can count on this in future.

## Slide 8: End of conveners update.