## Slide 1: EIC LAPPD Update Santa Fe 2015

## Slide 2: Reminder of Proposed Work
Continue performance characterization of base Argonne MCP-PMTS
  High B-field test at UVa (or possibly Argonne)
  Tests of QE, uniformity, radiation hardness, etc.
Work on UV sensitive photocathodes
  Swap in fused silica window and keep standard K2CsSb photocathode
  Try Na2KSb if that doesn’t improve N.P.E.
  Should result in factor of ~2 improvement in N.P.E.
Develop pixelated readout (2017)
  Two options: resistive anode or sealing PCB

## Slide 3: Incom SBIR
Builds on Gen-I LAPPD SBIR Phase-2 proposal
  All glass construction, strip-line readout, 20x20 cm2 tiles
  First pieces by end of year (possibly), and routine production after Q1 2016
  Should be able to receive some initial ones for testing
Gen-II versions are largely based on our EIC R&D proposal
  Pin free Pixelated readout (using capacitive coupling)
    Easier to maintain vacuum
  Fused silica window (better UV detection)
  More UV sensitive photocathode
    Default is K2CsSb
    Next to try is Na2KSb (w or w/o Cs)
  Ceramic package
    Cheaper and easier to seal than glass
  Expected cost will be an order of magnitude cheaper than existing MCP-PMT (in volume)

## Slide 4: UV Improved MCP-PMT Studies
Argonne has been steadily improving the production at their small tile facility
  Studying CsI as a UV only, solar blind, photocathode from 120-300 nm
Will start making tiles with fused silica window starting in November
Since their request for a UV spectrometer ($40K) wasn’t funded, it will be much harder and slower to pursue this research
  In the meantime, will send produced tiles to BNL for evaluation to evaluate QE from 170-1000 nm.
  Also possible, with more effort, down to 112 nm limit of MgF2.
  High priority to fund UV spectrometer at ANL
BNL (Triveni Rao, Thomas Tsang, John Smedley) will help with photocathode studies
  2 cm photocathodes will be studied (in reflective mode), November
  Start with QE down to 170 nm for K2CsSb, then Na2KSb
Pixelated Readout?

## Slide 5: B-field Testing of Large Tiles?
UVA MRI facility for small tiles
  Already Carl’s studies were extremely useful to improve design of LAPPD tiles
  Will optimize spacing of elements in , particularly reducing gap in between two MCPs.
For Large tiles, perhaps use Peter Winter’s Large Bore g-2 Magnet Test Facility (ANL)
  Up to 4 Tesla
  Set up as a test facility for devices (thus might be easier to incorporate MCP-PMTs, including rotations)
ANL