## Slide 1
1. The dedicated clock distribution tree can easily distribute a high precision clock. Minimum effort is required for R&D.
2. If the high radiation area requires lpGBT (no FPGA is allowed), a mixed clock distribution scheme can be adopted. We can derive a clock from that EIC clock frequency, which works with lpGBT (not necessarily 40.08 MHz).
Clock_lpGBT_freq = Clock_EIC_freq * N / M
where N and M are two integers, and as small as possible.
The streaming data time slice can be chosen to include an integer number of Clock_lpGBT_periods and an integer number of Clock_lpGBT_periods
EIC clock distribution idea

## Slide 2
Gigabit Ethernet for CCD/CCN (slow control)
Clock
Sync FiberMeas (fast control)
FiberMeas / FrontEnd Status (fast control)
Up stream
Computer / CCM / CCD_output
Down stream
Detector / CCN / CCD_input
QSFP signal assignment:
It is not expensive (Commercial !) and relatively compact:
  QSFP multimode optic transceiver $40 (~100 meters),
  Single-mode optic transceiver: $200 (~km),
  short Copper cables <$50 (~meters)
QSFP signal assignment
Gigabit Ethernet for CCD/CCN (slow control)
Tx1
Tx4
Tx3
Tx2
Rx1
Rx4
Rx3
Rx2
Tx1
Tx4
Tx3
Tx2
Rx4
Rx1
Rx2
Rx3
DataLink (streaming data)
DataLink
DataLink (streaming data)
Gigabit Ethernet (Slow control)
Sync etc. (Fast control)
DataLink
Clock/Status etc.
QSFP, 4 Rx 4 Tx