## Slide 1
IRT Reconstruction algorithm and performance studies in ATHENA
Alexander Kiselev and Chandradoy Chatterjee

## Slide 2: IRT library

## Slide 3
Inverse Ray Tracing: concept
Originally implemented by HERMES Collaboration
Recent re-implementations by Alessio del Dotto (2D), Roberto (2D), Marco (3D), …
radiator
sensor plane
mirror
emission point
detection point
?
charged particle trajectory
q
we want to know this angle (and nothing else!)
Cherenkov photon trajectory
reflection point

## Slide 4
Inverse Ray Tracing: machinery
In case of a single (unknown!) reflection point the task is reduced to a 2D case, a quartic equation follows, can be solved iteratively (e.g. using the Newton method)
The math can be extended to a case with a second (flat!) mirror
For dRICH the refraction on aerogel boundary can be accounted in a more or less consistent way a posteriori
More complicated cases (tilted aerogel tiles, acrylic layer, 2-d spherical mirror) require generalization into 3D space
Some sort of bookkeeping is required when
a single charged particle produces Cherenkov photons detected in different sectors
a pair of [emission, detection] 3D points allows for more than one optical path (like in a dual mirror configuration)
Very important: GEANT geometry should be consistent with the optical setup!

## Slide 5
Inverse Ray Tracing: implementation
A compact C++ library
Can be used in a standalone GEANT code as well as in the ATHENA environment
Optical geometry ROOT class instance is created in the same code, which creates RICH detector (therefore simulation-vs-reconstruction consistency is guaranteed)
Persistency model: optical setup dump in ROOT format
Newton-Gauss iterative solver for optical path defined by arbitrary sequence of refractive and reflective surfaces in 3D (presently flat and spherical boundaries only)
Absorbtion length accounting (azimuthally-asymmetric shift of emission point)
Emission angle uncertainly calculation (it does depend on the azimuthal angle!)
A wrapper for sampling along the charged particle trajectory (magnetic field case, etc.)
Repository (as of Dec 15, 2021) : https://eicweb.phy.anl.gov/EIC/irt/-/tree/irt-init-v02

## Slide 6
Inverse Ray Tracing: application (standalone GEANT4)
+190cm
sensor plane(s)
gap ~ 10cm
q = 250
q ~ 2-30
Barrel HCal
IP
Barrel EmCal
Cryostat
DIRC
+330cm
recess for the tracker
+350cm
gap ~ 10cm
+167cm
Endcap HCal
140cm
aerogel @ 192cm
140cm
Endcap EmCal
R ~ 230cm
20-25cm of the
upgrade space
spherical mirror#1 R = 2.8m
spherical mirror#2 R = 2.9m
Endcap HCal

## Slide 7
Inverse Ray Tracing: performance plots (C2F6, 50 GeV/c p+)
5s @ 50 GeV/c
1 mrad
120 cm
h = 4.0
h = 1.5
Stand Alone Geant4

## Slide 8: pfRICH

## Slide 9
<n> ~ 1.019
First Consistency Check  Validation of Rec. algorithm
N_theta /N_max = sin2(theta)/sin2(theta_max)
Refractive Index
Npe_sat ~ 10
0.7 safety factor included
Example pions at eta -1.7; open box exp. Open circle reconstructed

## Slide 10
Npe are as expected from estimations.
Acceptance is consistant with YR requirements

## Slide 11
N Sigma Separation
Yellow Report requirement: hadron
PID in the electron-going endcap: better than 3σ π/K separation either
(1) to 7 GeV/c (pp. 21)
(2) up to 10 GeV/c [table 3.1]
We consider the later as a reference!
YR requirement achieveable

## Slide 12: dRICH

## Slide 13
dRICH acceptance as a function of pseudorapidity
YR requirement:
acceptance for the dRICH is 1.0 ≤ η ≤ 3.5. These reference numbers were
taken as a guidance for the ATHENA implementation.

## Slide 14
Reconstructed Cherenkov Angle Vs momentum
@ pseudo rapidity = 2.4

## Slide 15
Dependence of ring resolution with pseudorapidity

## Slide 16: N Sigma Separation

## Slide 17
Performance plots
Left: reconstructed Cherenkov angle peaks for a 50:50 mix of 50 GeV/c kaon and pion tracks at η = 2.4 are ∼3σ apart (C2F6 radiator). Right: dependency of pion rejection factor on kaon detection efficiency with the selection cu varying between 37.6 mrad and 38.4 mrad applied to the left hand side plot.

## Slide 18
Reconstructed Kaon mass from Cherenkov angle.
~495 MeV/c2
Particle Mass as a function of momentum retrieved from reconstructed Cherenkov angle